## Slide 1: AHG7: RAP picture alignment and slice definition
JCT-3V 3rd Meeting: Geneva, CH, 17–23 Jan. 2013
Tomohiro Ikai
Yoshiya Yamamoto
Tadashi Uchiumi
SHARP Corporation
JCTVC-C0085:

## Slide 2: Motivation
It is asserted what distinguish 3DV from other HEVC extension (SHVC) is that multi layers are presented simultaneously in 3DV.
  In SHVC, either of base-layer or enhancement-layer is presented.
Random access in SHVC
  BL only access is ok because BL and EL has same content
Random access in 3DV
  Base view and dependent view should be decodable in random access
RAP picture alignment is needed to guranttee the above case

## Slide 3: Proposal #1
RAP picture alignment
      If base layer is RAP picture, the associated layer shall be RAP picture
nal_unit_type specifies the type of RBSP data structure contained in the NAL unit as specified in Table 7‑1.
All coded slice segment NAL units of all layers of an access unit shall have the same value of nal_unit_type.
or
All coded slice segment NAL units of each layer of an access unit shall have the same value of nal_unit_type.
If the nuh_layer_id of coded slice segment NAL units is equal to 0 and the nal_unit_type of the NAL units is the range of 16 to 23, the associated coded slice segment NAL units of which nuh_layer_id is not equal to 0 shall has the same nal_unit_type as the coded slice segment NAL units of which nuh_layer_id is 0.
Anticipated problem:
RAP picture alignment may degrade coding efficiency because RAP picture can only use I_SLICE (Proposal #2 fix the issue)
use the current specification as is

## Slide 4: Proposal #2
Slice definition
      Enabling inter-layer prediction in RAP picture by allowing the use of P_SLICE and B_SLICE in non-base layer RAP picture
G.7.4.5 Slice header semantics
When nal_unit_type has a value in the range of 16 to 23 inclusive (RAP picture) and nuh_layer_id is equal to 0, slice_type shall be equal to 2.

## Slide 5: Conclusion
Proposal
  RAP picture alignment [proposal #1]
    If base layer is RAP picture, the associated layer shall be RAP picture
  Slice definition [proposal #2]
    Enabling inter-layer prediction in RAP picture by allowing the use of P_SLICE and B_SLICE in non-base layer RAP picture
Recommendation
  Adopt this proposal in the next WD of MV-HEVC and 3D-HEVC.