## Slide 1: AHG7: On VPS extension
JCT-3V 3rd Meeting: Geneva, CH, 17–23 Jan. 2013
Tomohiro Ikai
Yoshiya Yamamoto
Tadashi Uchiumi
SHARP Corporation
JCTVC-C0086:

## Slide 2: Motivation
Motivation
  Approach 1 in JCTVC-J1007 was updated in K1007 and is considered helpful as common used syntax in All HEVC extension (incl. MV-HEVC and SHVC)
  Current 3DV spec uses Approach 2 in JCTVC-J1007, which might not appropriate align with other HEVC extension.
  Approach 1 is better for common syntax but Approach 2 is considered helpful because it provide a property that distinguish view_id or texture / depth without specifying the associate VPS and parse the syntax in decoder.
Approach 1 text (Proposal #1)
Approach 2 in Approach 1 syntax (Proposal #2)

## Slide 3: Current 3D test model text
vps_extension( ) { | Descriptor
while( !byte_aligned( ) ) | 
vps_extension_byte_alignment_reserved_one_bit | u(1)
num_additional_layer_operation_points | u(8)
num_additional_profile_level_sets_minus1 | u(8)
for( i = 0; i <= vps_max_layers_minus1; i++ ) { | 
// mapping of layer ID to scalability dimension IDs | 
reserved_zero_4bits_num_types[ i ] | u(4)
reserved_zero_4bits_type[ i ] | u(4)
view_id[ i ] | u(8)
if ( i>0 ) | 
num_direct_ref_layers[ i ] | u(6)
for( j = 0; j < num_direct_ref_layers[ i ] && i; j++ ) | 
ref_layer_id[ i ][ j ] | u(6)
} | 
... | 
for( i = 0; i <= vps_max_layers_minus1; i++ ) { | 
if ( (i ! = 0) && !( i % 2 ) ) { | 
multi_view_mv_pred_flag[ i ] | u(1)
multi_view_residual_pred_flag[ i ] | u(1)
} | 
if ( i % 2 ) { | 
enable_dmm_flag[ i ] | u(1)
use_mvi_flag[ i ] | u(1)
lim_qt_pred_flag[ i ] | u(1)
dlt_flag[ i ] | u(1)
... | 
} | 
} | 
} | 
ViewIdx = layer_id >> 1 (G‑14)
DepthFlag = layer_id%2 (G‑15)

## Slide 4: Proposal #1
Approach 1 text
vps_extension( ) { | Descriptor
.. | 
for( i = 0; i <= vps_max_layers_minus1; i++ ) { | 
if( !dimension_id[ i ][ depth_dimension_id ] ) { // (i ! = 0) && !( i % 2 ) | 
multi_view_mv_pred_flag[ i ] | u(1)
multi_view_residual_pred_flag[ i ] | u(1)
} | 
if( dimension_id[ i ][ depth_dimension_id ] ) { // i % 2 | 
enable_dmm_flag[ i ] | u(1)
use_mvi_flag[ i ] | u(1)
... | u(1)
} | 
} | 
ViewIdx = dimension_id[ nuh_layer_id ][ 1 ]
DepthFlag = dimension_id[ nuh_layer_id ][ 0 ]

## Slide 5: Proposal #2
Approach 2 capability in Approach 1 text
vps_extension( ) { | Descriptor
.. | 
for( i = 0; i <= vps_max_layers_minus1; i++ ) { | 
valid_layer_flag[i] | u(1)
if (valid_layer_flag[i]) { | 
if( !dimension_id[ i ][ depth_dimension_id ] ) { // (i ! = 0) && !( i % 2 ) | 
multi_view_mv_pred_flag[ i ] | u(1)
multi_view_residual_pred_flag[ i ] | u(1)
} | 
if( dimension_id[ i ][ depth_dimension_id ] ) { // i % 2 | 
enable_dmm_flag[ i ] | u(1)
use_mvi_flag[ i ] | u(1)
... | u(1)
} | 
} | 
} | 
ViewIdx = nuh_layer_id >> 1
DepthFlag = nuh_layer_id %2

## Slide 6: Proposal #2
dimension_id [add restrection]
valid_layer_flag [new flag]
valid_layer_flag[ i ] indicates whether the layer is valid. valid_layer_flag[ i ] equal to 1 specifies the layer may be used in in the coded video sequence. valid_layer_flag[ i ] equal to 0 specifies the layer shall not be used in the coded video sequence.
dimension_id[ i ][ j ] specifies the identifier of the j-th scalability dimension type of the i-th layer. When not present, the value of dimension_id[ i ][ j ] is inferred to be equal to 0.
When present dimension_id[ layer_id ][ 1 ] shall be equal to nuh_layer_id >>1 and dimension_id[ layer_id ][ 0 ] shall be equal to nuh_layer_id % 2

## Slide 7: Conclusion
Proposal
  Proposal #1
    provide approach 1 text
  Proposal #2
    use approach 1 syntax
    restrict dimension_id to enable approach 2 derivation property
    add valid_layer_flag
      explicit no existence of layers in coded video sequences
Recommendation
  Adopt this proposal#2 in the next WD in MV-HEVC and 3D-HEVC