## Slide 1: Improvement of the rate control for 3D multi-view video coding
W. Lim, I.V. Bajić and D. Sim
<number>
Notes: <number>

## Slide 2: Introduction
Rate control for 3D multi-view video coding
  Base view : the conventional rate control scheme of HEVC
  Extended view : additional tools
    Initial setting of QP for the first frame in a GOP of the extended view
    Depth map-based inter-view MAD prediction for the extended view
<number>

## Slide 3: Rate control for HEVC-based multi-view coding
To improve the rate control performance, we propose
  QP initialization in extended view
  Depth map-based inter-view MAD prediction
<number>
HEVC with
rate control
(extended view)
Initial QP
HEVC with
rate control
(Base view)
MAD
MAD
Amount of bits
Amount of bits
Initial QP
View layer QP offset

## Slide 4: QP initialization in extended view
In the existing HEVC rate control methods, at the beginning of encoding
  initial QP for the first frame in the base view is decided based on the target bitrate using an empirically obtained table of QP values
  However, unlike the base view, the first frame in each GOP in extended views is inter-coded relative to the reconstructed first frame in the base view
  So a different set of QP values would seem more appropriate
<number>

## Slide 5: Depth map-based inter-view MAD prediction
In order to select a QP value for the current CTU
  a rate control algorithm needs to predict the MAD value of the current CTU using previously encoded information
  In single-view rate control, this is done by using the MAD of a block in the reference frame (temporal MAD prediction)
  While this may work well in the case of low motion
  Temporal MAD prediction is less accurate as the motion level increases, and becomes completely unreliable in case of scene changes
<number>

## Slide 6: Depth map-based inter-view MAD prediction
<number>

## Slide 7: Depth map-based inter-view MAD prediction
MAD comparison
  Dancer (1920x1088)
  CTU-wise comparison
  Pearson correlation
    Slow motion
      t-MAD and a-MAD : 0.981
      iv-MAD and a-MAD : 0.990
    Fast motion
      t-MAD and a-MAD : 0.919
      iv-MAD and a-MAD : 0.975
<number>
Slow motion
Fast motion

## Slide 8: Experimental results
Percentage error in the actual bitrate (%)
<number>
Sequence | Proposed methods off |  | Proposed methods on | 
 | average view1 | average view2 | average view1 | average view2
Balloons | 0.35 | 0.49 | 0.48 | 0.71
Kendo | 0.68 | 0.86 | 0.98 | 0.69
Newspaper | 2.48 | 2.51 | 2.00 | 2.10
GTFly | 6.40 | 2.84 | 0.96 | 0.99
Poznanhall2 | 0.96 | 1.79 | 0.49 | 0.96
Poznanstreet | 4.04 | 1.25 | 0.27 | 0.46
Dancer | 1.03 | 0.67 | 0.66 | 0.69
Average | 2.28 | 1.49 | 0.83 | 0.94

## Slide 9: Experimental results
PSNR degradation in extended views (dB)
<number>
Sequence | Proposed methods off |  | Proposed methods on | 
 | average view1 | average view2 | average view1 | average view2
Balloons | 1.64 | 1.53 | 1.62 | 1.52
Kendo | 2.29 | 1.43 | 1.86 | 1.16
Newspaper | 1.51 | 1.40 | 1.65 | 1.64
GTFly | 0.94 | 0.98 | 0.84 | 0.86
Poznanhall2 | 0.56 | 0.48 | 0.53 | 0.49
Poznanstreet | 1.39 | 1.36 | 1.53 | 1.59
Dancer | 1.15 | 1.15 | 0.98 | 0.98
Average | 1.35 | 1.19 | 1.29 | 1.18

## Slide 10: Experimental results
Standard deviation of bits per second (bps)
<number>
Sequence | Proposed methods off |  | Proposed methods on |  | Avg. diff.
 | avg view1 | avg view2 | avg view1 | avg view2 | 
Balloons | 8303 | 9365 | 5843 | 6449 | 2688
Kendo | 5582 | 6478 | 4709 | 5416 | 967
Newspaper | 12001 | 11618 | 8900 | 8648 | 3036
GTFly | 16735 | 15604 | 13616 | 13372 | 2676
Poznanhall2 | 6722 | 7648 | 7548 | 8132 | 655
Poznanstreet | 24353 | 27542 | 16044 | 18906 | 8473
Dancer | 24116 | 21025 | 17025 | 15276 | 6420
Average | 13973 | 14183 | 10526 | 10886 | 3372

## Slide 11: Experimental results
Usage of virtual buffer occupancy vs. frame index
<number>

## Slide 12: Conclusion and future work
We proposed two methods to improve rate control of extended views in multi-view video coding based on HEVC
It was demonstrated that interview MAD prediction leads to more accurate MAD prediction compared to conventional methods, especially in the case of fast motion
The two proposed methods led to better rate control accuracy, reduced fluctuation of instantaneous bitrate, as well as a small reduction of PSNR degradation, compared to the benchmark method.
The proposed methods can be used with any rate control scheme that relies on the prediction of to-be-generated bits from MAD or other error metrics, including the newly adopted R-lambda model-based algorithm
We recommend the proposed methods to be adopted to the current rate control scheme for multi-view video coding
<number>