## Slide 1: 3D-HEVC: Alignment of inter-view vector scaling
JCT3V-C0115
Y. Takahashi, O. Nakagami, S. Hattori and T. Suzuki
Sony Corporation

## Slide 2: Summary
Background
  Inter-view vector scaling (IVS) can scale the predictive inter-view vector with the difference of view indices.
    Similar tool to motion vector scaling which scales the motion vector with POC
  IVS for TMVP is adopted in both HTM-5.1 and 3D-HEVC draft text.
Problem
  Not sufficient alignment between HTM-5.1 and 3D-HEVC draft text.
    In HTM-5.1, view_order_index is used as scaling factor.
      view_order_index is assumed to be assigned in spatial order of views.
    In 3D-HEVC draft text, view_id is used as scaling factor.
      view_id is no restrictions on values.
Proposal
  Scaling factor is unified to view_id .
    HTM-5.1 is modified to use view_id as scaling factor.
  iv_vector_scaling_flag is transmitted in SPS.
    In order to avoid incorrect inter-view vector scaling when view_id are not assigned in spatial order of views
  In comparison with unused IVS, IVS can achieve 4.6% BD-rate gain in video 2 and 0.7% BD-rate gain in all views in HTM-5.1.

## Slide 3: Example of IVS
P0
P1
P2
V0
V1
V2
Inter-view
reference picture
Inter-view
reference picture
CodingBlock
ColBlock
ColRefBlock
CodingRefBlock
Situation
  V1 refers to V0 and V2 as inter-view reference pictures.
  Coding inter-view vector
    Current block in V1 refers to reference block in V0.
  Co-located inter-view vector
    Co-located block in V1 refers to reference block in V2.
Scaling method
  Co-located inter-view vector is scaled with the difference of (V1-V0) and (V1-V2).

## Slide 4: Problem
Not sufficient alignment between HTM-5.1 and 3D-HEVC draft text.
  In HTM-5.1, view_order_index is used as scaling factor.
    view_order_index is assumed to be assigned in spatial order of views.
  In 3D-HEVC draft text, view_id is used as scaling factor.
    view_id is no restrictions on values.
0
spatial order
view_order_index
1
2
3
4
spatial order
view_id
4
3
2
1
0
0
1
2
3
4
3
1
0
2
4
or
or
…
Anything is OK.
Spatial order
view_order_index
view_id

## Slide 5: Proposal
  View index is unified to view_id in both software and text.
    HTM-5.1 is modified to use view_id instead of view_order_index
    3D-HEVC text is not changed.
  iv_vector_scaling_flag is transmitted in SPS.
    IVS is used when this flag is equal to 1, otherwise, IVS is not used.
    In order to avoid incorrect inter-view vector scaling
      This flag is assumed to be set to 1 when view_id is assigned in spatial order.
      This flag is assumed to be set to 0 when view_id is not assigned in spatial order.

## Slide 6: Experimental results
Coding Structure is changed.
  IVS runs in case of referring to two inter-view reference pictures at least.
  IVS runs in only video 2 which refers to video1 and video2 in this experiment.
Anchor
  Created with unused IVS.
IVS can achieve 4.6% BD-rate gain in video 2 and 0.7% BD-rate gain in all views in HTM-5.1.
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Balloons | 0.0% | 0.0% | -3.4% | -0.6% | -0.6% | -0.5%
Kendo | 0.0% | 0.0% | -4.8% | -0.9% | -0.8% | -0.7%
Newspaper_CC | 0.0% | 0.0% | -3.7% | -0.7% | -0.6% | -0.6%
GT_Fly | 0.0% | 0.0% | -6.4% | -0.7% | -0.7% | -0.6%
Poznan_Hall2 | 0.0% | 0.0% | -3.3% | -0.7% | -0.6% | -0.6%
Poznan_Street | 0.0% | 0.0% | -5.9% | -0.8% | -0.8% | -0.7%
Undo_Dancer | 0.0% | 0.0% | -4.5% | -0.6% | -0.6% | -1.1%
1024x768 | 0.0% | 0.0% | -3.9% | -0.7% | -0.7% | -0.6%
1920x1088 | 0.0% | 0.0% | -5.0% | -0.7% | -0.7% | -0.7%
average | 0.0% | 0.0% | -4.6% | -0.7% | -0.7% | -0.7%
0
1
I
B
P
2
coding order
spatial order
video0
video2
video1