## Slide 1: 3D-HEVC: Inter-view vector scaling for AMVP
JCT3V-C0116
Y. Takahashi, O. Nakagami, S. Hattori and T. Suzuki
Sony Corporation

## Slide 2: Summary
Background
  Inter-view vector scaling (IVS) can scale the predictive inter-view vector with the difference of view indices.
    Similar tool to motion vector scaling which scales the motion vector with POC
  IVS for TMVP has been already adopted in both HTM-5.1 and 3D-HEVC draft text.
Proposal
  IVS for AMVP is proposed.
    IVS can be also used in AMVP since the vector scaling process occurs in AMVP.
  In comparison with unused IVS, IVS for AMVP and TMVP can achieve 4.8% BD-rate gain in video 2 and 0.7% BD-rate gain in all views in HTM-5.1.
  In comparison with IVS for TMVP, IVS for AMVP and TMVP can achieve 0.2% BD-rate gain in video 2 and 0.0% BD-rate gain in all views in HTM-5.1.

## Slide 3: Example of IVS for TMVP (Current)
P0
P1
P2
V0
V1
V2
Inter-view
reference picture
Inter-view
reference picture
CodingBlock
ColBlock
ColRefBlock
CodingRefBlock
Situation
  V1 refers to V0 and V2 as inter-view reference pictures.
  Coding inter-view vector
    Current block in V1 refers to reference block in V0.
  Co-located inter-view vector
    Co-located block in V1 refers to reference block in V2.
Scaling method
  Co-located inter-view vector is scaled with the difference of (V1-V0) and (V1-V2).

## Slide 4: Example of IVS for AMVP (Proposal)
P0
P1
P2
V0
V1
V2
Inter-view
reference picture
Inter-view
reference picture
CodingBlock
CodingRefBlock
Situation
  V1 refers to V0 and V2 as inter-view reference pictures.
  Coding inter-view vector
    Current block in V1 refers to reference block in V0.
  Neighboring inter-view vector
    Co-located block in V1 refers to reference block in V2.
Scaling method
  Co-located inter-view vector is scaled with the difference of (V1-V0) and (V1-V2).
NeibRefBlock
NeibBlock

## Slide 5: Experimental results
Coding Structure is changed.
  IVS runs in case of referring to two inter-view reference pictures at least.
  IVS runs in only video 2 which refers to video0 and video1 in this experiment.
Test 1
  Anchor is created with unused IVS.
  Proposal is IVS for AMVP and TMVP.
Test 2
  Anchor is created with IVS for TMVP (JCT3V-C0115)
  Proposal is IVS for AMVP and TMVP.
0
1
I
B
P
2
coding order
spatial order
video0
video2
video1

## Slide 6: Experimental results
In comparison with unused IVS, IVS for AMVP and TMVP can achieve 4.8% BD-rate gain in video 2 and 0.7% BD-rate gain in all views in HTM-5.1.
In comparison with IVS for TMVP, IVS for AMVP and TMVP can achieve 0.2% BD-rate gain in video 2 and 0.0% BD-rate gain in all views in HTM-5.1.
Test1 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Balloons | 0.0% | 0.0% | -3.4% | -0.6% | -0.6% | -0.6%
Kendo | 0.0% | 0.0% | -4.9% | -0.9% | -0.8% | -0.7%
Newspaper_CC | 0.0% | 0.0% | -3.6% | -0.7% | -0.6% | -0.6%
GT_Fly | 0.0% | 0.0% | -6.7% | -0.8% | -0.7% | -0.6%
Poznan_Hall2 | 0.0% | 0.0% | -3.7% | -0.8% | -0.7% | -0.5%
Poznan_Street | 0.0% | 0.0% | -6.2% | -0.9% | -0.8% | -0.7%
Undo_Dancer | 0.0% | 0.0% | -4.8% | -0.7% | -0.6% | -0.7%
1024x768 | 0.0% | 0.0% | -4.0% | -0.7% | -0.7% | -0.7%
1920x1088 | 0.0% | 0.0% | -5.3% | -0.8% | -0.7% | -0.6%
average | 0.0% | 0.0% | -4.8% | -0.7% | -0.7% | -0.7%
Test2 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Kendo | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | 0.0%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1%
GT_Fly | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | 0.0%
Poznan_Hall2 | 0.0% | 0.0% | -0.4% | -0.1% | -0.1% | 0.0%
Poznan_Street | 0.0% | 0.0% | -0.3% | 0.0% | 0.0% | 0.0%
Undo_Dancer | 0.0% | 0.0% | -0.3% | 0.0% | 0.0% | -0.2%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
1920x1088 | 0.0% | 0.0% | -0.3% | 0.0% | 0.0% | -0.1%
average | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | 0.0%