## Slide 1: JCT3V-C0122 3D-CE2.a results on simplification on the disparity vector derivation
ETRI & KyungHee Univ.
Notes: <number>

## Slide 2: The Development of Simple Disparity Vector Derivation
2012, 1st JCT3V Meeting, Stockholm
  JCT3V-A0046 was adopted. (MediaTek)
    When MV predictor is not available, use the maximum depth sample among the samples at 4 corners to derivate the disparity for MVP process of inter-view and skip/direct mode.
    Total -0.02% (coded), -0.02% (synthetic). Complexity 98.83%(encoder), 97.66%(decoder)
2012, 2nd JCT3V Meeting, Shanghai
  JCT3V-B0073 (ETRI & KHU)
    It provides more reduction in memory access bandwidth for disparity vector derivation.
    For Inter-view MVP, use a bottom-right depth samples of current MB Instead of calculating maximum depth from 4 candidates when MV predictor is not available.
    Total 0.06% (coded), 0.02% (synthetic). Complexity 98%(encoder), 100%(decoder)
  JCT3V-B0153 was adopted. (Samsung)
    Use the identical process to the disparity derivation of JCT3V-A0046 for temporal MVP.
    Total -0.11% (coded), -0.08% (synthetic). Complexity 98.65%(encoder), 100.18%(decoder)
2013, 3rd JCT3V Meeting, Geneva
    JCT3V-C0122 (ETRI & KHU)
      The method of B0073 was implemented for temporal MVP due to the adoption of JCT3V-B0153.
      Total 0.05% (coded), 0.02% (synthetic). Complexity 99%(encoder), 99%(decoder)
      Simulation using full resolution depth was performed and the results are similar to the results using half depth resolution.
<number>

## Slide 3: Algorithm description
Weak Point of current method
  the number of the required depth sample will be increased by the increment of the number of sub-block.
  the number of the accessed depth samples in a 16x16 MB:
    1. 16x16 partition : 4
    2. 8x8 partitions : 16
    3. 4x4 partitions : 64 (Worst Case)
  In worst case (4x4 partitions), the number of the depth samples to be accessed is increased.
    It maybe should be solved for problem of the memory access bandwidth in worst case.
<number>
8x8 partitions
4x4 partitions (worst case)
16x16 partition
The number of the depth samples to be accessed in a 16x16 MB

## Slide 4: Algorithm description
Simplification on the disparity vector derivation
  In the last meeting, a simplified disparity vector derivation method was proposed by ETRI and KHU to reduce the memory access bandwidth using only one depth sample in a 16x16 MB.
  All the partitions inside a 16x16 MB take only one depth sample(bottom-right) for deriving the disparity vector. Thus, memory access bandwidth can be saved.
<number>
Derivation of the depth value in case a 16x16 MB is partitioned into 4x4 partitions

## Slide 5: Implementation for Temporal MVP(JCT3V-B0153 : Samsung)
  An additional modification is required because the proposal JCT3V-B0153 from Samsung Electronics Co. Ltd was adopted at the last meeting.
<number>
Temporal motion vector prediction
When the temporal motion vector is unavailable in the neighboring block A, B, or C, inter-view motion vector is employed for the unavailable blocks instead of the zero vector.
A max disparity which is associated with Current block(Cb) is used for the inter-view motion vector derivation.
The max disparity can be calculated from a max depth value among four corner depth samples.
Method of JCT3V-B0153

## Slide 6: Implementation for Temporal MVP
  The disparity vector derivation of both temporal and inter-view motion vector prediction is identical in processing. So, temporal motion vector prediction has also same problem associated with memory access bandwidth.
  Therefore, the proposed method was implemented for the disparity vector derivation of the inter-view motion vector prediction and the temporal motion vector prediction, respectively.
<number>
Temporal motion vector prediction
Disparity derived from bottom-right depth sample of current MB

## Slide 7: Reasonability of C0122
Memory access bandwidth reduction (in worst case, from 64 to 1)
  significantly reduce the number of the depth samples to be accessed
Remove the search operation of the depth samples according to the size of partition
Remove the comparison operation of the depth samples
Complexity reduction for encoding (avg. 99%)
<number>

## Slide 8: WD Text modification
  JCT3V-B1002, 3D-AVC Draft Text 4
  Anchor: cyan marked Proposed method: yellow marked
<number>

## Slide 9: WD Text modification
<number>

## Slide 10: Experimental Test Sets
There are 3 test set.
  Test 1.H : half depth, inter-view
  Test 1.F : full depth, inter-view
  Test 2.H : half depth, temporal
  Test 2.F : full depth, temporal
  Test 3.H : half depth, inter-view + temporal
  Test 3.F : full depth, inter-view + temporal
<number>

## Slide 11: Results Summary
Cross-check by Nokia (JCT3V-C0174), Samsung (JCT3V-C0213) and Qualcomm (JCT3V-C0226)
<number>
Test cases for bottom-right depth position
Average results for test cases

## Slide 12: Depth positions for each sets
  top-left
  top-right
  bottom-left
  bottom-right
  center
<number>
Case 1
Case 5
Case 4
Case 3
Case 2

## Slide 13: Results
Test 1.H : ATM 6.0 / ATM 6.0 + DMVP(inter-view)
Test 1.F : Full resolution depth, ATM 6.0 / ATM 6.0 + DMVP(inter-view)
<number>
 | Texture Coding |  | Depth Coding |  | Total (Coded PSNR) |  | Total (Synthesed PSNR) | 
sample position | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB
top-left | 0.25 | -0.01 | 0.00 | 0.00 | 0.23 | -0.01 | 0.16 | -0.01
top-right | 0.19 | -0.01 | 0.00 | 0.00 | 0.18 | -0.01 | 0.12 | 0.00
bot-left | 0.13 | -0.01 | 0.00 | 0.00 | 0.12 | 0.00 | 0.09 | 0.00
bot-right | 0.06 | 0.00 | 0.00 | 0.00 | 0.05 | 0.00 | 0.03 | 0.00
center | 0.15 | -0.01 | 0.00 | 0.00 | 0.14 | -0.01 | 0.11 | 0.00
Average results for Test 1.H
 | Texture Coding |  | Depth Coding |  | Total (Coded PSNR) |  | Total (Synthesed PSNR) | 
sample position | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB
top-left | 0.25 | -0.01 | 0.00 | 0.00 | 0.22 | -0.01 | 0.14 | 0.00
top-right | 0.18 | -0.01 | 0.00 | 0.00 | 0.15 | -0.01 | 0.09 | 0.00
bot-left | 0.18 | -0.01 | 0.00 | 0.00 | 0.16 | -0.01 | 0.09 | 0.00
bot-right | 0.08 | 0.00 | 0.00 | 0.00 | 0.07 | 0.00 | 0.03 | 0.00
center | 0.14 | -0.01 | 0.00 | 0.00 | 0.12 | 0.00 | 0.07 | 0.00
Average results for Test 1.F

## Slide 14: Results
Test 2.H : ATM 6.0 / ATM 6.0 + DMVP(temporal)
Test 2.F : Full resolution depth, ATM 6.0 / ATM 6.0 + DMVP(temporal)
<number>
 | Texture Coding |  | Depth Coding |  | Total (Coded PSNR) |  | Total (Synthesed PSNR) | 
sample position | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB
top-left | 0.02 | 0.00 | 0.00 | 0.00 | 0.02 | 0.00 | 0.01 | 0.00
top-right | 0.01 | 0.00 | 0.00 | 0.00 | 0.01 | 0.00 | 0.00 | 0.00
bot-left | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
bot-right | 0.01 | 0.00 | 0.00 | 0.00 | 0.01 | 0.00 | 0.01 | 0.00
center | 0.02 | 0.00 | 0.00 | 0.00 | 0.01 | 0.00 | 0.01 | 0.00
Average results for Test 2.H
Average results for Test 2.F
 | Texture Coding |  | Depth Coding |  | Total (Coded PSNR) |  | Total (Synthesed PSNR) | 
sample position | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB
top-left | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
top-right | 0.01 | 0.00 | 0.00 | 0.00 | 0.01 | 0.00 | 0.01 | 0.00
bot-left | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
bot-right | 0.01 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
center | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00

## Slide 15: Results
Test 3.H : ATM 6.0 / ATM 6.0 + DMVP(inter-view + temporal)
Test 3.F : Full resolution depth, ATM 6.0 / ATM 6.0 + DMVP(inter-view + temporal)
<number>
 | Texture Coding |  | Depth Coding |  | Total (Coded PSNR) |  | Total (Synthesed PSNR) | 
sample position | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB
top-left | 0.24 | -0.01 | 0.00 | 0.00 | 0.22 | -0.01 | 0.15 | -0.01
top-right | 0.19 | -0.01 | 0.00 | 0.00 | 0.18 | -0.01 | 0.12 | 0.00
bot-left | 0.15 | -0.01 | 0.00 | 0.00 | 0.13 | -0.01 | 0.11 | 0.00
bot-right | 0.05 | 0.00 | 0.00 | 0.00 | 0.05 | 0.00 | 0.02 | 0.00
center | 0.13 | 0.00 | 0.00 | 0.00 | 0.12 | 0.00 | 0.09 | 0.00
Average results for Test 3.H
Average results for Test 3.F
 | Texture Coding |  | Depth Coding |  | Total (Coded PSNR) |  | Total (Synthesed PSNR) | 
sample position | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB
top-left | 0.25 | -0.01 | 0.00 | 0.00 | 0.22 | -0.01 | 0.13 | 0.00
top-right | 0.19 | -0.01 | 0.00 | 0.00 | 0.16 | -0.01 | 0.10 | 0.00
bot-left | 0.18 | -0.01 | 0.00 | 0.00 | 0.16 | -0.01 | 0.09 | 0.00
bot-right | 0.08 | 0.00 | 0.00 | 0.00 | 0.07 | 0.00 | 0.04 | 0.00
center | 0.13 | 0.00 | 0.00 | 0.00 | 0.12 | 0.00 | 0.07 | 0.00

## Slide 16: Conclusions
The simplified derivation method of the disparity vector was proposed.
While the proposed method shows negligible BD rate loss and complexity, it reduces the memory access bandwidth and removes the searching and comparing operation of the depth samples depending on a partition size.
It is recommended to adopt the proposed method to the next 3DV-ATM and the 3D-AVC WD.
<number>

## Slide 17
<number>