## Slide 1: JCT3V-C0131 3D-CE1.h results on Depth-oriented Neighboring Block Disparity Vector (DoNBDV) with Virtual Depth
Yu-Lin Chang, Chi-Ling Wu, Yu-Pao Tsai, and Shawmin Lei (MediaTek)
Presented by Yu-Lin Chang
JCT on 3D Video Coding Extension Development
Jan., 2013

## Slide 2: Overall Summary of DoNBDV
Inter-view motion prediction provides more coding gain by using interview candidate with estimated disparity vector
  Coded depth map, predicted depth map (PDM), and neighboring block disparity vector (NBDV) were used for the estimated disparity vector
  Interview candidate using depth map provides more coding gains in 3D-AVC
  Problems
    PDM: need one more depth map buffer
    NBDV: accuracy can be improved but no real depth map for current view in current CTC of 3D-HTM
Proposed depth-oriented neighboring block disparity vector (DoNBDV)
  Provide more accurate estimated DV for inter-view motion prediction
  Use coded depth map in reference picture list, no need to change coding order
  Performance
    1.6% and 1.8% BD-rate reduction for video 1 and video 2, 0.6% BD-rate reduction for video over total bitrate over 3D-HTM 5.1 CTC
Notes:     Problem and proposeVSP off, finding inter-view reference without warping

## Slide 3: Inter-view Motion Prediction in 3DVC
In 3D-AVC, inter-view motion prediction is applied with the interview candidate obtained from real depth map (7% coding gain was observed in JCT3V-A0045)
In 3D-HEVC, inter-view motion prediction is applied in two modes: the AMVP mode and the merge mode
AMVP mode
  Use the NBDV to derive the MCP motion hypothesis or DCP motion hypothesis as the interview motion vector predictor
  An inter-view motion vector predictor is added and inserted at the first position of the candidate list
Merge mode
  Use the NBDV to derive the MCP motion hypothesis or DCP motion hypothesis as a inter-view motion vector candidate
With more accurate disparity vector, comes more accurate inter-view motion vector predictor

## Slide 4: Proposed Method – Virtual Depth
Use an estimated disparity vector (NBDV) to locate the corresponding block in the coded texture view
Use the collocated depth in the coded view as the virtual depth for the current block (coding unit)
CB
T1
Coded D0
Collocated depth
NBDV
Virtual depth
NBDV

## Slide 5: Proposed Method – Obtain DoNBDV for Inter-view Motion Prediction
Use the maximum value within the virtual depth block to convert it to a new estimated disparity vector “DoNBDV”
NBDV output is overridden by DoNBDV in the AMVP mode and the merge mode
CB
T1
Coded D0
Collocated depth
NBDV
Virtual depth
New estimated disparity vector DoNBDV

## Slide 6: Test Results
Anchor: 3D-HTM v5.1 CTC
Test: Override NBDV with DoNBDV in the AMVP mode and the Merge mode
Cross-checked by JCT3V-C0181(NTT)
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time | ren time
Balloons | 0.0% | -1.2% | -0.9% | -0.4% | -0.4% | -0.4% | 100.1% | 98.2% | 100.5%
Kendo | 0.0% | -1.6% | -1.9% | -0.7% | -0.6% | -0.6% | 100.3% | 95.8% | 103.2%
Newspapercc | 0.0% | -0.5% | -0.7% | -0.2% | -0.3% | -0.3% | 101.7% | 101.1% | 101.2%
GhostTownFly | 0.0% | -3.9% | -3.4% | -1.1% | -0.8% | -0.9% | 97.9% | 105.6% | 101.2%
PoznanHall2 | 0.0% | -0.1% | -2.4% | -0.6% | -0.4% | -0.4% | 95.1% | 101.5% | 101.2%
PoznanStreet | 0.0% | -1.3% | -1.5% | -0.5% | -0.4% | -0.4% | 99.5% | 115.6% | 101.6%
UndoDancer | 0.0% | -2.4% | -1.4% | -0.7% | -0.4% | -0.5% | 99.5% | 97.4% | 102.6%
1024x768 | 0.0% | -1.1% | -1.2% | -0.4% | -0.4% | -0.4% | 100.7% | 98.3% | 101.7%
1920x1088 | 0.0% | -1.9% | -2.2% | -0.7% | -0.5% | -0.5% | 98.0% | 104.8% | 101.7%
average | 0.0% | -1.6% | -1.8% | -0.6% | -0.5% | -0.5% | 99.2% | 102.0% | 101.7%

## Slide 7: Conclusions of DoNBDV
A depth oriented neighboring block disparity vector with virtual depth is proposed
  The inter-view information can be predicted more accurately by coded depth map from other views
  No additional depth map buffer is required
Performance
  Almost no encoding/decoding time difference
  1.6% and 1.8% BD-rate gain for video1 and video2, 0.6% BD-rate gain for video over the total bit-rate

## Slide 8: Thanks for your attention!
www.mediatek.com

## Slide 9: Inter Component Dependency
Coded depth map is required in this scheme
  VSP also requires the same inter component dependency
Solution
  NBDV will be used if there’s no depth reference picture in the reference picture list
  A virtual_depth_flag is proposed in slice header for indicating if the virtual depth can be used in a slice

## Slide 10: Complexity
Maximum depth is used here, but can be simplified by many other related methods
  Maximum of four corner (JCTVC-B0081)