## Slide 1: 3D-CE3.h results on removal of parsing dependency and picture buffers for motion parameter inheritance
Yi-Wen Chen, Jian-Liang Lin, Yu-Wen Huang, and Shawmin Lei.
Presented by Jian-Liang Lin
3rd JCT3V Meeting in Geneva
17 Jan. – 23 Jan., 2013

## Slide 2: Overall Summary
MPI allows depth inherit MV, ref. index and CU structures from texture
  Cause parsing dependency between depth and texture
  Requires extra buffers to store CU structures of texture
As an alternative and simplification to MPI, texture merging candidate is proposed for depth coding
  Reuse only the MV and ref. index of the texture picture
  Remove parsing dependency and buffers for CU structures
  Reduce coding time
  Unify the merge operations between texture and depth
  0.2% BD-rate savings for overall coded and synthesized views

## Slide 3: Motion Parameter Inheritance in HTM-5.0
MPI allows depth to reuse the CU/PU structure and the corresponding motion parameters from the texture
Parsing dependency between depth coding and texture CU splitting information
Extra buffers are required to store CU/PU structure info.

## Slide 4: Proposed Texture Merging Candidate
Add texture merging candidate for depth coding
  Added into the first position in the merging candidate set
  Inherit only motion parameters from texture
  Analogous to inter-view candidate
The MV and reference index of the corresponding texture block is derived as texture merging candidate

## Slide 5: Unification of Merge Operations
The derivation of texture merging candidate is analogous to inter-view candidate
Removal of the special case of MPI from candidate set unifies merge operations between texture and depth
Merge candidate set in HTM-5.0 |  | The proposed scheme | 
Texture | Depth | Texture | Depth
1.Inter-view candidate | 1.MPI | 1.Inter-view candidate | 1.Texture candidate
2. Spatial/DV candidate | 2. Spatial Candidate | 2. Spatial/DV candidate | 2. Spatial candidate
3. Temporal Candidate | 3. Temporal Candidate | 3. Temporal Candidate | 3. Temporal Candidate
4. Additional Candidate | 4. Additional | 4. Additional Candidate | 4. Additional Candidate

## Slide 6: Simulation Results
Anchor : HTM-5.0.1 (MPI enabled)
Test : HTM-5.0.1 with the following modifications
  MPI disabled
  Enable the proposed texture merging candidate
  Results crosschecked and confirmed in JCT3V-B0139
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | -0.3% | -0.3% | 97.7% | 95.1% | 101.8%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | 95.2% | 97.6% | 101.4%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.1% | 96.7% | 100.8% | 94.7%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.3% | 98.6% | 99.4% | 102.1%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | -0.6% | -0.5% | 97.1% | 99.2% | 99.8%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.2% | 98.3% | 97.0% | 97.4%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 98.5% | 97.7% | 98.2%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | -0.1% | 96.5% | 97.8% | 99.3%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | -0.2% | 98.1% | 98.3% | 99.3%
average | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | -0.2% | 97.4% | 98.1% | 99.3%

## Slide 7: Conclusion
Texture merging candidate is added to the merge candidate set for depth coding
  Follow essence of MPI but only reuse motion data from texture
  Remove the parsing dependency
  Remove the buffers for the CU/PU partition information
  Reduced encoding/decoding run time
  0.2% BD-rate savings for coded and synthesized views
Recommend to adopt the proposed method into HTM for its coding efficiency and simplicity

## Slide 8: Thank you for your attention!