## Slide 1: JCT3V-C0142 3D-CE6.h related: An efficient coding method for DLT in 3DVC
Kai Zhang, Jicheng An, Shawmin Lei (MediaTek)
Presented by Yu-Lin Chang
JCT on 3D Video Coding Extension Development
Jan., 2013

## Slide 2: Overview
Background
Proposed Method
Experimental results

## Slide 3: Background(1)
In the current HTM, a depth lookup table (DLT) is adopted to improve the intra coding efficiency for the depth map
All values in the DLT are coded with exp-Golomb codes
dlt_flag[ i ] | u(1)
if( dlt_flag[ i ] ) { | 
num_depth_values_in_dlt[ i ] | ue(v)
for ( j = 0; j < num_depth_values_in_dlt ; j++) { | 
dlt_depth_value[ i ][ j ] | ue(v)
} | 
} | 
Notes: In the current HTM, the encoder will not use DLT if more than half the values from 0 to MAX_DEPTH_VALUE (e.g., 255 for 8-bit depth samples) appear in the original depth map at the analysis step. Otherwise, DLT will be coded in SPS. In order to code DLT, the number of valid depth values is coded with Exp-Golomb code first. Then each valid depth value is also coded with an exp-Golomb code.

## Slide 4: Background(2)
Exp-Golomb codes are efficient when shorter codes possess higher probabilities of occurrence
  Not exactly for valid depth values and the number of valid depth values
Value | Code | Length
0 | 1 | 1
1 | 010 | 3
2 | 011 | 3
… | … | …
127 | 000000010000000 | 15
128 | 000000010000001 | 15
… | … | …
254 | 000000011111111 | 15
255 | 00000000100000000 | 16

## Slide 5: Background(3)
DLT generates lots of bits, thus makes SPS much larger
 |  | DLT Size (bits) | SPS Size (bits) | D/S (%)
Balloons | V0_depth | 555 | 845 | 65.68%
 | V1_depth | 641 | 937 | 68.41%
 | V2_depth | 617 | 915 | 67.43%
Kendo | V0_depth | 485 | 775 | 62.58%
 | V1_depth | 637 | 933 | 68.27%
 | V2_depth | 649 | 947 | 68.53%
Newspapercc | V0_depth | 606 | 896 | 67.63%
 | V1_depth | 621 | 917 | 67.72%
 | V2_depth | 696 | 994 | 70.02%
PoznanHall2 | V0_depth | 420 | 712 | 58.99%
 | V1_depth | 380 | 678 | 56.05%
 | V2_depth | 381 | 681 | 55.95%
Average |  | 557.33 | 852.50 | 65.38%
Notes: Statistics are done on the four sequences.

## Slide 6: Proposed
To code the DLT more efficiently, a range constrained bit map (RCBM) coding method is proposed
  min_dlt_value and diff_max_dlt_value are coded as unsigned integer to constrain the value range [min_dlt_value, MaxDltValue] of DLT.
  bit_map_flag[i] for i = 0 .. (MaxDltValue - min_dlt_value – 2), is coded
    bit_map_flag[i] = 1 value (i + min_dlt_value + 1) in DLT.
    bit_map_flag[i] = 0 value (i + min_dlt_value + 1) not in DLT.
  A flag is used to signal whether to code the range or not
code_full_bit_map_flag[i] | u(1)
if(!code_full_bit_map_flag[i]){ | 
min_dlt_value[i] | u(v)
diff_max_dlt_value[i] | u(v)
} | 
for(j=0;j< MaxDltValue[i] - min_dlt_value[i] – 1;j++) | 
bit_map_flag[i][j] | u(1)
Notes:     The smallest value in DLT is min_dlt_value, and the largest is MaxDltValue, which equals to min_dlt_value + diff_max_dlt_value
    When the range is not coded, a full bit map is coded
    The encoder can decide whether to code the range or not depending on which operation generates fewer bits.
    u(v) is used for v-bit sample. It’s u(8) if 8-bit sample is used.

## Slide 7: Experimental results(1)
DLT sizes and SPS sizes are compared using the four sequences that enable DLT
 |  | DLT Size (bits) |  |  | SPS Size (bits) |  | 
 |  | Anchor | Proposed | P/A (%) | Anchor | Proposed | P/A (%)
Balloons | V0_depth | 555 | 213 | 38.38% | 845 | 503 | 59.53%
 | V1_depth | 641 | 257 | 40.09% | 937 | 553 | 59.02%
 | V2_depth | 617 | 255 | 41.33% | 915 | 553 | 60.44%
Kendo | V0_depth | 485 | 191 | 39.38% | 775 | 481 | 62.06%
 | V1_depth | 637 | 255 | 40.03% | 933 | 551 | 59.06%
 | V2_depth | 649 | 257 | 39.60% | 947 | 555 | 58.61%
Newspapercc | V0_depth | 606 | 191 | 31.52% | 896 | 481 | 53.68%
 | V1_depth | 621 | 195 | 31.40% | 917 | 491 | 53.54%
 | V2_depth | 696 | 213 | 30.60% | 994 | 511 | 51.41%
PoznanHall2 | V0_depth | 420 | 111 | 26.43% | 712 | 403 | 56.60%
 | V1_depth | 380 | 101 | 26.58% | 678 | 399 | 58.85%
 | V2_depth | 381 | 104 | 27.30% | 681 | 404 | 59.32%
Average |  | 557.33 | 195.25 | 34.39% | 852.50 | 490.42 | 57.68%
Notes: The proposed method can reduce 2/3 of the original DLT size, and the size of SPS in a depth component is also reduced significantly.

## Slide 8: Experimental results(2)
Worst case compared
Anchor
  With the encoder in HTM5, if there are 128 values in DLT, which are 128, 129…., 254, 255, DLT generates 1937 bits
  With an encoder always encoding DLT, if all 256 values are in DLT, DLT generates 3365 bits.
Proposed
  With the proposed encoder, DLT generates 257 bits at most, since the full bit map always holds 256 bits.
  With an encoder always encoding the range, if all 256 values are in DLT, DLT generates 271 bits (1+8+8+254).

## Slide 9: Experimental results(3)
Common test condition
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time | ren time
Balloons | 0.00% | 0.00% | 0.00% | 0.00% | -0.02% | -0.02% | 87.3% | 94.1% | 92.0%
Kendo | 0.00% | 0.00% | 0.00% | 0.00% | -0.02% | -0.02% | 90.2% | 93.0% | 91.2%
Newspapercc | 0.00% | 0.00% | 0.00% | 0.00% | -0.02% | -0.02% | 88.8% | 98.7% | 93.2%
GhostTownFly | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 77.1% | 72.2% | 81.7%
PoznanHall2 | 0.00% | 0.00% | 0.00% | 0.00% | -0.03% | -0.03% | 94.7% | 94.6% | 94.2%
PoznanStreet | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 63.2% | 72.5% | 71.6%
UndoDancer | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 74.9% | 70.1% | 82.4%
1024x768 | 0.00% | 0.00% | 0.00% | 0.00% | -0.02% | -0.02% | 88.8% | 95.2% | 92.2%
1920x1088 | 0.00% | 0.00% | 0.00% | 0.00% | -0.01% | -0.01% | 76.7% | 76.7% | 82.1%
average | 0.00% | 0.00% | 0.00% | 0.00% | -0.01% | -0.01% | 81.7% | 84.2% | 86.3%
Notes: the coding performance is similar because SPS only takes a small percentage in the whole bit-stream.

## Slide 10
Thank you