## Slide 1: Fast DMM Selection for Depth Intra Coding
Zhouye Gu (Santa Clara University)
Jianhua Zheng (HiSilicon)
Nam Ling (Santa Clara University)
JCT3V-C0190

## Slide 2: Introduction
Intra depth frame compression usually takes much more time compared to intra texture frame compression.
Design additional condition for adding DMMs to full-RD cost calculation list to reduce unnecessary cost calculation .
Propose two methods, implemented on HTM5.1:
Method 1: 27.8% time saving, 0.31% BD-rate lost
Method 2: 14.7% time saving, 0.16% BD-rate lost
Thanks Qualcomm for cross-checking (JCT3V-C0209)

## Slide 3: Introduction
In 3D-HEVC intra depth coding, Depth Modeling Modes(DMMs) are added to the Full-RD cost calculation list after selection of several Most Probable Modes (MPMs)
uiRdModeList[0]
uiRdModeList[1]
…
uiRdModeList[m]
uiRdModeList[m+1]
uiRdModeList[m+2]
…
uiRdModeList[m+n]
MPMs
DMMs
Full RD cost Calculation

## Slide 4: Introduction
However, most of the CUs in depth frame are flat or smooth and DMMs are designed for CU with edge or sharp transition => less efficient for smooth CU compression.
For example, Newspaper sequence, after full RD-cost calculation, only 4.2% of best modes are DMMs. (QP = 25)
(a) Kendo (b) PoznanHall2
Example of Depth frames

## Slide 5: Our Proposal
Method 1: skip DMM full-RD cost calculation when the first mode in the full-RD calculation list is planar (uiRdModeList[0] == 0)
This is because when the first MPM is planar, the CU is very likely to be smooth and rarely select DMMs as best mode.
uiRdModeList[0]
uiRdModeList[1]
…
uiRdModeList[m]
uiRdModeList[m+1]
uiRdModeList[m+2]
…
uiRdModeList[m+n]
MPMs
DMMs
Full RD cost Calculation
==0

## Slide 6: Our Proposal
Method 2: Refinement for DMM mode1 and mode3 based on Method 1
Under the Pre-selection condition in Method 1, most unnecessary DMM full-RD cost calculation is skipped. However, it still misses some cases when DMM is selected as the best mode under that condition. For those missed DMMs, DMM mode1 without delta CPV(Constant Partition Value)s and DMM mode3 with delta CPVs are the two most probable missed DMMs.
Moreover, under the cases they are missed, we observe that the second mode in full-RD cost calculation list is very like to be DC (uiRdModeList[1] == 1).
DMMs | Additional Conditions required to add DMMs to Full-RD Search List
DMM mode1 with delta CPVs | First mode in full-RD cost calculation list is not planar (uiRdModeList[0] != 0)
DMM mode2 without delta CPVs | 
DMM mode2 with delta CPVs | 
DMM mode3 without delta CPVs | 
DMM mode4 without delta CPVs | 
DMM mode4 with delta CPVs | 
DMM mode1 without delta CPVs | First mode in full-RD cost calculation list is not planar (uiRdModeList[0] != 0) ¦¦ Second mode in full-RD cost calculation list is DC (uiRdModeList[1] == 1)
DMM mode3 with delta CPVs | 

## Slide 7: Test result of Method 1
Method 1:All Intra 3 view test result
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time | ren time
Balloons | 0.00% | 0.00% | 0.00% | 0.00% | 0.49% | 0.31% | 70.02% | 100.91% | 96.68%
Kendo | 0.00% | 0.00% | 0.00% | 0.00% | 0.52% | 0.32% | 70.82% | 102.20% | 101.54%
Newspapercc | 0.00% | 0.00% | 0.00% | 0.00% | 0.79% | 0.48% | 77.18% | 98.53% | 102.95%
GhostTownFly | 0.00% | 0.00% | 0.00% | 0.00% | 0.38% | 0.25% | 76.02% | 99.04% | 97.79%
PoznanHall2 | 0.00% | 0.00% | 0.00% | 0.00% | 0.64% | 0.43% | 65.64% | 98.03% | 97.90%
PoznanStreet | 0.00% | 0.00% | 0.00% | 0.00% | 0.27% | 0.15% | 70.52% | 102.41% | 95.58%
UndoDancer | 0.00% | 0.00% | 0.00% | 0.00% | 0.37% | 0.26% | 75.90% | 99.17% | 97.66%
1024x768 | 0.00% | 0.00% | 0.00% | 0.00% | 0.60% | 0.37% | 72.61% | 100.54% | 100.35%
1920x1088 | 0.00% | 0.00% | 0.00% | 0.00% | 0.41% | 0.27% | 71.89% | 99.65% | 97.23%
average | 0.00% | 0.00% | 0.00% | 0.00% | 0.49% | 0.31% | 72.20% | 100.03% | 98.55%
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time | ren time
Balloons | 0.00% | 0.00% | 0.00% | 0.00% | 0.10% | 0.06% | 99.00% | 96.78% | 95.47%
Kendo | 0.00% | 0.00% | 0.00% | 0.00% | 0.01% | 0.01% | 98.94% | 99.38% | 97.07%
Newspapercc | 0.00% | 0.00% | 0.00% | 0.00% | 0.25% | 0.14% | 98.53% | 99.48% | 97.09%
GhostTownFly | 0.00% | 0.00% | 0.00% | 0.00% | 0.12% | 0.09% | 97.50% | 94.39% | 97.09%
PoznanHall2 | 0.00% | 0.00% | 0.00% | 0.00% | 0.15% | 0.09% | 98.87% | 98.43% | 94.60%
PoznanStreet | 0.00% | 0.00% | 0.00% | 0.00% | 0.09% | 0.04% | 98.77% | 92.81% | 95.64%
UndoDancer | 0.00% | 0.00% | 0.00% | 0.00% | 0.07% | 0.05% | 99.05% | 99.05% | 97.13%
1024x768 | 0.00% | 0.00% | 0.00% | 0.00% | 0.12% | 0.07% | 98.82% | 98.54% | 96.54%
1920x1088 | 0.00% | 0.00% | 0.00% | 0.00% | 0.11% | 0.07% | 98.54% | 96.13% | 96.11%
average | 0.00% | 0.00% | 0.00% | 0.00% | 0.11% | 0.07% | 98.66% | 97.16% | 96.29%
Method 1:Random Access 3 view test result

## Slide 8: Test result of Method 2
Method 2: All Intra 3 view test result
Method 2: Random Access 3 view test result
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time | ren time
Balloons | 0.00% | 0.00% | 0.00% | 0.00% | 0.07% | 0.05% | 99.41% | 100.50% | 97.30%
Kendo | 0.00% | 0.00% | 0.00% | 0.00% | -0.01% | -0.01% | 99.60% | 99.97% | 97.86%
Newspapercc | 0.00% | 0.00% | 0.00% | 0.00% | 0.10% | 0.06% | 98.88% | 97.81% | 97.04%
GhostTownFly | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.01% | 99.58% | 99.80% | 99.64%
PoznanHall2 | 0.00% | 0.00% | 0.00% | 0.00% | 0.15% | 0.09% | 99.72% | 98.83% | 98.50%
PoznanStreet | 0.00% | 0.00% | 0.00% | 0.00% | 0.01% | 0.00% | 99.89% | 99.33% | 99.18%
UndoDancer | 0.00% | 0.00% | 0.00% | 0.00% | 0.08% | 0.05% | 100.19% | 101.54% | 96.48%
1024x768 | 0.00% | 0.00% | 0.00% | 0.00% | 0.06% | 0.03% | 99.29% | 99.42% | 97.40%
1920x1088 | 0.00% | 0.00% | 0.00% | 0.00% | 0.06% | 0.04% | 99.85% | 99.87% | 98.44%
average | 0.00% | 0.00% | 0.00% | 0.00% | 0.06% | 0.04% | 99.61% | 99.68% | 97.99%
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time | ren time
Balloons | 0.00% | 0.00% | 0.00% | 0.00% | 0.21% | 0.14% | 84.13% | 101.17% | 98.06%
Kendo | 0.00% | 0.00% | 0.00% | 0.00% | 0.26% | 0.16% | 83.52% | 103.34% | 100.74%
Newspapercc | 0.00% | 0.00% | 0.00% | 0.00% | 0.37% | 0.23% | 88.43% | 101.27% | 100.25%
GhostTownFly | 0.00% | 0.00% | 0.00% | 0.00% | 0.25% | 0.17% | 86.00% | 100.40% | 99.18%
PoznanHall2 | 0.00% | 0.00% | 0.00% | 0.00% | 0.29% | 0.20% | 84.57% | 97.67% | 99.06%
PoznanStreet | 0.00% | 0.00% | 0.00% | 0.00% | 0.12% | 0.07% | 84.38% | 99.94% | 97.56%
UndoDancer | 0.00% | 0.00% | 0.00% | 0.00% | 0.17% | 0.12% | 86.65% | 97.95% | 97.35%
1024x768 | 0.00% | 0.00% | 0.00% | 0.00% | 0.28% | 0.18% | 85.33% | 101.92% | 99.68%
1920x1088 | 0.00% | 0.00% | 0.00% | 0.00% | 0.21% | 0.14% | 85.40% | 98.98% | 98.29%
average | 0.00% | 0.00% | 0.00% | 0.00% | 0.24% | 0.16% | 85.37% | 100.23% | 98.88%

## Slide 9: Conclusion
Fast mode selection algorithm of intra depth coding for 3D-HEVC is proposed. The proposed method avoids unnecessary DMM full-RD cost calculation based on the selection of MPMs.
Method 1: 27.8% encoding time saving with 0.31% bitrate lost for all intra
Method 2: 14.7% encoding time saving with 0.16% bitrate lost for all intra
It is compactable with other algorithms designed for specific DMM performance improvement.
It is suggested to include the fast DMM selection methods in HTM5.1.

## Slide 10: Thank you!