## Slide 1
Results on Weighted Prediction for 3D-HEVC (JCT3V-C0223)
Jan. 17, 2013
Jiwook Jung, Hongbin Liu, Sehoon Yea (LG)

## Slide 2
Weighted Prediction (WP)
  - useful for coding fading sequences (normative in HEVC)
HTM computes the WP parameters independently for each view
  - Currently non-CTC, the current implementation buggy
In principle, the fading in/out effect apply to all views simultaneously with the same magnitude
  - predominantly a temporal effect
Backdrop

## Slide 3
Provides a SW bug-fix that would make the WP in the HTM work
Propose to inherit WP parameters for a dependent view
  by inheriting from the base view when available
  by setting to default values (weight 1, offset 0) when unavailable
Results
- BD-gains on fading seq.: -7.4%, -7.5%, -2.6% for V1, V2, video only
- Anchor: HTM (with the proposed bug-fix) without inheritance
Contribution
WP Parameters
WP Parameters
Base view
Dependent view

## Slide 4
weighted_pred_flag = 1
Contribution
Y=W*X+O
Set by the encoder per slice
as per RD-consideration
W & O saved in a table for
each ref_pic candidate
Bug-fix for dependent view
yes
Copy, if available, from the base-view
Contribution 1
Contribution 2

## Slide 5
Bug Fix on Weighted Prediction in HTM5.0.1
TComRdCostWeightPrediction::xGetSADw( DistParam* pcDtParam) in TComRdCostWeightPrediction.cpp,
pcDtParam->pUsed represents whether the tool InterViewSkip is on or off.
(default setting : InterViewSkip is off in CTC)
Original code
Bug fixed code

## Slide 6
Inheritance of WP parameters for a dependent view
For each temporal reference picture of the dependent view, refPic with refIdx,
A reference picture of the base view picture, refPicBase, having the same POC with refPic is searched
If the refPicBase is found,
  WP_Param( refIdx ) = WP_Param_Base( RefIdx(refPicBase ) )
otherwise,
  WP_Param( refIdx ) = default values (weight 1, offset 0)
The WP parameters for inter-view reference pictures are set equal to default values: 1.0 for weight, 0.0 for offset.
Proposal
LumaWeightL0 parameters of
base view picture
refIdx | 0 | 1
POC | 2 | 0
LumaWeightL0[refIdx] | 1 | 0.5
LumaWeightL0 parameters of
dependent view picture
refIdx | 0 | 1 | 2
POC | 2 | 0 | V0
LumaWeightL0[refIdx] | 1 | 0.5 | 1

## Slide 7
Syntax change
slice_header( ) { | Descriptor
first_slice_in_pic_flag | u(1)
… | 
if( !entropy_slice_flag ) { | 
… | …
if( ( weighted_pred_flag && slice_type = = P) ¦ ¦ ( weighted_bipred_flag = = 1 && slice_type = = B ) ) { | 
if(ViewIdx>0 && !DepthFlag) { | 
base_pred_weight_table_flag | u(1)
if( base_pred_weight_table_flag== 0 ) | 
pred_weight_table() | 
} | 
… | 
} | 
base_pred_weight_table_flag equals to 1 specifies that the weighted prediction parameter
for the texture of dependent view are inherited from the texture picture of base view.
When the base_pred_weight_table_flag is not present, it is inferred to be 0.

## Slide 8
Test Sequences
Fading sequences
  The fading tool used in HEVC (JCTVC-E041) applied to 3DV Sequences
  A linear fade in/out on each of the Y, U, V components
  First 2-seconds of texture videos
  : linear fade-out for 0 ~ 1 sec interval
  : linear fade-in for 1~2 sec interval
  : fading in/out strength [0.25,1]

## Slide 9
Simulation result 1
Anchor : WP Off
Test : WP On w/o Parameter Inheritance
(weight and offset for inter-view ref. pic set to 1.0, 0.0)
 | video 0 | video 1 | video 2 | video only | enc time | dec time
Balloons | -36.0% | -19.5% | -18.3% | -29.7% | 147.0% | 102.6%
Kendo | -18.6% | -4.6% | -2.5% | -13.5% | 186.2% | 100.4%
Newspapercc | -33.0% | -21.9% | -23.5% | -29.2% | 127.7% | 97.8%
GhostTownFly | -29.6% | -2.0% | -2.8% | -24.6% | 159.6% | 106.2%
PoznanHall2 | -32.1% | -9.7% | -15.9% | -24.8% | 160.2% | 100.4%
PoznanStreet | -27.5% | -16.3% | -14.5% | -24.6% | 128.5% | 101.3%
UndoDancer | -37.2% | -19.0% | -23.7% | -33.3% | 150.7% | 98.6%
1024x768 | -29.2% | -15.3% | -14.8% | -24.1% | 151.8% | 100.3%
1920x1088 | -31.6% | -11.8% | -14.2% | -26.8% | 149.2% | 101.6%
average | -30.6% | -13.3% | -14.5% | -25.7% | 150.3% | 101.0%

## Slide 10
Simulation result 2
Anchor : WP On w/o WP Parameter Inheritance
(weight and offset for inter-view ref. pic set to 1.0, 0.0)
Test : WP On, WP Parameter Inheritance
 | video 0 | video 1 | video 2 | video only | enc time | dec time
Balloons | 0.0% | -8.7% | -8.8% | -3.4% | 103.1% | 101.0%
Kendo | 0.0% | -8.6% | -8.9% | -3.3% | 100.6% | 96.2%
Newspapercc | 0.0% | -7.5% | -7.3% | -2.8% | 104.0% | 94.3%
GhostTownFly | 0.0% | -9.7% | -8.2% | -1.9% | 101.2% | 100.6%
PoznanHall2 | 0.0% | -8.1% | -6.8% | -2.9% | 101.4% | 100.8%
PoznanStreet | 0.0% | -4.2% | -5.5% | -1.3% | 104.1% | 100.0%
UndoDancer | 0.0% | -4.6% | -3.2% | -0.8% | 101.5% | 100.9%
1024x768 | 0.0% | -8.3% | -8.4% | -3.2% | 102.6% | 97.1%
1920x1088 | 0.0% | -6.7% | -5.9% | -1.7% | 102.0% | 100.6%
average | 0.0% | -7.4% | -7.0% | -2.3% | 102.3% | 99.1%

## Slide 11
Simulation result 3
Anchor : WP Off
Test : WP On, WP parameter inheritance
 | video 0 | video 1 | video 2 | video only | enc time | dec time
Balloons | -36.0% | -26.6% | -25.5% | -32.1% | 151.6% | 103.7%
Kendo | -18.6% | -12.9% | -11.3% | -16.4% | 187.3% | 96.6%
Newspapercc | -33.0% | -27.9% | -29.2% | -31.3% | 132.8% | 92.2%
GhostTownFly | -29.6% | -11.7% | -10.9% | -26.1% | 161.5% | 106.8%
PoznanHall2 | -32.1% | -17.2% | -21.7% | -27.1% | 162.4% | 101.2%
PoznanStreet | -27.5% | -20.0% | -19.4% | -25.6% | 133.7% | 101.2%
UndoDancer | -37.2% | -23.0% | -26.4% | -33.9% | 153.0% | 99.5%
1024x768 | -29.2% | -22.5% | -22.0% | -26.6% | 155.6% | 97.4%
1920x1088 | -31.6% | -18.0% | -19.6% | -28.1% | 152.2% | 102.1%
average | -30.6% | -19.9% | -20.6% | -27.5% | 153.7% | 100.1%

## Slide 12
Conclusion
This contribution proposed the inheritance of WP parameters for dependent views from the base view.
BD-rate gains are -7.4%, -7.5%, -2.6% for V1, V2, video only
We recommend to adopt the proposal.