## Slide 1: Calculation Sample Reduction for Depth Modeling Mode 1 and 3
K. Kawamura, M. Sato, S. Naito
KDDI Corp. (KDDI R&D Labs. Inc.)

## Slide 2: Overview
Further simplification of DMM 1 and 3
  For reducing calculation sample of SAD etc,
  By skipping non-edge region of the pattern.
  Decoder/render runtime is reduced by 1.0%/4.4%.
Recommend to study the proposal in the core experiments.

## Slide 3: Introduction
Depth Modeling Modes are adapted to the depth map characteristics.
A Wedgelet search of DMM1 and 3 is a heavy burden in the decoder side
  Some simplification schemes have been adopted.
  Hardware acceleration is also considered.
    A very elaborated algorithm is not acceptable.

## Slide 4: DMM 1 and 3
Wedgelet patter lists are generated.
  4x4 pixels (half-pel)  8x8 samples
  8x8 pixels (half-pel)  16x16 samples
  16x16 pixels (full-pel)  16x16 samples
  32x32 pixels (double-pel) 16x16 samples
Calculation of average luma for two regions
Calculation of SAD for two regions

## Slide 5: Motivation & Solution
Concept
  Non-edge region may not affect the decision
  Chunk of pixels should be kept for SIMD
  Additive scheme for other complexity reduction
Proposed solution
  Skipping computation region based on the start/end position

## Slide 6: Proposed method (overview)
v
u
v
u
start/end position
coarse subset
Pattern left
Pattern all

## Slide 7: Experimental Result
Implemented on HTM5.0.1
Result for 3-view scenario

## Slide 8: Conclusion
Further simplification of DMM 1 and 3
  Calculation region is reduced roughly half.
  Decoder/render runtime is reduced by 1.0%/4.4%.
Recommend to study the proposal in the core experiments.