## Slide 1
AHG 13: Restriction of inter-layer prediction on tile boundaries JCT3V-D0051
Gerhard Tech Yago Sanchez Karsten Suehring Robert Skupin Thomas Schierl

## Slide 2: Outline
  Motivation
  Proposal
  Changes to MV-HEVC
  Changes to 3D-HEVC

## Slide 3: Motivation
  Any position in the reference view can be utilized for the prediction of the dependent view.
  A decoder is required to finalize decoding of all reference views in 3D- and MV-HEVC before decoding the current view.
   Without any restrictions: No parallel decoding of layers is possible.

## Slide 4: Proposal
  All predictions for a particular tile in the dependent view are constraint to use data from the same reference layer tile.
  The reference layer tile is the tile in the reference layer that includes the block that is collocated to the current block in the tile of the dependent layer.
   For low delay applications this approach enables the encoding and decoding of tiles in the dependent layer, before decoding or encoding of the reference layer is finished.

## Slide 5: Changes in MV-HEVC
  Whether the constraint applies is signalled by a flag in the SPS extension.
  When it is enabled following bitstream constraints shall apply for MV-HEVC:
    Motion vectors used for inter-layer prediction shall be constraint in a way that the reference samples are located in the same reference layer tile.
    When the collocated picture is in a layer different to the layer of the current picture syntax elements shall be constraint such that the collocated vector only needs to be derived when the position of the collocated block is in the (collocated) reference picture tile.
    Loop filtering over tile boundaries shall be disabled in the reference layer.

## Slide 6: MV-HEVC Syntax changes
sps_extension( ) { | Descriptor
... | u(1)
inter_layer_pred_tile_constraint_flag | u(1)
... | 
} | 

## Slide 7: MV-HEVC Semantics changes
inter_layer_pred_tile_constraint_flag specifies whether inter-layer prediction at tile boundaries is constrained in the CVS.
– If inter_layer_pred_tile_constraint_flag is equal to 1, the following applies:
– Motion vectors used for inter-layer prediction shall be constraint that in the fractional sample interpolation process all sample positions within the reference sample array that are used to derive prediction sample values are within the tile in the reference picture that includes the luma sample with a position relative to the top-left luma sample of the reference picture equal to the position of top-left sample of the current luma prediction block relative to the top-left sample of the current picture.
– When the collocated picture is a picture of a layer different to the current layer, syntax elements shall be constraint such that the collocated motion vector only needs to be derived when the position of the top-left sample of the collocated block relative to the top left-sample of the collocated picture is in the tile in the collocated picture that includes the luma sample with a position relative to the top-left sample of the collocated picture equal to the position of the top-left sample of the current luma prediction block relative to the top-left sample of the current picture.
Note – ­ The above constraint can be fulfilled by e.g. not using a collocated picture in a different layer, or by e.g. restricting merge_idx, mvp_lX_flag at tile boundaries.
– The syntax element loop_filter_across_tiles_enabled_flag of all reference layers used for inter-layer prediction of the current layer shall be equal to 0.
– Otherwise, ( inter_layer_pred_tile_constraint_flag is equal to 0 ), no constraints are signalled by this flag.
When not present the inter_layer_pred_tile_constraint_flag is inferred to be equal to 0.

## Slide 8: Changes in 3D-HEVC
  In 3D-HEVC the decoding process need to be restricted when the proposed flag is equal to 1.
  Only small modifications are required.
    Clipping of reference positions (e.g. inter-view residual prediction or motion prediction), such that they are within the reference layer tile.
    Marking of block as unavailable, when not within the reference layer tile (TMVP, NBDV)
  Tools that need to be modified are
    TMVP, NBDV, DoNBDV, Inter-view motion vector prediction, Inter-view residual prediction, Illumination compensation, Fractional sample interpolation process