## Slide 1: 3D-CE5.h related: Illumination compensation regression improvement and simplification (JCT3V-D0061)
JCT3V 4th Meeting: Incheon, KR, 20–26 Apr. 2013
Tomohiro Ikai
SHARP Corporation

## Slide 2: Overall summary
Motivation
  Improve regression
  Simplify ic prediction and ic parameter derivation
Proposal
  Regression improvement with parameter cost
  Constant shift
  2Nx2N only
  L0 only
Experimental results
  0.24 % gain in total video
  0.18 % gain in synthesis video

## Slide 3: Problem statement (1)
IC utilizes the linear regression model in which parameters are derived by least square error (LSE) algorithm. However these LSE model is known not robust in real world where a lot of outliner and noise exists.
add parmeter cost
(reguralization parameter)

## Slide 4: Problem statement (2)
IC has several complexity problems
  Adaptive shift operation
  Complex parameter derivation
  Small block size
    Smallest PU might use IC (4x8/8x4) which increases worst case computation
  Bi-prediction operation
    IC might be used in both L0 and L1
(predSamplesL0[ x ][ y ] * icWeightL0 ) >> icShift ) + ( icOffsetL0 << shift1 )

## Slide 5: Proposal (1)
Add parmeter cost
improve coding efficiency (0.2%)

## Slide 6: Proposal (2)
Constant shift
  range
  Remove adaptive shift part in IC parameter derivation
( clipPredVal * icWeightL0 ) >> 5 ) + icOffsetL0
The variable icWeight specifying a weight for illumination compensation with 7 bit precision is derived as specified in the following:
If invPsIcWeight is greater than or equal to −26 and less than 26, the following applies.
      icWeight = invPsIcWeight (H‑228)
Otherwise, ( invPsIcWeight is less than −26 or greater than or equal to 26 ), the following applies.
      decIcShift = Max( 0, Floor(Log2( Abs( icWeight ) ) − 5 ) ) (H‑229)
      [Ed (GT): In software a function counting leading zero ones is utilized to derive decIcShift. Does this match with draft text?]
      icWeight = invPsIcWeight >> decIcShift (H‑230)
      icShift −= decIcShift (H‑231)
clipPredVal and icWeightL0 is within 0..255
(can be processed with unsigned 8 bit)

## Slide 7: Proposal (3)
Easier parameter derivation
psDenomDiv | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
divCoeff | 0 | 32768 | 16384 | 10923 | 8192 | 6554 | 5461 | 4681 | 4096 | 3641 | 3277 | 2979 | 2731
psDenomDiv | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
divCoeff | 2521 | 2341 | 2185 | 2048 | 1928 | 1820 | 1725 | 1638 | 1560 | 1489 | 1425 | 1365 | 1311
psDenomDiv | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38
divCoeff | 1260 | 1214 | 1170 | 1130 | 1092 | 1057 | 1024 | 993 | 964 | 936 | 910 | 886 | 862
psDenomDiv | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51
divCoeff | 840 | 819 | 799 | 780 | 762 | 745 | 728 | 712 | 697 | 683 | 669 | 655 | 643
psDenomDiv | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64
divCoeff | 630 | 618 | 607 | 596 | 585 | 575 | 565 | 555 | 546 | 537 | 529 | 520 | 512
If psDenomDiv is greater than 0, the following applies,
The value of variable divCoeff is derived from Table H‑12 depending on psDenomDiv.
The value of psIcWeight is derived as
psIcWeight = psNumerDiv * divCoeff (H‑224)
Otherwise( psDenomDiv is less or equal to 0), psIcWeight is set equal to 0.
not used
(remove)
usually table starts from 0

## Slide 8: Proposal (4)
2Nx2N only
coding_unit( x0, y0, log2CbSize , ctDepth) { | Descriptor
… | 
if ( icEnableFlag && PartMode == 2Nx2N ) | 
ic_flag | ae(v)
Smallest size become larger
(8x4/4x8 to 8x8)
Plus, anyIvRefPicFlag only check one PU (up to 4PU to 1PU)

## Slide 9: Proposal (5)
L0 only
Avoid the case IC is used in both L0 and L1

## Slide 10: Results (Regression only)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -1.2% | -1.3% | -0.5% | -0.5% | -0.5% | 101.0% | 98.7% | 99.4%
Kendo | 0.0% | -0.9% | -1.3% | -0.5% | -0.4% | -0.3% | 100.0% | 100.6% | 100.0%
Newspaper_CC | 0.0% | -0.4% | -0.7% | -0.2% | -0.2% | -0.2% | 99.0% | 101.2% | 101.2%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.5% | 101.1% | 100.0%
Poznan_Hall2 | 0.0% | -0.8% | -1.6% | -0.6% | -0.5% | -0.2% | 99.5% | 100.3% | 99.9%
Poznan_Street | 0.0% | 0.1% | -0.6% | -0.1% | -0.1% | -0.1% | 100.0% | 98.7% | 100.0%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.1% | 100.1% | 100.0%
1024x768 | 0.0% | -0.8% | -1.1% | -0.4% | -0.4% | -0.3% | 100.0% | 100.2% | 100.2%
1920x1088 | 0.0% | -0.2% | -0.5% | -0.2% | -0.2% | -0.1% | 99.5% | 100.1% | 100.0%
average | 0.0% | -0.5% | -0.8% | -0.27% | -0.24% | -0.16% | 99.7% | 100.1% | 100.1%
cross-checked by LG (JCT3V-D0099)
Thank you very much

## Slide 11: Results (Simplification only)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 99.1% | 100.2% | 99.7%
Kendo | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 97.0% | 99.6% | 98.4%
Newspaper_CC | 0.0% | -0.2% | -0.1% | 0.0% | 0.0% | -0.1% | 98.1% | 102.5% | 101.2%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.4% | 100.8% | 99.6%
Poznan_Hall2 | 0.0% | -0.2% | -0.5% | -0.1% | -0.1% | 0.0% | 98.1% | 100.8% | 100.3%
Poznan_Street | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 99.5% | 99.4% | 100.0%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.1% | 98.8% | 99.4%
1024x768 | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 98.1% | 100.8% | 99.8%
1920x1088 | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 98.8% | 100.0% | 99.8%
average | 0.0% | 0.0% | -0.1% | -0.02% | -0.01% | -0.02% | 98.5% | 100.3% | 99.8%
cross-checked by LG (JCT3V-D0099)
Thank you very much

## Slide 12: Results (Regression + simplification)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -1.3% | -1.2% | -0.5% | -0.4% | -0.4% | 99.1% | 99.7% | 99.4%
Kendo | 0.0% | -1.0% | -1.4% | -0.5% | -0.4% | -0.3% | 97.5% | 100.0% | 100.7%
Newspaper_CC | 0.0% | -0.3% | -0.8% | -0.2% | -0.2% | -0.2% | 98.3% | 100.3% | 100.6%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.9% | 100.4% | 99.8%
Poznan_Hall2 | 0.0% | -1.2% | -2.0% | -0.7% | -0.6% | -0.4% | 99.1% | 98.6% | 99.9%
Poznan_Street | 0.0% | 0.2% | -0.7% | -0.1% | -0.1% | -0.1% | 100.1% | 98.8% | 100.1%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.0% | 100.5% | 100.2%
1024x768 | 0.0% | -0.9% | -1.1% | -0.4% | -0.3% | -0.3% | 98.3% | 100.0% | 100.2%
1920x1088 | 0.0% | -0.3% | -0.7% | -0.2% | -0.2% | -0.1% | 99.5% | 99.6% | 100.0%
average | 0.0% | -0.51% | -0.86% | -0.28% | -0.24% | -0.18% | 99.0% | 99.8% | 100.1%
cross-checked by LG (JCT3V-D0099)
Thank you very much

## Slide 13: Overall summary
Motivation
  Improve regression
  Simplify ic prediction and ic parameter derivation
Proposal
  Regression improvement with parameter cost
  Constant shift
  2Nx2N only
  L0 only
Experimental results
  0.24 % gain in total video
  0.18 % gain in synthesis video

## Slide 14
Comparison with related proposals

## Slide 15: Comparison Simplification
Sharp
(D0061)
Samsung
(D0114)
LG
(D0096)
a = (NΣxy – Σx*Σy - c) / (NΣxx – Σx*Σx -c)
b = (Σy – a*Σx) >> shift
y = (a*x + 16) >> 5 + b
a = (Σy / Σx)
b = (Σy – a*Σx) >> shift
y = (a*x + 8) >> 4 + b
a = ...
b = (Σy – Σx) >> shift
y = x + b

## Slide 16: Complexity comparison
 | Add | Mul | Shift | Div or LUT | Clip
Sharp (D0060) | 130 | 97 | 71 | 1 | 64
Samsung (D0114) | 96 | 65 | 65 | 1 | 64
LG (D0096) | 96 | 0 | 65 | 0 | 64
MCP | 1288 | 1472 | 128 | 0 | 64
Cost | 1 | 2 | 1 | 30 | 1
Chart: Operation cost (8x8 block)
| Sharp (D0060) | Samsung (D0114) | LG (D0096) | MCP
cost | 1 | 0.78732 | 0.32924 | 9.047
 | Sharp (D0061) | Samsung (D0114) | LG (D0096) | MCP
8x8 | 1.00 | 0.79 | 0.33 | 9.05
16x16 | 1.00 | 0.87 | 0.37 | 9.59
32x32 | 1.00 | 0.93 | 0.38 | 9.75

## Slide 17: Coding performance comparison
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Balloons | 0.0% | -1.3% | -1.2% | -0.5% | -0.4% | -0.4%
Kendo | 0.0% | -1.0% | -1.4% | -0.5% | -0.4% | -0.3%
Newspaper | 0.0% | -0.3% | -0.8% | -0.2% | -0.2% | -0.2%
average | 0.0% | -0.5% | -0.9% | -0.28% | -0.24% | -0.18%
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Balloons | 0.0% | -1.3% | -0.8% | -0.4% | -0.3% | -0.4%
Kendo | 0.0% | 0.4% | -0.1% | 0.1% | 0.1% | 0.2%
Newspaper | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1%
average | 0.0% | -0.2% | -0.6% | -0.16% | -0.14% | -0.09%
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Balloons | 0.0% | -0.8% | -0.5% | -0.2% | -0.2% | -0.4%
Kendo | 0.0% | 1.9% | 1.5% | 0.7% | 0.7% | 0.4%
Newspaper | 0.0% | 0.1% | 0.2% | 0.1% | 0.0% | -0.1%
average | 0.0% | 0.1% | -0.2% | -0.02% | 0.00% | -0.08%
Sharp
(D0061)
Samsung
(D0114)
LG
(D0096)
0.2 % gain (up to 1.1% gain) compared to the simplest one (D0096)

## Slide 18: Remark
Compared with MCP, IC’s computation cost is not high
We recommend to adopt the best performance method