## Slide 1
1. Summary
2. Proposed Method
3. Experimental Results
4. Conclusion
Contents
CE6.h related : Removal of DC from SDC Mode (JCT3V-D0066)
China TV Lab. / Media Part
Hongbin Liu, Jie Jia, Jin Heo, Junghak Nam
(LG Electronics)

## Slide 2: Summary
Proposed Method
  Remove DC mode from SDC
Performance
  CTC: -0.1% coding gain on synthesized view
  All intra: -0.1% coding gain on synthesized view
Crosscheck
  JCT3V-Dxxxx (by MediaTek)
JCT3V-D0066

## Slide 3: Proposed Method
Problem
  In SDC, DC mode is inefficient because
    It is selected with low probability
    It requires to assign 2 bits for binary index of DMM1 and Planar modes.
Fig.1. Probability distribution of four modes in SDC
a) Statistics results (CTC)
b) Statistics results (All intra)
Intra Prediction Mode | Binary Index
Intra_DC | 1
Intra_DepthPartition( 35 ) | 01
Intra_Planar | 00
JCT3V-D0066

## Slide 4: Proposed Method
Solution
  Remove DC mode from SDC
Intra Prediction Mode | Binary Index
Intra_DepthPartition( 35 ) | 1
Intra_Planar | 0
Table 2: Modified Binary Index
JCT3V-D0066

## Slide 5: Experimental Results (CTC)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1% | 99.9% | 99.9%
Kendo | 0.0% | 0.1% | 0.2% | 0.0% | 0.0% | -0.1% | 100.0% | 100.0%
Newspaper_CC | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | -0.1% | 99.6% | 100.0%
GT_Fly | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 100.1% | 100.0%
Poznan_Hall2 | 0.0% | -0.2% | -0.9% | -0.2% | -0.3% | -0.3% | 99.5% | 99.7%
Poznan_Street | 0.0% | 0.4% | 0.1% | 0.1% | 0.0% | 0.0% | 99.6% | 100.1%
Undo_Dancer | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.5% | 99.5% | 99.9%
1024x768 | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | -0.1% | 99.8% | 100.0%
1920x1088 | 0.0% | 0.0% | -0.2% | -0.1% | -0.1% | -0.2% | 99.7% | 99.9%
average | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 99.7% | 99.9%
JCT3V-D0066

## Slide 6: Experimental Results (All Intra)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.4% | 98.4%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | 100.3% | 97.7%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 99.1% | 100.6%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 113.1% | 101.1%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | 110.3% | 99.0%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 109.7% | 101.3%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 115.1% | 100.8%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 99.6% | 98.9%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 112.1% | 100.5%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 106.7% | 99.8%
JCT3V-D0066

## Slide 7: Conclusion
Propose method
  Remove DC mode from SDC
Performance
  -0.1% coding gain
It is recommended to adopt proposed method into 3D-HEVC
JCT3V-D0066