## Slide 1
1. Summary
2. Proposed Method
3. Experimental Results
4. Conclusion
Contents
CE1.h related : Unification of Disparity Vector Accuracy in VSP with Motion Vector/Disparity Vector Accuracy in Temporal/Inter-View Prediction for Depth Coding (JCT3V-D0068)
China TV Lab. / Media Part
Hongbin Liu, Jie Jia, Taesup Kim
(LG Electronics)

## Slide 2: Summary
Proposed Method
  For depth coding, unify disparity vector accuracy in VSP with motion vector/disparity vector used in temporal/inter-view prediction,
  i.e., use integer-pel disparity vector in VSP
Performance
  No compress performance loss
Crosscheck
  JCT3V-Dxxxx (by Hisilicon)
JCT3V-D0068

## Slide 3: Proposed Method
Problem
  For depth coding, in VSP, sub-pel disparity vector is employed, however, integer-pel motion vector/disparity vector is used in temporal/inter-view prediction
Solution
  Unify accuracy of motion vector and disparity vector, i.e., also use integer-pel disparity vector in VSP for depth coding
JCT3V-D0068

## Slide 4: Experimental Results (CTC)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons | 0.0% | 0.00% | 0.00% | 0.00% | 0.00% | 0.02% | 106.5% | 99.9%
Kendo | 0.0% | 0.00% | 0.00% | 0.00% | 0.00% | 0.01% | 114.0% | 100.0%
Newspaper_CC | 0.0% | 0.00% | 0.00% | 0.00% | 0.02% | 0.00% | 99.3% | 99.8%
GT_Fly | 0.0% | 0.00% | 0.00% | 0.00% | -0.01% | -0.02% | 108.0% | 98.9%
Poznan_Hall2 | 0.0% | 0.00% | 0.00% | 0.00% | -0.01% | -0.01% | 102.7% | 99.7%
Poznan_Street | 0.0% | 0.00% | 0.00% | 0.00% | 0.00% | 0.02% | 102.6% | 99.9%
Undo_Dancer | 0.0% | 0.00% | 0.00% | 0.00% | -0.02% | -0.03% | 106.1% | 99.3%
1024x768 | 0.0% | 0.00% | 0.00% | 0.00% | 0.00% | 0.01% | 106.6% | 99.9%
1920x1088 | 0.0% | 0.00% | 0.00% | 0.00% | -0.01% | -0.01% | 104.9% | 99.5%
average | 0.0% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 105.6% | 99.6%
JCT3V-D0068

## Slide 5: Conclusion
Propose method
  Unify accuracy of motion vector and disparity vector for depth coding
Performance
  No compress coding loss
It is recommended to adopt proposed method into 3D-HEVC
JCT3V-D0068