## Slide 1
1. Summary
2. Proposed Method
3. Experimental Results
4. Conclusion
Contents
Non-CE: Simplified Inter Mode Coding of Depth (JCT3V-D0069)
China TV Lab. / Media Part
Hongbin Liu, Jie Jia, Junghak Nam
(LG Electronics)

## Slide 2: Summary
Proposed Method
  Encode one residual for each prediction unit of the inter mode coded depth CU.
Performance
  CTC: -0.1% coding gain for texture coding and -0.6% coding gain for synthesized view
  4.7% encoding time increase and negligible decoding time change
Crosscheck
  JCT3V-D0206 (by Qualcomm)
JCT3V-D0069

## Slide 3: Proposed Method
Basic idea
  Encode one residual for each prediction unit of the inter mode coded depth CU
  Table1: Number of residuals for different partition modes
Partition mode | SIZE_2Nx2N | SIZE_2NxN, SIZE_2NxnU, SIZE_2NxnD, SIZE_Nx2N, SIZE_nLx2N, SIZE_nRx2N | SIZE_NxN
Residual number | 1 | 2 | 4
JCT3V-D0069

## Slide 4: Proposed Method
  Details
  Residual calculation
    it is set to the difference between average of the original signal and average of the prediction signal
    No quantization
  One flag is encoded for each inter-coded but non-skipped CU to indicate if the CU employs proposed method
  Rate distortion optimized selection between proposed approach and approaches in 3D-HEVC
JCT3V-D0069

## Slide 5: Proposed Method
JCT3V-D0069
if ( icEnableFlag ) | 
ic_flag | ae(v)
if( DepthFlag && PredMode[ x0 ][ y0 ] ! = MODE_INTRA && !skip_flag[ x0 ][ y0 ] ) | 
inter_sdc_flag | ae(v)
if ( inter_sdc_flag ) | 
{ | 
puNum = ( PartMode = = PART_2Nx2N ) ? 1 : ( PartMode = = PART_NxN ? 4 : 2 ) | 
for( i = 0; i < puNum; i++ ) | 
{ | 
inter_sdc_resi_abs [ x0 ][ y0 ][ i ] | ae(v)
if( inter_sdc_resi_abs [ x0 ][ y0 ][ i ] ) | 
inter_sdc_resi_sign_flag[ x0 ][ y0 ][ i ] | ae(v)
} | 
} | 
if( !pcm_flag ) { | 
if( PredMode[ x0 ][ y0 ] != MODE_INTRA && !(PartMode = = PART_2Nx2N && merge_flag[x0][y0]) ) | 
no_residual_syntax_flag | ae(v)
if( !no_residual_syntax_flag && !sdc_flag && !inter_sdc_flag ) { | 
MaxTrafoDepth = ( PredMode[ x0 ][ y0 ] = = MODE_INTRA ? max_transform_hierarchy_depth_intra + IntraSplitFlag : max_transform_hierarchy_depth_inter ) | 
transform_tree( x0, y0 x0, y0, log2CbSize, 0, 0 ) | 
} | 
… | 
} | 

## Slide 6: Experimental Results (CTC)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons | 0.0% | -0.1% | 0.1% | 0.0% | 0.2% | -0.3% | 104.7% | 100.8%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.4% | -0.3% | 104.2% | 101.0%
Newspaper_CC | 0.0% | 0.0% | 0.2% | 0.0% | 0.5% | -0.3% | 104.5% | 101.0%
GT_Fly | 0.0% | -0.5% | -0.5% | -0.1% | 0.4% | -0.8% | 106.9% | 100.6%
Poznan_Hall2 | 0.0% | -0.5% | -0.3% | -0.2% | 0.3% | -1.2% | 103.2% | 100.9%
Poznan_Street | 0.0% | -0.1% | 0.0% | 0.0% | 0.2% | -0.2% | 104.3% | 101.2%
Undo_Dancer | 0.0% | -0.3% | -0.4% | -0.1% | 0.2% | -0.9% | 105.0% | 100.9%
1024x768 | 0.0% | -0.1% | 0.1% | 0.0% | 0.4% | -0.3% | 104.5% | 100.9%
1920x1088 | 0.0% | -0.3% | -0.3% | -0.1% | 0.3% | -0.8% | 104.8% | 100.9%
average | 0.0% | -0.2% | -0.1% | -0.1% | 0.3% | -0.6% | 104.7% | 100.9%
JCT3V-D0069

## Slide 7: Conclusion
Propose method
  Encode one residual for each prediction unit of the inter mode coded depth CU.
Performance
  -0.1% coding gain for texture coding and -0.6% coding gain for synthesized view
  4.7% encoding time increase and negligible decoding time change
It is recommended to adopt proposed method into 3D-HEVC
JCT3V-D0069