## Slide 1: CE6.H related: Results on Modified Binarization for Region Boundary Chain Coding (JCT3V-D0076)
Peng Lu and Lu Yu (yul@zju.edu.cn)

## Slide 2: Problem Statement
In boundary chain coding, the syntax element edge_code is used to derive the edge direction.
Currently, truncated unary binarization is applied for the syntax element edge_code
edge_code | edge direction | bin string
0 | 0° | 0
1 | 45° | 10
2 | −45° | 110
3 | 90° | 1110
4 | −90° | 11110
5 | 135° | 111110
6 | −135° | 111111

## Slide 3: Problem Statement
However, statistical analysis shows that the occurring probabilities of the edge direction differ importantly.
Larger relative edge directions have smaller occurring probabilities.
The edge directions with the same absolute value but different sign have similar occurring probabilities.

## Slide 4
Proposed method
A new method of binarization is proposed
edge_code | edge direction | bin string
0 | 0° | 1
1 | 45° | 0 1 1
2 | −45° | 0 1 0
3 | 90° | 0 0 1 1
4 | −90° | 0 0 0 1
5 | 135° | 0 0 1 0
6 | −135° | 0 0 0 0

## Slide 5
Proposed method
The proposed binarization makes the probablity distribution sharper as this table shows
Bypass mode is used for the 3rd bin and 3 CABAC contexts are used for the 1st bin, the 2nd bin and the 4th bin, respectively.
Bin idx | probablity of being 1
1 | ≈ 69%
2 | ≈ 97%
3 | ≈ 50%
4 | ≈ 96%

## Slide 6
Experimental Results
Synth PSNR / total bitrate
  Common test condition (CTC)
    0.1% BD-rate gains
  All Intra
    0.005% BD-rate gains
Depth PSNR / depth bitrate
  Common test condition (CTC)
    0.3% BD-rate gains
  All Intra
    0.1% BD-rate gains

## Slide 7: Conclusion
This proposal modifies the binarization and CABAC context of the syntax element edge_code in region boundary chain coding.
This proposal achieves 0.1% and 0.005% BD-rate gains compared to 3D-HTM6.0 under the common test condition (CTC) and all intra test condition with the same encoding/decoding time.

## Slide 8
This concludes my presentation.
Thank You.
Q & A