## Slide 1: JCT3V-D0078 Deblocking for ALC in 3D-AVC (Cross-checked by JCT3V-D0280, JCT3V-D0298)
Kyung Hee University
K.Y. Kim, H.S. Hwang, G.H. Park

## Slide 2: Summary
In the last meeting, deblocking for ALC was proposed to remove the blocking artifacts caused by luminance changes.
  However, in the CTC (GOP size = 8), the subjective viewing result was similar to the anchor because the ALC only turns on in P-slices.
  We tested in IPPPP and IBBBP (GOP Size = 4) configuration.
    Actually the real market may frequently use the low latency configuration.
  Simulation results show that the simplified deblocking for ALC can improve the subjectively-visible blocking artifacts caused by block-based LC methodology, with slightly better coding gains.

## Slide 3: Motivation of this contribution
The ALC can improve the coding efficiency of 3DV-ATM.
However, the block-based LC (ALC) may generate subjectively-visible blocking artifacts.
Three Purposes
  Mandatory preprocessing for LC should be eliminated !!
  (WHY do we have both frame-based and block-based LC’s?)
  Subjectively-visible blocking artifacts caused by the block-based LC should be reduced.
  Computational complexity required for deblocking for block-based LC should be minimum.
We already have the deblocking for block-based LC for such three purposes.
We reminded and also tested two deblocking filters for block-based LC
  deblocking that had been adopted in the JMVM
  Simplified deblocking for ALC
Both can be simply integrated on the 3DV-ATM 7.0

## Slide 4: Proposed 3DV-ATM Architecture
Preprocessing for LC
(Luminance Compensation)
Block-based LC
(ALC)
3DV-ATM
Preprocessor
3D-Video
Bitstream
3DV-ATM
Preprocessor
3D-Video
Bitstream
Simplified
deblocking
Block-based LC
(ALC)
X
Current 3DV-ATM Architecture
Proposed 3DV-ATM Architecture
- Preprocessing for LC is necessary before 3DV-ATM applies
Block-based LC (ALC) is also required to improve coding efficiency
Hardware complexity for mandatory preprocessor is definitely burden
- If there is no preprocessing for LC, many blocking artifacts are subjectively-visible
- Preprocessing for LC is eliminated
Complexity of the simplified deblocking is almost negligible

## Slide 5: Facts: Blocking Artifacts caused by block-based LC
We made an investigation whether the block-based LC method causes the subjectively-visible blocking artifacts or not on the 3DV test sequences.
  Current 3DV test sequence were rectified and corrected for luminance by the preprocessor.
Also, we made an investigation on the MVC test sequences.
  MVC test sequences
    Ballroom, Exit, Uli, Race1, Flamenco2, Breakdancers, Rena, Akko&Kayo
  MVC test sequences had not been preprocessed for the LC.

## Slide 6: Facts: Blocking Artifacts caused by block-based LC in the MVC sequences
Block-based LC creates the blocking artifacts a lot in the MVC sequences
Anchor (3DV-ATM 7.0), Exit, VGA 1st view, 240th frame (QP=31)

## Slide 7: Facts: Blocking Artifacts caused by block-based LC in the MVC sequences
Block-based LC creates the blocking artifacts a lot in the MVC sequences
Anchor (3DV-ATM 7.0), Race1, VGA 1st view, 144th frame (QP=31)

## Slide 8: Facts: Blocking Artifacts caused by block-based LC in the MVC sequences
Block-based LC creates the blocking artifacts a lot in the MVC sequences
Anchor (3DV-ATM 7.0), Akko&Kayo, VGA 5th view, 216th frame (QP=31)

## Slide 9: Facts: Blocking Artifacts caused by block-based LC in the MVC sequences
Block-based LC creates the blocking artifacts a lot in the MVC sequences
Anchor (3DV-ATM 7.0), Rena, VGA 5th view, 18th frame (QP=31)

## Slide 10: Facts: Blocking Artifacts caused by block-based LC in the 3DV sequences
Block-based LC creates the blocking artifacts
Anchor (3DV-ATM 7.0), Kendo, 1024x768 5th view, 192th frame (QP=31)

## Slide 11: Facts: Blocking Artifacts caused by block-based LC in the 3DV sequences
Block-based LC creates the blocking artifacts
Anchor (3DV-ATM 7.0), Poznan_Street, 1920x1088 5th view, 236th frame (QP=31)

## Slide 12: (Case#1) Deblocking for the ALC that were adopted in the JMVM
Case#1. deblocking for the ALC that were adopted in the JMVM
  ( K1=1 (weak filtering), K2=3 (strong filtering), T=5 )
One||both of the p and q
is intra coded?
The edge
between p and q is
MB edge?
One||both of the p and q
has coded coefficient?
bS = 4
bS = 3
bS = 2
no
yes
yes
yes
no
Difference of
block motion >= 1 or
MC from different
reference frame
no
bS = 1
yes
no
boundary filtering strength
INTRA MODE
bS = 0
(Both p and q are ALC coded
&& their ALC values are not the same)
or
(the only one of the p and q
is ALC coded)
yes
no
bS = K1
ALC MODE
INTER MODE
bS = 0
X
|ValueALCp - ValueALCq|
>= T
yes
no
bS = K2

## Slide 13: (Case#2) Simplified Deblocking for ALC
Case#2. Simplified deblocking for ALC
One||both of the p and q
is intra coded?
The edge
between p and q is
MB edge?
One||both of the p and q
has coded coefficient?
bS = 4
bS = 3
bS = 2
no
yes
yes
yes
no
Difference of
block motion >= 1 or
MC from different
reference frame
no
bS = 1
yes
no
boundary filtering strength
INTRA MODE
bS = 0
(Both p and q are ALC coded
&& their ALC values are not the same)
or
(the only one of the p and q
is ALC coded)
yes
no
bS = 1
ALC MODE
INTER MODE
bS = 0
X

## Slide 14: Test Conditions
  Prediction structure: “IPPPP” and “IBBBP (GOP Size = 4)" configuration.
Two test sequences
  1. 3DV sequences
    The other configuration settings are same as “JCTVC-C1100”.
  2. MVC sequences (No-preprocessed)
    Ballroom, Exit, Uli, Race1, Flamenco2, Breakdancers, Rena, Akko&Kayo
    Configuration
      3DVCodingOrder = “T0T1T2D0D1D2” for independent coding between texture and depth.
        The default depth map is generated by setting all value to “128”.
      Texture view only : no view synthesis (because there are no depth maps in MVC sequences.)
      The other configuration settings are same as “JCTVC-C1100”.
      Input and output view to be used for experiments.
Test Sequence | Image Property | Frames to be encoded | 3-view input
Ballroom | 640x480, 25fps | 250 | 1-3-5
Exit | 640x480, 25fps | 250 | 1-3-5
Uli | 1024x768, 25fps | 250 | 1-3-5
Race1 | 640x480, 30fps | 300 | 1-3-5
Flamenco2 | 640x480, 30fps | 300 | 1-0-3
Breakdancers | 1024x768, 15fps | 100 | 1-3-5
Rena | 640x480, 30fps | 300 | 1-3-5
Akko&Kayo | 640x480, 30fps | 300 | 5-7-9

## Slide 15: Temporary bug fix in the FCO (T0-T1-T2-D0-D1-D2)
  The 3DV-ATM7.0 encoder crashes with the “T0-T1-T2-D0-D1-D2” configuration.
  This crash happens in the IVMP, therefore we modified the source code.
  This temporary bug-fix does not affect the simulation result, since the IVMP is coding method for the depth.
  This temporary bug fix has been applied for the simulation of the MVC test sequences.

## Slide 16: Simulation Results (IPPPP configuration)
The following Table shows the summary of the simulation results of the deblocking applied for the ALC of 3DV-ATM using two different kinds of the 3D video sequences.
  1. MVC video sequences: Sequences are not luminance-compensated (No-preprocessed).
    The amount of bits for depth map was excluded from the total amount of bits.
  2. 3DV video sequences: Many sequences are preprocessed for the luminance compensation.
Cross-checked by KWU (JCT3V-D0298)
 | Texture Coding |  | Depth Coding |  | Total (Coded PSNR) |  | Total (Synthesized PSNR) |  | Complexity estimate (ratio to anchor) | 
 | dBR | dPSNR | dBR | dPSNR | dBR | dPSNR | dBR | dPSNR | Enc. time | Dec. time
Test-1: MVC (deblocking for ALC) | -0.03 % | 0.00 dB | N/A | N/A | -0.03 % | 0.00 dB | N/A | N/A | 99 % | 101 %
Test-2: MVC (Simplified deblocking for ALC) | -0.06 % | 0.00 dB | N/A | N/A | -0.06 % | 0.00 dB | N/A | N/A | 99 % | 101 %
Test-3: 3DV (deblocking for ALC) | 0.07 % | 0.00 dB | 0.00 % | 0.00 dB | 0.07 % | 0.00 dB | 0.01 % | 0.00 dB | 99 % | 102 %
Test-4: 3DV (Simplified deblocking for ALC) | -0.01 % | 0.00 dB | 0.00 % | 0.00 dB | 0.00 % | 0.00 dB | -0.02 % | 0.00 dB | 99 % | 101 %

## Slide 17: Simulation Results (IBBBP configuration)
The following Table shows the summary of the simulation results of the deblocking applied for the ALC of 3DV-ATM using two different kinds of the 3D video sequences.
  1. MVC video sequences: Sequences are not luminance-compensated (No-preprocessed).
    The amount of bits for depth map was excluded from the total amount of bits.
  2. 3DV video sequences: Many sequences are preprocessed for the luminance compensation.
3DV result: Cross-checked by Samsung (JCT3V-D0280)
 | Texture Coding |  | Depth Coding |  | Total (Coded PSNR) |  | Total (Synthesized PSNR) |  | Complexity estimate (ratio to anchor) | 
 | dBR | dPSNR | dBR | dPSNR | dBR | dPSNR | dBR | dPSNR | Enc. time | Dec. time
Test-1: MVC (deblocking for ALC) | 0.00 % | 0.00 dB | N/A | N/A | 0.00 % | 0.00 dB | N/A | N/A | 100 % | 103 %
Test-2: MVC (Simplified deblocking for ALC) | -0.04 % | 0.00 dB | N/A | N/A | -0.04 % | 0.00 dB | N/A | N/A | 100 % | 102 %
Test-3: 3DV (deblocking for ALC) | 0.07 % | 0.00 dB | 0.00 % | 0.00 dB | 0.07 % | 0.00 dB | 0.03 % | 0.00 dB | 100 % | 102 %
Test-4: 3DV (Simplified deblocking for ALC) | 0.02 % | 0.00 dB | 0.00 % | 0.00 dB | 0.02 % | 0.00 dB | 0.01 % | 0.00 dB | 100 % | 103 %

## Slide 18: Subjective Comparisons in MVC sequences
Exit, VGA 1st view, 240th frame (QP=31)
(a) Anchor (3DV-ATM7.0)
(b) Simplified MVC deblocking (Case#2)

## Slide 19: Subjective Comparisons in MVC sequences
Exit, VGA 1st view, 240th frame (QP=31)
(a) Anchor (3DV-ATM7.0)
(b) Simplified MVC deblocking (Case#2)

## Slide 20: Subjective Comparisons in MVC sequences
Race1 640x480 1st view, 144th frame (QP=31)
(a) Anchor (3DV-ATM7.0)
(b) Simplified MVC deblocking (Case#2)

## Slide 21: Subjective Comparisons in MVC sequences
Race1 640x480 1st view, 144th frame (QP=31)
(a) Anchor (3DV-ATM7.0)
(b) Simplified MVC deblocking (Case#2)

## Slide 22: Subjective Comparisons in MVC sequences
Akko&Kayo 640x480 5th view, 216th frame (QP=31)
(a) Anchor (3DV-ATM7.0)
(b) Simplified MVC deblocking (Case#2)

## Slide 23: Subjective Comparisons in MVC sequences
Akko&Kayo 640x480 5th view, 216th frame (QP=31)
(a) Anchor (3DV-ATM7.0)
(b) Simplified MVC deblocking (Case#2)

## Slide 24: Subjective Comparisons in MVC sequences
Rena 640x480 5th view, 18th frame (QP=26)
(a) Anchor (3DV-ATM7.0)
(b) Simplified MVC deblocking (Case#2)

## Slide 25: Subjective Comparisons in MVC sequences
Rena 640x480 5th view, 18th frame (QP=26)
(a) Anchor (3DV-ATM7.0)
(b) Simplified MVC deblocking (Case#2)

## Slide 26: Subjective Comparisons in 3DV sequences
Kendo 1024x768 5th view, 192nd frame (QP=31)
(a) Anchor (3DV-ATM7.0)
(b) Simplified MVC deblocking (Case#2)

## Slide 27: Subjective Comparisons in 3DV sequences
Kendo 1024x768 5th view, 192nd frame (QP=31)
(a) Anchor (3DV-ATM7.0)
(b) Simplified MVC deblocking (Case#2)

## Slide 28: Subjective Comparisons in 3DV sequences
Poznan_Street 1920x1088 5th view, 236th frame (QP=31)
(a) Anchor (3DV-ATM7.0)
(b) Simplified MVC deblocking (Case#2)

## Slide 29: Subjective Comparisons in 3DV sequences
Poznan_Street 1920x1088 5th view, 236th frame (QP=31)
(a) Anchor (3DV-ATM7.0)
(b) Simplified MVC deblocking (Case#2)

## Slide 30: Conclusions
In this contribution, deblocking methods for the ALC of 3DV-ATM are introduced.
  Deblocking had previously been proposed and adopted for the JMVM in the MVC standardization.
Simulation results show that the simplified deblocking for ALC can improve the subjectively-visible blocking artifacts caused by block-based LC methodology, with slightly better coding gain.
By using the simplified deblocking, eliminations of both mandatory preprocessing for LC and the subjectively-visible blocking artifacts caused by block-based LC are possible, while the complexity required for deblocking for LC is negligible.
We strongly recommend to adopt the simplified deblocking for the ALC of 3DV-ATM WD.

## Slide 32: Simulation Results
The following Table shows the summary of the simulation results of the deblocking applied for the ALC of 3DV-ATM using two different kinds of the 3D video sequences.
  1. MVC video sequences: Sequences are not luminance-compensated (No-preprocessed).
    The amount of bits for depth map was excluded from the total amount of bits.
    Coding order: T0T1T2D0D1D2
  2. 3DV video sequences: Many sequences are preprocessed for the luminance compensation.
    In the CTC
 | Texture Coding |  | Depth Coding |  | Total (Coded PSNR) |  | Total (Synthesized PSNR) |  | Complexity estimate (ratio to anchor) | 
 | dBR | dPSNR | dBR | dPSNR | dBR | dPSNR | dBR | dPSNR | Enc. time | Dec. time
Test-1: MVC (deblocking for ALC) | 0.01 % | 0.00 dB | N/A | N/A | 0.01 % | 0.00 dB | N/A | N/A | 99 % | 102 %
Test-2: MVC (Simplified deblocking for ALC) | -0.02 % | 0.00 dB | N/A | N/A | -0.02 % | 0.00 dB | N/A | N/A | 99 % | 103 %
Test-3: 3DV (deblocking for ALC) | 0.08 % | 0.00 dB | 0.00 % | 0.00 dB | 0.08 % | 0.00 dB | 0.05 % | 0.00 dB | 100 % | 102 %
Test-4: 3DV (Simplified deblocking for ALC) | 0.03 % | 0.00 dB | 0.00 % | 0.00 dB | 0.03 % | 0.00 dB | 0.02 % | 0.00 dB | 100 % | 103 %

## Slide 33: Facts: Blocking Artifacts caused by IC (or ALC)
Block-based LC creates the blocking artifacts
Left image shows the boundary filtering strengths (bS) between IC block boundaries (bS=0: Red, bS=1: Blue, bS=2: Green, bS=3: Magenta, bS=4: Cyan) in the Ballroom QVGA 3rd view, 191st frame (QP=37) and right image shows the magnified image of the white-dashed rectangle of the left image indicated by the white arrow.

## Slide 34: Facts: Blocking Artifacts caused by IC (or ALC)
Block-based LC creates the blocking artifacts
Left image shows the boundary filtering strengths (bS) between IC block boundaries (bS=0: Red, bS=1: Blue, bS=2: Green, bS=3: Magenta, bS=4: Cyan ) in Exit QVGA sequence 3rd view, 12th frame (QP=37), and right image shows the magnified image of the white-dashed rectangle of the left image indicated by the white arrow.

## Slide 35: Can AVC Deblocking cover ALC?
INTRA vs. IC (or ALC) block case
  AVC/H.264 deblocking can cover IC (or ALC) (using bS = 3 or 4)  No problem!!
INTER vs. IC (or ALC) block case (or IC (or ALC) block vs. IC (or ALC) block)
  If there are coded coefficients?
    AVC/H.264 deblocking can cover IC (or ALC) (using bS = 2)  No problem!!
  If there are no coded coefficients && if their motions are different || their references are different
    AVC/H.264 deblocking can cover IC (or ALC) (using bS = 1)  No problem!!
INTER &
IC (or ALC)
Block
INTER &
IC (or ALC)
Block
INTER &
IC (or ALC)
Block
INTER &
IC (or ALC)
Block
Vertical boundary
Horizontal boundary
INTER &
IC (or ALC)
Block
INTER
Block
INTER &
IC (or ALC)
Block
INTER
Block
Horizontal boundary
Vertical boundary
INTER &
IC (or ALC)
Block
INTRA
Block
INTER &
IC (or ALC)
Block
INTRA
Block
Vertical boundary

## Slide 36: Most IC blocking artifacts are shown due to NO-Filtering in case bS=0
  Otherwise, all of the following conditions is true, the bS = 0  NO filtering
    INTER &&
    There are NO coded coefficients &&
    They have same or similar MV and Reference
INTER &
IC (or ALC)
Block
INTER &
IC (or ALC)
Block
INTER &
IC (or ALC)
Block
INTER &
IC (or ALC)
Block
Vertical boundary
INTER &
IC (or ALC)
Block
INTER
Block
INTER &
IC (or ALC)
Block
INTER
Block
Horizontal boundary
Vertical boundary

## Slide 37: Most IC blocking artifacts are shown due to NO-Filtering
Balloons sequence in the 3DV-ATM6.0 anchor,
  If all of the following conditions is true,  Frequency is 86%.
    (Condition 1) P Slice && bS == 0 && MB boundary && (P_SKIP || P_L0_16x16) && the one of the p or q is ALC coded
  Otherwise if all of the following conditions is true,  Frequency is 6%.
    (Condition 2) P Slice && bS != 0 && MB boundary && (P_SKIP || P_L0_16x16) && the one of the p or q is ALC coded
  Otherwise if all of the following conditions is true,  Frequency is 8%.
    (Condition 3) P Slice && MB boundary && the one of the p or q is ALC coded
Most of blocking artifacts of ALC are subjectively shown to users due to NO FILTERING (bS = 0).
Balloons | QP26 | QP31 | QP36 | QP41
Condition 1 | 76 % | 86 % | 90 % | 93 %
Condition 2 | 7 % | 7 % | 6 % | 6 %
Condition 3 | 17 % | 8 % | 4 % | 2 %
INTER &
IC (or ALC)
Block
INTER &
IC (or ALC)
Block
INTER &
IC (or ALC)
Block
INTER &
IC (or ALC)
Block
Vertical boundary
INTER &
IC (or ALC)
Block
INTER
Block
INTER &
IC (or ALC)
Block
INTER
Block
Horizontal boundary
Vertical boundary

## Slide 38: Highlight: Fact & Attack point
Many IC (or ALC) blocks are SKIPPED or DIRECT (P_16x16 in ALC) MB’s
NO-FILTERING is massively assigned to those blocks in the AVC deblocking
Therefore, no filtering is applied to many IC (or ALC) blocks.
FACT: about 86% of IC (or ALC) blocks are assigned to bS = 0 (no-filtering)
NO-FILTERING brings the subjective blocking-artifacts
Let’ make a NEW process for the block-based LC especially in the case of the boundary condition is assigned to bS = 0 (no-filtering).
It is simple to construct and cost-effective deblocking for block-based LC.

## Slide 39: Deblocking for ALC
We remind and test two deblocking methods for block-based LC.
  Case#1. deblocking that were adopted in the JMVM
    This method is same as deblocking for IC in JMVM.
  Case#2. Simplified deblocking for ALC.
    This method is same as Case#1.
    But, the process of comparison of the ALC weighting value between P and Q block using threshold is removed.
  Deblocking for ALC is carried out with the cost of minimum complexity, because it covers only bS = 0 case and it is carried out the MB boundary.

## Slide 40: (Case#1) Deblocking for the ALC that were adopted in the JMVM
Case#1. deblocking for the ALC that were adopted in the JMVM
  ( K1=1 (weak filtering), K2=3 (strong filtering), T=5 )
One||both of the p and q
is intra coded?
The edge
between p and q is
MB edge?
One||both of the p and q
has coded coefficient?
bS = 4
bS = 3
bS = 2
no
yes
yes
yes
no
Difference of
block motion >= 1 or
MC from different
reference frame
no
bS = 1
yes
no
boundary filtering strength
INTRA MODE
bS = 0
(Both p and q are ALC coded
&& their ALC values are not the same)
or
(the only one of the p and q
is ALC coded)
yes
no
bS = K1
ALC MODE
INTER MODE
bS = 0
X
|ValueALCp - ValueALCq|
>= T
yes
no
bS = K2

## Slide 41: (Case#2) Simplified Deblocking for ALC
Case#2. Simplified deblocking for ALC
One||both of the p and q
is intra coded?
The edge
between p and q is
MB edge?
One||both of the p and q
has coded coefficient?
bS = 4
bS = 3
bS = 2
no
yes
yes
yes
no
Difference of
block motion >= 1 or
MC from different
reference frame
no
bS = 1
yes
no
boundary filtering strength
INTRA MODE
bS = 0
(Both p and q are ALC coded
&& their ALC values are not the same)
or
(the only one of the p and q
is ALC coded)
yes
no
bS = 1
ALC MODE
INTER MODE
bS = 0
X

## Slide 42: Comparison of the Case#1 and Case#2
Difference is process of comparison of the ALC weighting value between P and Q block using threshold.
  Case#1. deblocking for ALC that were adopted in the JMVM
  Case#2. Simplified deblocking for ALC
In case the boundary conditions for deblocking filter satisfies bS = 0 IF ALC is applied to both comparing blocks & their ALC values are not same OR ALC is applied to only ONE block (the other block is not coded by ALC mode) IF ¦ValueALCp-ValueALCq¦ >= T (=5) SET bS = K2 (=3: strong deblocking) ELSE SET bS = K1 (=1: weak deblocking) OTHERWISE SET bS = 0
In case the boundary conditions for deblocking filter satisfies bS = 0 IF ALC is applied to both comparing blocks & their ALC values are not same OR ALC is applied to only ONE block (the other block is not coded by ALC mode) SET bS = 1 OTHERWISE SET bS = 0

## Slide 43: Simple WD
Just insert the text into section J.8.8.2.1
  Case#1. deblocking for the ALC that were adopted in the JMVM
  Case#2. Simplified deblocking for ALC
– If values of mb_alc_skip_flag or mb_alc_flag for the luma blocks of the samples of both p0 and q0 are equal to 1 and the ALC weighting value of the luma block of the samples of p0 is different from the ALC weighting value of the luma block of the samples of q0, or value of mb_alc_skip_flag or mb_alc_flag for the luma blocks of the samples p0 or q0 is equal to 1, the following applies:
  - If the absolute difference of the ALC weighting value between the two blocks of samples of p0 and q0 is greater than or equal to 5, a value of bS equal to 3 shall be the output.
  - Otherwise, a value of bS equal to 1 shall be the output.
– Otherwise, a value of bS equal to 0 shall be the output.
– If values of mb_alc_skip_flag or mb_alc_flag for the luma blocks of the samples of both p0 and q0 are equal to 1 and the ALC weighting value of the luma block of the samples of p0 is different from the ALC weighting value of the luma block of the samples of q0, or value of mb_alc_skip_flag or mb_alc_flag for the luma blocks of the samples p0 or q0 is equal to 1, the following applies:
  - If the absolute difference of the ALC weighting value between the two blocks of samples of p0 and q0 is greater than or equal to 5, a value of bS equal to 3 shall be the output.
  - Otherwise, a value of bS equal to 1 shall be the output.
– Otherwise, a value of bS equal to 0 shall be the output.