## Slide 1: 3D-CE2.a: MB-level depth-to-DV conversion in ATM
J.-L. Lin, Y.-W. Chen, Y.-W. Huang, S. Lei (MediaTek),
J. Y. Lee, H.-C. Wey, C. Kim (Samsung)
G. Bang, W.-S. Cheong, N. Hur (ETRI)
K. Y. Kim, Y. S. Heo, G. H. Park (KHU)
Presented by Jian-Liang Lin
4th JCT3V Meeting in Incheon
20–26 Apr. 2013

## Slide 2: Overall Summary
In Inter mode, depth-to-DV conversion needs to be performed multiple times for motion vector prediction to derive DVs for various partition blocks in one MB
Propose to let all partition blocks of Inter mode within the same MB share the same DV
The proposed scheme brings no coding loss while the complexity and memory access bandwidth are reduced

## Slide 3: Depth-to-DV Conversion in Skip/Direct
To derive the inter-view MVP for Skip/Direct mode, the depth-to-DV conversion is only needed to be performed once for each MB
The DV is derived from a maximum depth value of four corner samples of the associated depth block of current MB

## Slide 4: Depth-to-DV Conversion in Inter Mode
Depth-to-DV conversion is employed to derive a DV for unavailable neighboring blocks
Perform multiple times for various partitions for one MB
For example, if current MB is partitioned into 16 4x4 blocks, the depth-to-DV conversion is performed 16 times

## Slide 5: Proposed MB-level Depth-to-DV Conversion
All partition blocks of Inter mode within the same MB share the same DV
The depth-to-DV conversion needs to be performed only once for Skip/Direct and Inter mode for each MB
Inter mode
Skip/Direct

## Slide 6: Experiment Results
Anchor : ATM-7.0
Test : ATM-7.0 with the proposed MB-level Depth-to-DV conversion scheme
No coding loss
  Results crosschecked and confirmed in JCT3V-D0232 (NTT)

## Slide 7: Additional Experiment
Based on the proposed MB-level depth-to-DV conversion
The basic unit for VSP is also enlarged from 4x4 to 8x8
0.17% overall BD-rate increase
  Results crosschecked and confirmed in JCT3V-D0232 (NTT)

## Slide 8: Comparison of the number of the depth sample access
Compared to the anchor, the proposed simplification can significantly reduce the number of memory access at worst cases (4x4) with almost no coding loss.
 | Number of memory access |  |  |  |  | 
 | BVSP |  | Motion Partition |  |  | 
 |  |  | MV Prediction |  |  | Skip/ Direct
 | 4x4 | 8x8 | 4x4 | 8x8 | 16x16 | 
Anchor (ATM-7.0) | 64 | - | 64 | 16 | 4 | 4
Experiment (MB-level DV conversion) | 64 | - | 4 | 4 | 4 | 4
Additional Experiment (MB-level DV conversion & 8x8 VSP) | - | 16 | 4 | 4 | 4 | 4

## Slide 9: Conclusion
Proposes a MB-level depth-to-DV conversion scheme to simplify current design
Depth-to-DV conversion only needs to be performed once for Skip/Direct and Inter mode for each MB
No coding loss while the complexity and memory access bandwidth are reduced

## Slide 10: Thank you for your attention!