## Slide 1: 3D-CE5.h related: Additional Inter-view Merging Candidate
Jian-Liang Lin, Yi-Wen Chen, Yu-Wen Huang, Shawmin Lei
JCT3V-D0109
Presented by Jian-Liang Lin
4th JCT-3V Meeting in Incheon
20–26 Apr. 2013

## Slide 2: Overall Summary
In this contribution, an additional inter-view merging candidate is proposed.
In the pruning process, the additional inter-view candidate is only compared with the original inter-view candidate.
The experimental results show 0.2%, 0.1% and 0.1% coding gain for video1, video2, and overall results, respectively.

## Slide 3: The Merging Candidate List in HTM6.0
Original merging candidate list
Inter-view candidate (I)
A1
B1
B0
A0
Disparity candidate (DV)
B2
VSP candidate
Temporal candidate (H or C)
The size of candidate list is fixed to 6.

## Slide 4: The Proposed Merging Candidate List
Propose to add an additional inter-view candidate to improve the coding efficiency
Proposed merging candidate list
Inter-view candidate (I)
A1
B1
B0
A0
Disparity candidate (DV)
B2
VSP candidate
Additional inter-view candidate (I2)
Temporal candidate (H or C)
derived from a corresponding block which is located as the H position shifted by the same DV in the candidate list

## Slide 5: Pruning Process
In the pruning process, the additional inter-view candidate is only compared to the first inter-view candidate.

## Slide 6: Experiment Results
Anchor : HTM-6.0 under CTC
0.1% coding gain
Results are crosscheck and confirmed by Sharp (JCT3V-D0256)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -0.2% | -0.3% | -0.1% | -0.1% | -0.2% | 98.3% | 102.7% | 94.7%
Kendo | 0.0% | -0.1% | -0.2% | -0.1% | -0.1% | -0.2% | 98.5% | 100.0% | 99.2%
Newspaper_CC | 0.0% | -0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 98.7% | 100.6% | 100.9%
GT_Fly | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 99.1% | 101.6% | 98.7%
Poznan_Hall2 | 0.0% | -0.6% | -0.1% | -0.2% | -0.2% | -0.1% | 100.3% | 99.3% | 102.2%
Poznan_Street | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 99.2% | 99.7% | 96.9%
Undo_Dancer | 0.0% | -0.1% | -0.2% | -0.1% | -0.1% | -0.2% | 99.3% | 101.4% | 98.8%
1024x768 | 0.0% | -0.2% | -0.2% | -0.1% | -0.1% | -0.1% | 98.5% | 101.1% | 98.3%
1920x1088 | 0.0% | -0.1% | 0.0% | -0.1% | -0.1% | -0.1% | 99.5% | 100.5% | 99.1%
average | 0.0% | -0.2% | -0.1% | -0.1% | -0.1% | -0.1% | 99.1% | 100.8% | 98.8%

## Slide 7: Conclusions
Propose to add an additional inter-view candidate in the merging candidate list for texture coding.
The redundancy checking of this additional candidate is only compared with the original inter-view candidate to save the computational complexity.
The simulation results show 0.2%, 0.1% and 0.1% coding gain for video1, video2 and overall results, respectively.
We suggest add include this additional candidate into the merging candidate list to improve the coding efficiency.

## Slide 8: Thanks for your attention!
www.mediatek.com

## Slide 9: Backup