## Slide 1: 3D-CE6.h related: Sample-based Simplified Depth Coding
Jian-Liang Lin, Yi-Wen Chen, Yu-Wen Huang, Shawmin Lei
JCT3V-D0110
Presented by Jian-Liang Lin
4th JCT-3V Meeting in Incheon
20–26 Apr. 2013

## Slide 2: Overall Summary
In current SDC design, all depth samples in one coding partition are represented by a same reconstructed value even when the intra coding mode is planar mode.
This contribution proposes to update each prediction sample by adding a same residual
  instead of changing all the prediction samples to a same reconstructed value.
The experimental results show
  0.2% coding gain for overall video over total bitrates in both CTC and all-Intra
  0.2% and 0.1% coding gain for the synthesized view in CTC and all-Intra, respectively

## Slide 3: Simplified Depth Coding (SDC)
Three intra modes are applied in SDC
  DC mode (1 partition)
  DMM mode 1 (2 partitions)
  Planar mode (1 partition)
Input:
  The mean of the original depth value
  The mean of the prediction samples of current depth block generated by intra prediction DC, DMM mode1, or Planar mode
A depth lookup table (DLT) is used to map the mean of the original depth value and the mean of the prediction samples to index values.
The residual of each partition is coded by transmitting a constant residual value to the decoder.

## Slide 4: The Reconstruction Process in SDC (1/2)
DC mode
DMM mode 1
residual
PredDC
RecDC
residual1
PredDC1
RecDC1
residual2
PredDC2
RecDC2
PredDC1
PredDC2
PredDC
RecDC
RecDC1
RecDC2

## Slide 5: The Reconstruction Process in SDC (2/2)
Planar mode
In current SDC design, all depth samples are represented by a same reconstructed depth value when the intra prediction mode is planar mode.
residual
PredDC
RecDC
RecDC
PredDC

## Slide 6: Proposed Method
Propose to add the residual on each prediction sample instead of using a same reconstructed value to represent all depth samples.
residual
Px,y
P’x,y

## Slide 7: Source Code Modification
for( UInt uiY = 0; uiY < uiHeight; uiY++ ) {
for( UInt uiX = 0; uiX < uiWidth; uiX++ ) {
UChar ucSegment = pMask?(UChar)pMask[uiX]:0;
assert( ucSegment < uiNumSegments );
Pel pResiDC = apDCResiValues[ucSegment];
#if MTK_SAMPLE_BASED_SDC
pReco [ uiX ] = Clip( pPred[ uiX ] + pResiDC );
#else
Pel pPredVal= apDCPredValues[ucSegment];
pReco [ uiX ] = Clip( pPredVal + pResiDC );
#endif
pRecIPred[ uiX ] = pReco[ uiX ];
}
}
Add 1 line
Remove 2 lines

## Slide 8: Experiment Results - CTC
Anchor : HTM-6.0 under CTC
0.2% coding gain
Results are crosscheck and confirmed by Sharp (JCT3V-D0257) and Intel (JCT3V-D0281).
Identical results in JCT3V-D0136 proposed by LG

## Slide 9: Experiment Results – All Intra
Anchor : HTM-6.0 under All Intra test conditions
0.2% coding gain for video over total bit-rate
0.1% coding gain for the synthesized view

## Slide 10: Conclusions
Propose to add the residual on each prediction sample
  instead of using a same reconstructed value to represent all depth samples
  keep the smooth surface generated by the intra prediction.
The simulation results show
  0.2% coding gain for overall video over total bitrates in both CTC and all-Intra
  0.2% and 0.1% coding gain for the synthesized view in CTC and all-Intra, respectively
We suggest to adopt this modification into HTM.

## Slide 11: Thanks for your attention!
www.mediatek.com

## Slide 12: The reconstruction process in SDC
DC mode
DMM mode 1

## Slide 13: The reconstruction process in SDC (2/2)
Planar mode
DMM mode 1
residual
PredDC
RecDC
residual1
PredDC1
RecDC1
residual2
PredDC2
RecDC2
PredDC1
PredDC2
PredDC
RecDC
RecDC1
RecDC2

## Slide 14: The reconstruction process in SDC
DC mode
DMM mode 1