## Slide 1
JCT3V-D0112 – CE2.h related: Default Disparity Vector Derivation
Min Woo Park
Multimedia Platform Lab.
DMC R&D Center
Samsung Electronics

## Slide 2: Current DV Derivation
Initialization
  availableDV is set to 0
  DV is set to (0, 0) by Default  “Default DV”
NBDV derivation
  When DV is found, availableDV is set to 1.
After NBDV derivation
  If availableDV == 1 (DV is available),
    Refine DV from coded depth map
    Using Refined DV for inter-view prediction
  If availableDV == 0 (DV is not available)
    Using Default DV (0, 0) for inter-view prediction
    It might cause inaccuracy inter-view prediction
      Default DV (0, 0) may be far different from a Real DV
availableDV = 0,
DV = (0, 0)
NBDV derivation
availableDV == 1 &&
deriveFromDepthFlag == 1
DV refinement
Start
End
no
yes

## Slide 3: Proposed Method
After NBDV derivation, If DV is not available (availableDV == 0)
  Refine Default DV (0, 0) from coded depth map
Refined default DV might be more accurate than Default DV (0, 0)
  Because Real DV normally has non-zero vector.
  Thus, More coding gains can be expected by using Refined default DV
availableDV = 0,
DV = (0, 0)
NBDV derivation
availableDV == 1 &&
deriveFromDepthFlag == 1
DV refinement
Start
End
yes
no
availableDV == 0
no
yes

## Slide 4: Experimental Results
Based on CTC w/ HTM6.0
  0.2% gain on dependent view
  0.1% gain on coded and synthesized view

## Slide 5: Conclusions
We propose a refinement of Default DV (0, 0)
  Minor changes in 3D-HEVC text and HTM software
  0.2% gain on dependent view
  0.1% gain on coded and synthesized view
We recommend to adopt the proposed method into next 3D-HEVC TM.
Thanks to Qualcomm for the cross checking (JCT3V-D0276).