## Slide 1
JCT3V-D0113– CE2.h related: Simplification of DV Derivation
Min Woo Park
Multimedia Platform Lab.
DMC R&D Center
Samsung Electronics

## Slide 2: Current Disparity Vector Derivation
1st Step: NBDV derivation
  Temporal Candidates Search  BR, Col in co-located & RAP pic.
  Spatial Candidates Search  A1, B1, B0, A0, and B2
  DV-MCP  A1, B1, B0, A0, and B2
2nd Step: Depth based derivation
  Find corresponding depth block by using NBDV
  Max. depth value  DV
Depth
Texture
View 0
View 1
NBDV
Current
block
Final DV
convert
Current block
B2
A1
A0
B1
B0
Co-located block
BR
Col
Spatial
Candidates (MV search
& DV-MCP search)
Temporal
Candidates (in co-located picture &
RAP picture)
NBDV’s accuracy decides the accuracy of DV
NBDV derivation
(from Temporal and Spatial Candidates)

## Slide 3: Proposed Method
1st Step: Depth based derivation
  Find corresponding depth block by using initial DV
  Max. depth value  1st DV
2nd Step: Depth based derivation
  Find corresponding depth block by using 1st DV
  Max. depth value  DV
Depth
Texture
View 0
View 1
1st DV
Current
block
Initial DV
Final DV
Depth value 128
convert
convert
convert
(NBDV) vs. (1st DV)
If 1st DV has better accuracy compared to NBDV,
the accuracy of DV might be also enhanced, and more coding gains can be expected.
  Initial DV is set to corresponding value of depth value 128 (1 << (bit depth-1))

## Slide 4: Experimental Result
Based on CTC w/ HTM6.0
  0.2% and 0.4% gain on video 1 and video 2
  0.1% gain on overall coded and synthesized view

## Slide 5: Conclusions
We propose a simplification method for DV derivation
  Only using coded depth information
  Text simplification (saving 3-page of specification)
  In spite of the simplification,
    0.2% and 0.4% coding gain on dependent view
    0.1% coding gain on coded and synthesized view
We recommend to adopt the proposed method into next 3D-HEVC TM
Thanks NTT for the cross checking (JCT3V-D0230).