## Slide 1
JCT3V-D0114 – CE5.h related: Simplification of Illumination Compensation
Min Woo Park
Multimedia Platform Lab.
DMC R&D Center
Samsung Electronics

## Slide 2: Contents
Method 1: Simplification of Scale factor
Method 2: Applying IC to 2Nx2N partition only
Method 3: Derivation of top-left sample in the reference block
Method 4: Preventing useless decoding process

## Slide 3: Simplification of Scale Factor Derivation
Current derivation for the scale factor
  There are numerous multiplications
  In one CU, this derivation is performed for
    every PUs
    every prediction directions (reference list 0 and list 1)
    every color component (Y, U and V) and depth.
  e.g. When PU partition mode is NxN & each PU is bi-predictive mode
    4 (NxN) x 2 (bi-predictive) x 3 (Y, U, and V) = 24 times
Current
: Correlation between NBcurr and NBref
Proposed : Remove multiplicative terms
: Ratio of NBcurr to NBref
current block
NBref
NBcurr
ref. block

## Slide 4: Simplification of Scale Factor Derivation
Test results (CTC w/ HTM6.0)
  0.1% and 0.3% gain on dependent view
  0.1% gain on overall video

## Slide 5: Applying IC to 2Nx2N only
Current
  IC is applied to all PU partition sizes
Proposed Method
  Apply IC to 2Nx2N partition only
    Number of neighboring pixel can be represented as the power of 2
    At Encoder side, mode decision for IC doesn’t need below 2Nx2N PU size
Test Results (CTC w/ HTM6.0): no coding loss

## Slide 6: Derivation of top-left sample
In the current IC parameter derivation
  When deriving the top-left sample of the reference block
  If DV points fractional sample position (a, b, c,…, o), above-left integer sample position (A) is always selected.
  If the nearest integer sample is chosen, the coding efficiency can be increased

## Slide 7: Derivation of top-left sample
Proposed Method
  To point the nearest integer sample  Apply the rounding offset
  Spec. modification
Test Results (CTC w/ HTM6.0): 0.1% gain on dependent view
H.8.5.2.2.5.1 Derivation process for illumination compensation mode availability and parameters
  The luma location (xRLX, yRLX) specifying the top-left sample of the reference block in refPicLX is derived as
    xRLX = xC + ( (mvLX[ 0 ] + 2 + (cIdx ? 2 : 0) ) >> (2 + (cIdx ? 1 : 0)) ) (H 193)
    yRLX = yC + ( (mvLX[ 1 ] + 2 + (cIdx ? 2 : 0) ) >> (2 + (cIdx ? 1 : 0)) ) (H 194)
  to top-left sample derivation

## Slide 8: Preventing Useless Decoding Process
After IC parameter derivation
  Some combinations of the scale factor and the offset do not need to perform the IC (e.g. the scale factor == 1 & the offset == 0)
  Frequency of these cases  almost 6%
a : the scale factor b : the offset
Unnecessary Processing

## Slide 9: Preventing Useless Decoding Process
Proposed Method
  Selectively applying IC by checking these cases
  Spec. modification
  Test Results (CTC w/ HTM6.0): no coding loss
H.8.5.2.2.5.1 Derivation process for illumination compensation mode availability and parameters
…
3. The derivation process for illumination compensation parameters as specified in subclause H.8.5.2.2.5.2 is invoked, with the list of neighbouring samples in the current picture curNeighSampleList, the list of neighbouring samples in the reference picture refNeighSample list, the number of neighbouring samples numNeighSamlesLX and the size of the current luma coding block nCSl as inputs and the illumination parameters icWeightLX, icOffsetLX and icShiftLX as outputs.
4. If icWeightLX is equal to (1 << icShiftLX) and icOffsetLX is equal to 0, puIcFlagLX is set to equal to 0.

## Slide 10: Combining All Methods
Combining all methods (1, 2, 3 and 4)
  Based on CTC w/ HTM6.0
  0.2% and 0.6% gain on dependent view
  0.2% and 0.1% gain on coded and synthesized view

## Slide 11: Summary of Result
More coding gains are obtained when combining all methods

## Slide 12: Conclusions
We propose 4 methods for illumination compensation
  In spite of the simplification,
    0.2% and 0.6% coding gain on dependent view
    0.2% and 0.1% coding gain on coded and synthesized view
  When combining all method, more coding gains are observed
We recommend to adopt all proposed methods into next 3D-HEVC TM
  Method 1: Simplification of the scale factor derivation
  Method 2: Applying IC to 2Nx2N partition only
  Method 3: Derivation of top-left sample in the reference block
  Method 4: Preventing useless decoding process
Thanks LG for the cross checking (JCT3V-D0146).