## Slide 1
Skip Flag Coding
Jin Young Lee
Multimedia Platform Lab.
DMC R&D Center
Samsung Electronics

## Slide 2: Skip Flag Coding
When the left and above blocks are coded with Skip in B slices, it is highly possible for the current block to be coded with Skip.
 Propose more efficient run-length skip flag coding in this case (Max length=16)
S
S
S

## Slide 3: mb_skip_run_type
Proposed run-length coding is controlled by syntax mb_skip_run_type
If mb_skip_run_type = 1, skip flag is infered to 1 until the condition is broken
If mb_skip_run_type = 0, skip flag is not infered
S
S
S
Blk
NS
S
S
mb_skip_run_type = 1
En/decoding Blk
S
S
S
NS
S
S
S
En/decoding NS Blk
mb_skip_run_type = 0
skip_flag = 1
skip_flag = 1
skip_flag = 1
S
S
S
S
NS
NS

## Slide 4: Results
About 1% gain in overall views and synthesizes views