## Slide 1
JCT3V-D0123: DMM Simplification and Signalling
Jin Young Lee
Multimedia Platform Lab.
DMC R&D Center
Samsung Electronics

## Slide 2: Current DMM
For the efficient edge coding, four DMMs were developed
  DMM1 : Explicit wedgelet partitioning
  DMM2 : intra-predicted wedgelet partitioning
  DMM3 : inter-component wedgelete partitioning
  DMM4 : inter-component-predicted contour partitioning
Each DMM has two sub-modes based on a deta constant partition value (CPV)
dmm_mode | Method identifier
0 | MODE_DMM_WFULL
1 | MODE_DMM_WFULLDELTA
2 | MODE_DMM_WPREDTEX
3 | MODE_DMM_WPREDTEXDELTA
4 | MODE_DMM_CPREDTEX
5 | MODE_DMM_CPREDTEXDELTA
6 | MODE_DMM_WPREDDIR
7 | MODE_DMM_WPREDDIRDELTA
for( j = 0; j <= pbOffset; j = j + pbOffset )
for( i = 0; i <= pbOffset; i = i + pbOffset )
if (dmm_flag[ x0 + i ][ y0+ j ] )
dmm_mode[ x0 + i ][ y0+ j ]

## Slide 3: DMM Simplification
Four DMMs were developed with a simliar concept, so they are very redundant
It is observed that DMM1 is very dominant in terms of the performance
The proposed method uses only DMM1 including two sub-modes
for( j = 0; j <= pbOffset; j = j + pbOffset )
for( i = 0; i <= pbOffset; i = i + pbOffset )
if (dmm_flag[ x0 + i ][ y0+ j ] )
delta_dc_flag[ x0 + i ][ y0+ j ]
delta_dc_flag [ x0 ][ y0 ] equal to 0 specifies that delta dc is not used for depth modeling mode. delta_dc_flag[x0][y0] equal to 1 specifies that delta dc is used. When the delta_dc_flag[x0][y0] is not present, its value should be inferred to be equal to 0

## Slide 4: Results #1
Removing DMM3 and DMM4, which use the texture component
Minor gain in CTC and encoding time reduction by 96.8%.
Minor loss in AI, but significant encoding time reduction by 81.5%
CTC
AI

## Slide 5: Results #2
Using only DMM1
No loss in CTC and encoding time reduction by 94.7%.
Minor loss in AI, but significant encoding time reduction by 74.0%
Significant WD reduction (removed about eight pages)
CTC
AI

## Slide 6: Conclusion
No coding loss, and encoding/decoding time reduction in CTC
Minor coding loss, but singnificant encoding/decoding time reduction in AI
Significant WD ruduction