## Slide 1
3D-CE5.h related: Unification of disparity vector rounding
(JCT3V-D0135)
April 2013
LG Electronics
Junghak Nam (junghak.nam@lge.com)
Sehoon Yea (sehoon.yea@lge.com)

## Slide 2: Summary
Unification of Conversion of disparity vector to corresponding block
Proposed method
  Use of rounding operation for disparity vector with rounding offset
Experimental results
  CTC: 0.1% coding gain on synthesized view
Crosscheck
  JCT3V-D0128 (by Samsung)
<number>

## Slide 3: Current 3D-HEVC
In HTM-6.0, a disparity vector (DV) is used to find a virtual depth block or a corresponding texture block in reconstructed base view
  DoNBDV
    DV derived by NBDV process is exploited to find a virtual depth block
  2) IVMP
    Refined DV from DoNBDV process is used to find a corresponding PU
  3) B-VSP
    DV is used to get a corresponding virtual depth block to select PU-wise max depth value
  4) IC
    DV is used to get reference samples to calculate IC parameters
Problem statements
  Discrepancy in rounding operations with respect to rounding offset
    With offset: 2)
    Without offset: 1), 3), 4)
<number>

## Slide 4: Proposed method
Proposal
  Unification of DV rounding with rounding offset
<number>
The reference layer luma location ( xRef, yRef ) is derived by xRef = Clip3( 0, PicWidthInSamplesL – 1, xP + ( ( nPSW – 1 ) >> 1 ) + ( ( mvDisp[ 0 ] + 2 ) >> 2 ) ) (H‑161) yRef = Clip3( 0, PicHeightInSamplesL – 1, yP + ( ( nPSH – 1 ) >> 1 ) + ( ( mvDisp[ 1 ] + 2 ) >> 2 )) (H‑162)
< Draft modification of DoNBDV and B-VSP with rounding offset >
< Draft modification of IC with rounding offset >
< Draft modification of IVMP with rounding offset > - no change

## Slide 5: Experimental results
 | video 0 | video 1 | video 2 | video PSNR /video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons | 0.0% | -0.2% | -0.1% | -0.1% | 0.0% | -0.1% | 99.5% | 98.0%
Kendo | 0.0% | -0.5% | 0.0% | -0.1% | -0.1% | -0.1% | 99.7% | 100.6%
Newspapercc | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1% | 99.9% | 106.3%
GhostTownFly | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 99.7% | 99.7%
PoznanHall2 | 0.0% | 0.3% | -0.2% | 0.0% | -0.1% | 0.0% | 99.7% | 100.5%
PoznanStreet | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | 0.0% | 99.9% | 100.2%
UndoDancer | 0.0% | -0.4% | 0.2% | 0.0% | 0.0% | -0.4% | 99.9% | 99.1%
1024x768 | 0.0% | -0.3% | 0.0% | -0.1% | 0.0% | -0.1% | 99.7% | 101.7%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 99.8% | 99.9%
average | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | -0.1% | 99.8% | 100.6%
<number>
<3DV-HTM 6.0 vs. overall results for DV rounding offset>
<3DV-HTM 6.0 vs. DV rounding offset for DoNBDV>
 | video 0 | video 1 | video 2 | video PSNR /video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.6% | 98.1%
Kendo | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 99.6% | 102.1%
Newspapercc | 0.0% | 0.0% | 0.2% | 0.0% | 0.1% | 0.1% | 99.6% | 107.5%
GhostTownFly | 0.0% | 0.2% | 0.1% | 0.0% | 0.0% | 0.0% | 99.8% | 102.3%
PoznanHall2 | 0.0% | -0.7% | 0.0% | -0.2% | -0.2% | -0.1% | 99.7% | 99.0%
PoznanStreet | 0.0% | 0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 99.9% | 99.7%
UndoDancer | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 99.9% | 100.4%
1024x768 | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 99.6% | 102.6%
1920x1088 | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 99.8% | 100.4%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.7% | 101.3%

## Slide 6: Experimental results
 | video 0 | video 1 | video 2 | video PSNR /video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 99.8% | 95.2%
Kendo | 0.0% | 0.2% | 0.2% | 0.0% | 0.0% | 0.0% | 99.7% | 96.2%
Newspapercc | 0.0% | -0.1% | 0.2% | 0.0% | 0.1% | 0.1% | 99.8% | 98.5%
GhostTownFly | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 99.6% | 98.9%
PoznanHall2 | 0.0% | -0.3% | -0.5% | -0.2% | -0.2% | -0.1% | 99.9% | 100.2%
PoznanStreet | 0.0% | 0.3% | 0.1% | 0.1% | 0.0% | 0.0% | 100.1% | 104.8%
UndoDancer | 0.0% | -0.4% | 0.1% | 0.0% | 0.0% | -0.1% | 100.1% | 94.5%
1024x768 | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 99.8% | 96.7%
1920x1088 | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 99.9% | 99.6%
average | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 99.9% | 98.4%
<number>
<3DV-HTM 6.0 vs. DV rounding offset for B-VSP>
<3DV-HTM 6.0 vs. DV rounding offset for IC parameters derivation>
 | video 0 | video 1 | video 2 | video PSNR /video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons | 0.0% | -0.2% | 0.0% | 0.0% | 0.0% | -0.1% | 100.0% | 101.8%
Kendo | 0.0% | -0.4% | -0.2% | -0.1% | -0.1% | -0.1% | 100.1% | 96.9%
Newspapercc | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1% | 100.1% | 101.6%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.2% | 98.6%
PoznanHall2 | 0.0% | 0.0% | -0.4% | -0.1% | -0.1% | 0.0% | 100.2% | 94.8%
PoznanStreet | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 100.3% | 95.9%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.3% | 98.0%
1024x768 | 0.0% | -0.2% | -0.1% | -0.1% | -0.1% | -0.1% | 100.1% | 100.1%
1920x1088 | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 100.3% | 96.8%
average | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 100.2% | 98.2%

## Slide 7: Conclusion
Proposed method
  Use of rounding operation for disparity vector with rounding offset
Experimental results
  CTC: 0.1% coding gain on synthesized view
It is recommended to adopt proposed method into 3D-HEVC
<number>