## Slide 1
3D-CE6.h related: Improvement of SDC coding
(JCT3V-D0136)
April 2013
LG Electronics
Junghak Nam (junghak.nam@lge.com)
Hongbin Liu (hongbin.liu@lge.com)
Sehoon Yea (sehoon.yea@lge.com)

## Slide 2: Summary
Modification of depth value reconstruction process for Simplified Depth Coding (SDC)
Proposed method
  Use of predicted samples instead of DC of predicted samples in order to get recon. samples
Experimental results
  CTC: 0.2% coding gain on synthesized view
  All intra: 0.1% coding gain on synthesized view
Crosscheck
  JCT3V-D0159 (by Samsung)
<number>

## Slide 3: Current 3D-HEVC
Problem statements
  In current 3D-HEVC, use of Dcpred to get reconstructed samples in SDC
<number>
Planar
Predicted samples
DC of predicted samples
SDC residuals
+
Reconstructed samples
DMM1
+
=
=
DC
+
=
resSamples[ x ][ y ] = dcPred[ wedgePattern[ x ][ y ] ] + SdcResidual[ xB ][ yB ][ wedgePattern[ x ][ y ] ]

## Slide 4: Proposed method
Proposal: use of predicted samples for depth value reconstruction
  Reconstructed samples are calculated by adding SDC residuals with predicted samples instead of DC of predicted samples
  Fidelity of reconstructed samples could be improved by maintaining shape of the predicted samples
  There is no affect for DMM1 mode in SDC
<number>
  resSamples[ x ][ y ] = predSamples[ x ][ y ] + SdcResidual[ xB ][ yB ][ wedgePattern[ x ][ y ] ]
DC
Planar
+
Predicted samples
SDC residuals
+
Reconstructed samples
=
=

## Slide 5: Experimental results
 | video 0 | video 1 | video 2 | video PSNR /video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons | 0.0% | -0.1% | 0.0% | 0.0% | -0.3% | -0.1% | 101.3% | 98.0%
Kendo | 0.0% | 0.1% | 0.0% | 0.0% | -0.5% | -0.3% | 101.4% | 98.6%
Newspapercc | 0.0% | -0.1% | 0.1% | 0.0% | -0.1% | 0.0% | 100.8% | 99.4%
GhostTownFly | 0.0% | -0.6% | -0.2% | -0.1% | -0.4% | -0.4% | 100.8% | 98.4%
PoznanHall2 | 0.0% | -0.3% | 0.2% | 0.0% | -0.1% | 0.1% | 100.9% | 97.5%
PoznanStreet | 0.0% | 0.0% | 0.1% | 0.0% | -0.3% | -0.3% | 100.4% | 97.6%
UndoDancer | 0.0% | -0.2% | -0.2% | -0.1% | -0.1% | -0.4% | 100.8% | 97.7%
1024x768 | 0.0% | -0.1% | 0.0% | 0.0% | -0.3% | -0.1% | 101.2% | 98.6%
1920x1088 | 0.0% | -0.3% | 0.0% | 0.0% | -0.2% | -0.2% | 100.7% | 97.8%
average | 0.0% | -0.2% | 0.0% | 0.0% | -0.2% | -0.2% | 100.9% | 98.2%
<number>
<3DV-HTM 6.0 vs. CTC>
<3DV-HTM 6.0 vs. All Intra>
 | video 0 | video 1 | video 2 | video PSNR /video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | -0.3% | 0.0% | 103.4% | 98.7%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | -0.3% | 0.0% | 103.7% | 96.1%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.1% | 102.4% | 100.8%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | -0.2% | 97.7% | 100.7%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 104.7% | 99.0%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | -0.2% | 99.4% | 98.7%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 99.0% | 99.9%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | 0.0% | 103.2% | 98.5%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | 100.2% | 99.6%
average | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | -0.1% | 101.5% | 99.1%

## Slide 6: Conclusion
Proposed method
  Use of predicted samples instead of DC of predicted samples in order to get recon. samples
Experimental results
  CTC: 0.2% coding gain on synthesized view
  All intra: 0.1% coding gain on synthesized view
It is recommended to adopt proposed method into 3D-HEVC
<number>