## Slide 1: JCT3V-D0140 3D-HEVC HLS: Camera parameter signaling and Depth reference selection
Yu-Lin Chang, Yu-Pao Tsai, Shawmin Lei
Presented by Yu-Lin Chang
JCT on 3D Video Coding Extension Development
Apr., 2013

## Slide 2: Overall Summary
In 3D-HEVC, depth oriented tools were used but without proper switch and depth reference mechanism
  Current camera parameter signaling scheme is designed for texture first coding order – BVSP and DoNBDV may fail while coding order is changed
  BVSP and DoNBDV always use the depth picture in base view for depth reference
Proposed high level syntax for camera parameter and depth oriented tools
  Propose a depth_dependence_flag to explicitly control the depth oriented tools and the transmission of camera parameter
Proposed adaptive depth reference for depth oriented tools
  Propose to use proper depth reference adaptively under different coding order
  Performance
    Introduce 0.1% coding efficiency gain in the synthesized view over total bitrate against 3D-HTM 6.1 with flexible coding order on
Notes:     Problem and proposeVSP off, finding inter-view reference without warping

## Slide 3: Introduction to Camera Parameter
Camera parameter in the current 3D-HTM works differently under different coding order
  Inconsistent cam-param signaling scheme might increase the parsing througput
  Parsing dependency may exist for current mechanism under texture first coding order
Coding order | Cam-param of texture layer | Cam-param of depth layer
Texture first | Always sent in SPS | Always derived from texture layer of the same view
Depth first | Always sent in SPS | Always sent in SPS

## Slide 4: Proposed VPS for Camera Parameter
depth_dependence_flag for switching the depth oriented tools and signaling camera parameter
  vsp_compensation_flag – enable BVSP
  vsp_dv_refine_flag – enable DoNBDV
vps_extension2( ) { | Descriptor
… | 
if ( (layerId ! = 0) && !DepthLayerFlag[ layerId ] ) { | 
iv_mv_pred_flag[ layerId ] | u(1)
iv_res_pred_flag[ layerId ] | u(1)
depth_dependence_flag [ layerId ] | u(1)
if( depth_dependence_flag [ layerId ] != 0 ){ | 
vsp_compensation_flag [ layerId ] | u(1)
vsp_dv_refine_flag [ layerId ] | u(1)
} | 
} | 
if ( DepthLayerFlag[ layerId ] ) { | 
if ( (layerId ! = 0) | 
vsp_compensation_flag [ layerId ] | u(1)
… | 
} | 

## Slide 5: Proposed SPS for Camera Parameter
Propose to send camera parameter according to depth_dependence_flag
  In order to reduce parsing dependency, other_view_count is transmitted to let know how many camera parameters are there
sps_extension2( ) { | Descriptor
if( !VpsDepthFlag[ nuh_layer_id ] depth_dependence_flag[ nuh_layer_id ] ) { | 
cp_precision | ue(v)
cp_in_slice_header_flag | u(1)
if( !cp_in_slice_header_flag ) { | 
other_view_count | ue(v)
for ( i = 0; i < ViewId[ nuh_layer_id ]other_view_count; i++ ) { | 
cp_scale[ i ] | se(v)
cp_off[ i ] | se(v)
cp_inv_scale_plus_scale[ i ] | se(v)
cp_inv_off_plus_off[ i ] | se(v)
} | 
} | 
} | 
} | 

## Slide 6: Proposed Slice Header for Camera Parameter
Transmit camera parameter in slice header if required
slice_header_extension( ) { | Descriptor
if( cp_in_slice_header_flag && depth_dependence_flag ) { | 
for ( i = 0; i < ViewIdx; i++ ) { | 
cp_scale[ i ] | se(v)
cp_off[ i ] | se(v)
cp_inv_scale_plus_scale[ i ] | se(v)
cp_inv_off_plus_off[ i ] | se(v)
} | 
} | 
} | 

## Slide 7: Introduction to Depth Reference
In current 3D-HEVC, DoNBDV and BVSP all use the depth picture in base view as the depth reference because texture-first coding order is used
The depth picture in the same view provides better accuracy and less memory buffer to store the depth map
CB
T1
Coded D0
Associated depth
Estimated disparity vector
Virtual depth
CB
T1
Coded D0
Collocated depth
Depth availability under texture first coding order
Depth availability under depth first coding order
Coded D1

## Slide 8: Proposed Adaptive Depth Reference for DoNBDV and BVSP
Propose to use the depth picture in the same view for BVSP while vsp_comensation_flag = 1
Propose to use the depth picture in the same view for DoNBDV while vsp_dv_refine_flag = 1
 | depth_dependence_flag=0 | depth_dependence_flag=1
Depth first | BVSP off | BVSP from collocated current depth if vsp_compensation_flag is on
Texture first | BVSP off | BVSP from associated base depth if vsp_compensation_flag is on
 | depth_dependence_flag=0 | depth_dependence_flag=1 and vsp_dv_refine_flag=1
Depth first | From neighbor block disparity vector | From collocated depth block in the current view
Texture first | From neighbor block disparity vector | From associated depth block in the base view

## Slide 9: Experiment Results – HTM 6.1 FCO
Anchor: HTM 6.1 CTC
Test: HTM 6.1 with flexible coding order enabled

## Slide 10: Experiment Results – Proposed Adaptive Depth Reference vs HTM 6.1 FCO
Anchor: HTM 6.1 with flexible coding order enabled
Test: Proposed adaptive depth reference

## Slide 11: Conclusions
The camera parameters are proposed to be signaled in a normative way for both texture-first coding and depth-first coding
  An explicit flag is proposed to enable the depth oriented coding tools under different coding order while avoiding parsing dependencies
Adaptations on BVSP and DoNBDV are proposed to utilize proper depth reference under different coding order
  Depth buffer can be reduced
  Provide 0.1% coding efficiency gain on synthesized view over total bitrate against HTM 6.1 FCO

## Slide 12: Thanks for your attention!
www.mediatek.com