## Slide 1: Unification of the Reference View for Inter-view Motion Prediction and Inter-view Residual Prediction
Jicheng An, Jian-Liang Lin, Kai Zhang, and Shawmin Lei
Presented by Jian-Liang Lin
104th MPEG Meeting in Incheon
20-26 Apr., 2013

## Slide 2: Overall Summary
Unify the reference view for the inter-view motion prediction and inter-view residual prediction
  Providing a syntax in slice header to identify the reference view picture from the reference lists
    Unification of signaling reference view and collocated temporal reference picture
    More flexibility in reference view selection
  Prohibiting the reference view to be changed on every slice in a same picture
    Facilitate the management of decoded motion and residual data
No RD performance impact (0.0% for synthesized results).
<number>

## Slide 3: Reference View Setting in HTM6.0
Reference view for inter-view motion prediction (IVMP)
  The view with smallest view index in reference list.
Reference view for inter-view residual prediction (IVRP)
  The view with view index equal to 0.
The IVRP is combined with IVMP, so the reference views for IVMP and for IVRP should be unified.
<number>

## Slide 4: Proposed Unification of the Reference View
Similar to the signalling of the collocated reference picture
Signal the reference view from reference lists in the slice header, and semantically restrict that all slices in a picture shall point to a same reference view picture.
<number>

## Slide 5: Proposed Unification of the Reference View (cont.)
Benefits
  Unification of reference view for IVMP and IVRP
  Unification of signaling reference view and collocated temporal reference picture
  Facilitate the management of decoded motion and residual data
  More flexibility in reference view selection
<number>

## Slide 6: Experimental Results
Proposed method vs. HTM6.0
  Only difference is that more several bits in slice header
<number>

## Slide 7: Conclusions
Unify the reference view for the inter-view motion prediction and inter-view residual prediction
  Providing a syntax in slice header to identify the reference view picture from the reference lists
  Prohibiting the reference view to be changed on every slice in a same picture
Unification of signaling reference view and collocated temporal reference picture
Facilitate the management of decoded motion and residual data
More flexibility in reference view selection
No RD performance impact (0.0% for synthesized results)
<number>

## Slide 8: Thanks for your attention!