## Slide 1: 3D-CE4.h related: Limited inter-view residual prediction by CBF checking
Jicheng An, Kai Zhang, Jian-Liang Lin, and Shawmin Lei

## Slide 2: Overall Summary
Disable the inter-view residual prediction when the center TU in the reference block does not contain non-zero coefficients.
  Remove many inefficient IVRP cases whose reference residual block contain mostly the zero samples.
  9% decoding time reduction
  0.1% BD-rate gain for V1, V2
<number>

## Slide 3: Inter-view residual prediction in HTM6.0
The IVRP is enabled when the temporal inter-view merge candidate with 2Nx2N partition is selected.
A derived DV is used to locate the reference block in reference view to do IVRP.
However, in many cases, the reference residual block contains few non-zero transform coefficients. In those cases, the RD performance cannot justify the computational cost due to the addition operations.
<number>

## Slide 4: Proposed CBF Checking
Disable the IVRP if the transform unit (TU), which covers the center sample of the reference block in reference view, does not contain non-zero CBF.
Thus, the inefficient reference residual blocks which mostly contain zero residual samples would be removed from the IVRP mode so that the average computational complexity is reduced.
<number>

## Slide 5: Experimental Results
Proposed method vs. HTM6.0
<number>

## Slide 6: Conclusions
Disable the inter-view residual prediction when the center TU in the reference block does not contain non-zero coefficients.
  Remove many inefficient IVRP cases whose reference residual block contain mostly the zero samples.
  9% decoding time reduction
  0.1% BD-rate gain for V1, V2
<number>

## Slide 7: Thank you!

## Slide 8: Advanced residual prediction for multiview coding (D0177, QC)
Increased Encoding RDO times.
  3 times need to try: ARP weight = 0, 1, 0.5
  11% encoding time increase.
Increased syntax element to parsing in CU level
  More CABAC contexts needed.
Two kinds of interpolation filters
  DCTIF and bilinear
  Implementation cost
More reference pictures needed in on-chip memory.
  Two more ref pic with ref_idx=0 from both lists.
  More motion compensation in baseview
<number>