## Slide 1: D0151 CE6.h: results on an efficient coding method for DLT in 3DVC
Kai Zhang, Jicheng An, Shawmin Lei

## Slide 2: Overall Summary
Problem in the current HTM
  Depth lookup table (DLT) is coded in Exp-Golomb code in SPS
  It is inefficient so the size of SPS becomes very large
Proposed
  A range constrained bit map (RCBM) is used to code DLT
    The minimum and maximum values in DLT are signalled
    It is indicated by a bit in RCBM whether a value is in DLT or not
Results
  Reduce 2/3 of the original DLT size
  In CE6 test 3 ( DLT in SPS as HTM-6.0 )
    Similar coding performance to the anchor.
    Reduce 43% of the original SPS size

## Slide 3: Problem in the current HTM
Depth lookup table (DLT) is coded in Exp-Golomb code in SPS
DLT requires a large amount of bits
  Statistics on the four sequences turning on DLT, average DLT size is 557.33 bits, and accounts for more than 65% bits in SPS
The worst case of DLT coding
  If values from 128 to 255 are in DLT, DLT requires 1937 bits
  If values from 0 to 255 are all in DLT, DLT requires 3365 bits
The DLT size in worst case determines the buffer size for SPS

## Slide 4: Proposed
A Range Constrained Bit Map (RCBM) coding method
  First, the minimum and maximum values in DLT is signalled
  Values between them are signalled by a bit map. One flag in the map corresponds to one value.
    Whether a value is in DLT or not depends on the corresponding flag is 1 or 0
  Alternately, a full bit map can be coded without signalling the minimum and maximum values in DLT
code_full_bit_map_flag[layerId ] | u(1)
if(!code_full_bit_map_flag[layerId ]){ | 
min_dlt_value[layerId ] | u(v)
diff_max_dlt_value[layerId ] | u(v)
} | 
for(j=0;j< MaxDltValue[layerId ] - min_dlt_value[layerId ] – 1;j++) | 
bit_map_flag[layerId ][j] | u(1)

## Slide 5: Benefits
DLT can be compressed more efficiently
  RCBM generates only 34% bits as many as the anchor to code DLT averagely on the four test sequences with DLT on.
DLT can be coded in a fixed length
  257 bits is required by DLT coded in full bit map, this can also be regarded as the worst case
The coding method is direct and simple without any optimization for the test sequences
  The method is applicable to any sequences since it is not designed based on the characteristics of the test sequences
Bit map coding is friendly to error control
  One bit error in the bit map only affects one value in DLT without any error propagation

## Slide 6: Results
In average of the four sequences with DLT on, DLT size is reduced to 34%, thus SPS size is reduced to 58%.
 |  | DLT Size (bits) |  |  | SPS Size (bits) |  | 
 |  | Anchor | Proposed | P/A (%) | Anchor | Proposed | P/A (%)
Balloons | V0_depth | 555 | 213 | 38.38% | 845 | 503 | 59.53%
 | V1_depth | 641 | 257 | 40.09% | 937 | 553 | 59.02%
 | V2_depth | 617 | 255 | 41.33% | 915 | 553 | 60.44%
Kendo | V0_depth | 485 | 191 | 39.38% | 775 | 481 | 62.06%
 | V1_depth | 637 | 255 | 40.03% | 933 | 551 | 59.06%
 | V2_depth | 649 | 257 | 39.60% | 947 | 555 | 58.61%
Newspapercc | V0_depth | 606 | 191 | 31.52% | 896 | 481 | 53.68%
 | V1_depth | 621 | 195 | 31.40% | 917 | 491 | 53.54%
 | V2_depth | 696 | 213 | 30.60% | 994 | 511 | 51.41%
PoznanHall2 | V0_depth | 420 | 111 | 26.43% | 712 | 403 | 56.60%
 | V1_depth | 380 | 101 | 26.58% | 678 | 399 | 58.85%
 | V2_depth | 381 | 104 | 27.30% | 681 | 404 | 59.32%
Average |  | 557.33 | 195.25 | 34.39% | 852.50 | 490.42 | 57.68%

## Slide 7: Results
Coding performance is similar to the anchor because SPS only takes a small percentage in the entire bit-stream.
RA
AI

## Slide 8: Conclusion
Proposed
  A range constrained bit map (RCBM) is used to code DLT
    The minimum and maximum values in DLT are signalled
    It is indicated by a bit in RCBM whether a value is in DLT or not
Results
  Reduce 2/3 of the original DLT size
  In CE6 test 3 ( DLT in SPS as HTM-6.0 )
    Similar coding performance to the anchor.
    Reduce 43% of the original SPS size

## Slide 9: Thank you for your attention!