## Slide 1: D0152 CE5.h related: removal of parsing dependency for illumination compensation
Kai Zhang, Yi-Wen Chen, Jicheng An, Jian-Liang Lin, Shawmin Lei

## Slide 2: Overall Summary
Problem in the current HTM
  Illumination compensation (IC) introduces a parsing dependency since ic_flag is conditionally signalled in 3D-HEVC
Proposed
  Make two modifications to slices with both inter-view and inter-time reference pictures in the reference lists
    ic_flag is only signalled for an inter CU coded as one 2Nx2N PU
    ic_flag of a merge PU is derived from the selected merging candidate
  Remove the parsing dependency without introducing redundancy bits
Results
  0.1% increases in BD-rates for video1 and video2 on average

## Slide 3: Problem in the current HTM
ic_flag is parsed or not depends on whether inter-view prediction is used in the current CU
  No parsing dependency in two trivial cases
    if only inter-view reference pictures exist, ic_flag is always parsed in inter-CU
    if only inter-time reference pictures exist, ic_flag is never parsed in inter-CU
When both inter-view and inter-time reference pictures exist
  If all PUs in a CU are coded in AMVP mode
    No parsing dependency because reference indices are explicitly signalled
  If a PU in a CU is coded in merge mode: parsing dependency
    The reference index is derived from the selected merging candidate
    Then depends on neighbouring MVs due to the pruning process
    Finally depends on the collocated picture because the neighbouring MV may come from TMVP

## Slide 4: Problem in the current HTM
An example of the parsing dependency in IC
  Ref0: inter-time reference picture; Ref1: inter-view reference picture
  The second possible candidate is removed in the pruning process
    Thus the selected candidate refers to Ref1, ic_flag should be parsed
  If the collocated picture is damaged
    TMVP is wrong MVb is wrong Mva != MVb
    The second possible candidate is not removed
    The selected candidate refers to Ref0, ic_flag should not be parsed
Parsing error
Notes:   CU is coded in 2Nx2N merge mode, with Merge index = 1
  The reference indices from the first three candidates are 0, 0, and 1
  The MVs from the first two candidates are equal, i.e., Mva = MVb.
  MVb is obtained by TMVP from the collocated picture.
  This implies a dependency on the collocated picture

## Slide 5: Proposed
Straightforward way: always signal ic_flag for each inter-CU
This simple method can resolve the parsing problem with considerable overhead bits for signalling redundant ic_flag
To reduce the overhead, a picture-level IC on/off encoder strategy based on POC difference is designed
  IC is turned off on a picture if the absolute POC differences of one or more reference pictures are lower than a threshold
  The threshold is set to be 2 empirically
Notes:   The threshold is set to be 2 empirically
  Since the parsing problem only occurs when the slice has both inter-view and inter-time reference pictures in the reference lists, two modifications are applied to those slices.

## Slide 6: Proposed
Another method is proposed to remove the parsing dependency without introducing redundant bits
  Two modifications for slices with both inter-view and inter-time reference pictures since parsing problem only occurs on these slices
    ic_flag is only signalled for an inter CU coded as one 2Nx2N AMVP PU. For PUs with other sizes in non-merge mode, IC is disabled
    ic_flag of a merge PU is derived from the selected merging candidate

## Slide 7: Results
The simple method
  In average
    About 0.3% and 0.5% BD-rate increases for v1 and v2 respectively
    0.1% BD-rate increase for synthesis views
  Worst case (Kendo )
    BD-rate increase for synthesis views goes up to 0.6%

## Slide 8: Results
The proposed method
  In average
    About 0.1% BD-rate increases for v1 and v2
    No BD-rate increase for synthesis views
  Worst case (Kendo )
    BD-rate increase for synthesis views goes up to 0.1%

## Slide 9: Thank you for your attention!