## Slide 1: D0155 CE6.h related: Direct simplified depth coding in 3D-HEVC
Kai Zhang, Jicheng An, Jian-Liang Lin, Yi-Wen Chen, Shawmin Lei

## Slide 2: Overall Summary
Problem in the current HTM
  Simplified depth coding (SDC) is adopted for depth intra-coding
  A two-step ( intra prediction and averaging ) approach is applied to obtain the prediction values in SDC segments
    The two-step method introduces a high complexity
Proposed
  Remove the two-step method
  Instead, the prediction values are calculated from the neighbouring reconstructed samples directly by a simple rule
Results
  Can save 0.2% and 0.1% BD-rate on the synthesized view in the common test condition and all-intra test condition respectively

## Slide 3: Problem in the current HTM
There is a prediction value for each SDC segment
A two-step approach is applied to obtain the prediction values
  First, the normal intra-prediction procedure using neighboring reconstructed samples is invoked to get all the prediction samples in the coded block. DC, Planar and DMM-1 are possible prediction modes.
  Second, the average value of the prediction samples in a segment is calculated as the prediction value for this segment
Notes: For DC and Planar modes, there is only one segment in the coded block. For DMM-1 mode, there are two segments in the coded block, as the defined by DMM-1 mode. As a simplification, a sub-sampling method, which only uses one from each four prediction samples to get the average value, is adopted [3]. This method can reduce the addition operations in the averaging process significantly. The figure demonstrates two examples for the two-step SDC prediction approach, where there are one and two segments respectively.

## Slide 4: Proposed
  What we really want is the final SDC prediction value
    The prediction-averaging process is not necessary
  Direct SDC (dSDC) is proposed to simplify SDC prediction
    The prediction values are calculated from the neighbouring reconstructed samples directly

## Slide 5: Proposed
Initialize: neighbouring reconstructed samples are initialized as before the normal intra-prediction
For mode DMM-1.
  P0 and P1 are derived following the same method in DMM-1.
  P0 and P1 are treated as the final prediction values directly, without filling each prediction samples and calculating the average values
For mode DC.
  P=(A+B+1)>>1
For mode Planar.
  P= (X+Y+1) >> 1.

## Slide 6: Benefits
dSDC simplifies the derivation of SDC prediction values
  Remove the computational overhead of generating prediction samples and calculating the average value over these samples
  Generating a dSDC prediction value is even simpler than generating a normal prediction sample in mode DC or Planar
  The high bit-width of the averaging process is avoided in dSDC
    In SDC, as many as 64x64/4 prediction samples may be summed together, thus 18 bits are required by the accumulator for 8-bit samples

## Slide 7: Results
The proposed method can achieve 0.2% and 0.1% BD-rate gain on the synthesized view in CTC and AI test respectively
CTC
AI

## Slide 8: Conclusion
Proposed
  Remove the two-step method in SDC prediction value derivation
  Instead, the prediction values are calculated from the neighbouring reconstructed samples directly by a simple rule
Results
  Can save 0.2% and 0.1% BD-rate on the synthesized view in the common test condition and all-intra test condition respectively

## Slide 9: Thank you for your attention!