## Slide 1: D0156 CE1.h related: A high level syntax suggestion for stereo compatibility in 3D-HEVC
Kai Zhang, Jicheng An, Jian-Liang Lin, Shawmin Lei

## Slide 2: Overall Summary
Problem in the current HTM
  Depth dependent coding (DDC) tools ( BVSP, DoNBDV) are adopted
  The dependency between texture and depth pictures breaks the stereo compatibility in 3D-HEVC
Proposed
  Append syntax elements so that DDC tools can be switched on or off
  When DDC tools are turned off on texture pictures, the stereo compatibility in 3D-HEVC can be kept

## Slide 3: Problem in the current HTM
Depth dependent coding (DDC) tools like BVSP and DoNBDV are adopted to improve the coding efficiency
DDC tools introduces a dependency between texture and depth pictures, which breaks the stereo compatibility in 3D-HEVC
  In previous HTMs without DDC tools: texture pictures of dependent views can be encoded and decoded without depth pictures
  In HTM-6: texture pictures of dependent views cannot be encoded or decoded without depth pictures of the base view

## Slide 4: Problem in the current HTM
Even if depth pictures are available, DDC might be inefficient in the stereo application scenario
An example, where only V0 and V1 are desirable
  In HTM-5, only bitstreams of V0 and V1 need to be sent
  In HTM-6, bitstream of D0 as well as bitstreams of V0 and V1 need to be sent
  Although D0 can contribute to the coding efficiency improvement of V1, this may not justify the overhead bits of D0

## Slide 5: Proposed
A high level syntax suggestion for stereo compatibility in 3D-HEVC is proposed
  DDC tools such as BVSP and DoNBDV can be optional
  An encoder can decide whether to enable DDC depending on the application scenario
  These syntax elements can be in VPS or SPS
vps_extension2( ) { | Descriptor
… | 
if ( (layerId ! = 0) && !DepthLayerFlag[ layerId ] ) { | 
iv_mv_pred_flag[ layerId ] | u(1)
iv_res_pred_flag[ layerId ] | u(1)
depth_dependence_flag[ layerId ] | u(1)
if( depth_dependence_flag[ layerId ] != 0 ){ | 
vsp_compensation_flag [ layerId ] | u(1)
vsp_dv_refine_flag [ layerId ] | u(1)
} | 
} | 
if ( DepthLayerFlag[ layerId ] ) { | 
if ( (layerId ! = 0) | 
vsp_compensation_flag [ layerId ] | u(1)
… | 
} | 

## Slide 6: Conclusion
Proposed
  Append syntax elements so that DDC tools can be switched on or off
  When DDC tools are turned off on texture pictures, the stereo compatibility in 3D-HEVC can be kept

## Slide 7: Thank you for your attention!