## Slide 1: CE1.a related: Harmonization of inter-view and view synthesis prediction in 3D-AVC
S. Wenyi, D. Rusanovskyy, M. M. Hannuksela

## Slide 2: Inter-view and VSP in 3D-AVC v7.0
  Features of IVP/BVSP in 3D-ATM
    Generic MVP mode
    Direct/Skip mode
  Features of BVSP
    Complexity of 4x4 block size BVSP was argued
    8x8 block size BVSP was proposed
    Multi-directional VSP (reference index)

## Slide 3: Inter-view and VSP in 3D-AVC v7.0
  Co-existance of IVP/BVSP in generic MVP
    IVP and BVSP use different reference index in RPL
      refIdx of VSP is mapped to refIdx of IVP
      refIdx of VSP signal ommiting dMV coding (decoder side derivation)
    Different branches of direction separated prediction
      Redundancy between IVP and BVSP not utilized
    Harmonization between IVP and BVSP required
      Multi-directional IVP and VSP should be supported

## Slide 4: Inter-view and VSP in 3D-AVC v7.0
  VSP design
    VSP supports all motion partitions are supported
    4x4 block is elementary unit of VSP
    MV (disparity vector) is derived for each 4x4
    Increased 4x4 MCP usage

## Slide 5: Statistics on 4x4 MCP usage
  Percentage of 4x4 blocks to be utilized either in MCP or BVSP process, 3D-ATM v7.0 anchor.
 |  | left view |  |  | Right View |  | 
Sequence | RP | anchor P (%) | non- anchor P(%) | B slice (%) | anchor P (%) | non-anchor P(%) | B slice (%)
S01 | 0 | 7.19 | 5.97 | 1.16 | 5.53 | 4.14 | 1.42
 | 1 | 17.14 | 9.16 | 1.42 | 11.50 | 9.30 | 1.62
 | 2 | 24.40 | 13.50 | 2.07 | 25.37 | 14.33 | 2.60
 | 3 | 29.26 | 24.16 | 2.21 | 23.08 | 23.53 | 2.41
S02 | 0 | 29.31 | 10.61 | 2.82 | 24.00 | 7.41 | 2.45
 | 1 | 32.26 | 8.42 | 5.24 | 34.55 | 7.82 | 5.94
 | 2 | 36.80 | 16.97 | 9.47 | 36.69 | 14.09 | 7.61
 | 3 | 40.06 | 30.03 | 7.53 | 29.38 | 22.80 | 5.37
S03 | 0 | 44.17 | 46.88 | 9.82 | 46.71 | 48.06 | 9.31
 | 1 | 39.91 | 49.24 | 6.47 | 45.91 | 48.41 | 5.77
 | 2 | 36.59 | 57.72 | 5.88 | 40.78 | 48.46 | 5.03
 | 3 | 39.04 | 42.67 | 8.69 | 34.14 | 34.74 | 7.47
S04 | 0 | 68.77 | 74.36 | 49.99 | 67.22 | 68.00 | 49.56
 | 1 | 65.11 | 71.88 | 36.18 | 65.30 | 67.51 | 35.70
 | 2 | 63.94 | 71.22 | 29.77 | 61.99 | 64.66 | 24.64
 | 3 | 56.80 | 61.74 | 24.68 | 52.84 | 56.42 | 21.56
S05 | 0 | 4.50 | 4.39 | 3.84 | 5.39 | 7.02 | 4.69
 | 1 | 13.19 | 8.92 | 5.61 | 19.82 | 10.31 | 5.97
 | 2 | 13.76 | 15.06 | 5.80 | 19.43 | 15.75 | 5.96
 | 3 | 16.94 | 18.05 | 5.38 | 23.85 | 24.21 | 5.03
S06 | 0 | 3.47 | 4.05 | 2.29 | 6.02 | 4.39 | 2.62
 | 1 | 8.03 | 5.46 | 2.75 | 17.43 | 9.43 | 2.87
 | 2 | 13.36 | 10.96 | 2.47 | 27.80 | 18.73 | 2.35
 | 3 | 28.78 | 26.27 | 1.67 | 36.12 | 37.62 | 1.69
S08 | 0 | 2.32 | 1.18 | 0.65 | 1.75 | 0.91 | 0.46
 | 1 | 3.75 | 3.43 | 1.08 | 3.23 | 2.14 | 0.96
 | 2 | 8.72 | 7.29 | 1.14 | 7.21 | 4.04 | 1.20
 | 3 | 13.27 | 8.94 | 1.00 | 13.55 | 6.41 | 0.80
Average |  | 27.17 | 25.30 | 8.47 | 28.09 | 24.31 | 7.97
Maximal |  | 68.77 | 74.36 | 49.99 | 67.22 | 68.00 | 49.56

## Slide 6: BVSP with 8x8 block size
 | Texture Coding |  | Total (Coded PSNR) |  | Total (Synthesed PSNR) | 
 | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB
S01 | 0.00 | 0.00 | -0.01 | 0.00 | 0.08 | 0.00
S02 | 0.01 | 0.00 | 0.01 | 0.00 | 0.02 | 0.00
S03 | 0.48 | -0.02 | 0.46 | -0.02 | 0.41 | -0.01
S04 | -0.27 | 0.01 | -0.25 | 0.01 | -0.27 | 0.01
S05 | 0.22 | -0.01 | 0.15 | -0.01 | 0.29 | -0.01
S06 | 0.37 | -0.02 | 0.32 | -0.02 | 0.42 | -0.02
S08 | 0.17 | -0.01 | 0.15 | -0.01 | 0.23 | -0.01
Average | 0.14 | -0.01 | 0.12 | -0.01 | 0.17 | -0.01
  Coding performance of BVS 8x8

## Slide 7: Harmonized IVP/VSP
  MCP in IVP and VSP is performed identically
    Single reference index for IVP and VSP
    Signal type of prediction to the refIDx
      Type of prediction specifies MV signaling/derivation
      Single MV is derived for motion partition (4x4...16x16)

## Slide 8: Simulation results on Harmonized IVP/VSP
 | Texture Coding |  | Total (Coded PSNR) |  | Total (Synthesed PSNR) | 
 | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB
S01 | -0.12 | 0.00 | -0.11 | 0.00 | -0.08 | 0.00
S02 | -0.11 | 0.00 | -0.09 | 0.00 | -0.15 | 0.00
S03 | -0.09 | 0.00 | -0.08 | 0.00 | -0.10 | 0.00
S04 | -0.15 | 0.01 | -0.14 | 0.01 | -0.16 | 0.01
S05 | 0.00 | 0.00 | 0.02 | 0.00 | 0.00 | 0.00
S06 | 0.03 | 0.00 | 0.04 | 0.00 | -0.01 | 0.00
S08 | 0.02 | 0.00 | 0.03 | 0.00 | -0.03 | 0.00
Average | -0.06 | 0.00 | -0.04 | 0.00 | -0.08 | 0.00
  Coding performance of proposed method, ATM v7.0 anchor

## Slide 9: Changes to VSP_SKIP/DIRECT
  Variable VSP block size is supported through the MVP
  VSP_SKIP/DIRECT
    8x8 block is elementary unit of VSP

## Slide 10: Simulation results on Harmonized IVP/VSP
 | Texture Coding |  | Total (Coded PSNR) |  | Total (Synthesed PSNR) | 
 | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB
S01 | -0.04 | 0.00 | -0.04 | 0.00 | -0.06 | 0.00
S02 | -0.02 | 0.00 | 0.00 | 0.00 | -0.09 | 0.00
S03 | 0.38 | -0.01 | 0.36 | -0.01 | 0.30 | -0.01
S04 | -0.24 | 0.01 | -0.21 | 0.01 | -0.28 | 0.01
S05 | 0.12 | -0.01 | 0.10 | 0.00 | 0.16 | -0.01
S06 | 0.24 | -0.01 | 0.23 | -0.01 | 0.25 | -0.01
S08 | 0.02 | 0.00 | 0.03 | 0.00 | 0.01 | 0.00
Average | 0.06 | 0.00 | 0.07 | 0.00 | 0.04 | 0.00
  Coding performance of proposed method, ATM v7.0 anchor

## Slide 11: Statistics on 4x4 MCP usage in proposed method
  Percentage of 4x4 blocks to be utilized either in MCP or BVSP process, 3D-ATM v7.0 anchor.
 |  | left view |  |  | Right View |  | 
Sequence | RP | anchor P (%) | non- anchor P(%) | B slice (%) | anchor P (%) | non-anchor P(%) | B slice (%)
S01 | 0 | 0.04 | 0.03 | 0.00 | 0.07 | 0.08 | 0.00
 | 1 | 0.01 | 0.01 | 0.00 | 0.02 | 0.02 | 0.00
 | 2 | 0.00 | 0.00 | 0.00 | 0.01 | 0.00 | 0.00
 | 3 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
S02 | 0 | 0.01 | 0.01 | 0.00 | 0.01 | 0.01 | 0.00
 | 1 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
 | 2 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
 | 3 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
S03 | 0 | 0.08 | 0.05 | 0.00 | 0.06 | 0.05 | 0.00
 | 1 | 0.02 | 0.01 | 0.00 | 0.02 | 0.01 | 0.00
 | 2 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
 | 3 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
S04 | 0 | 0.23 | 0.20 | 0.02 | 0.24 | 0.15 | 0.02
 | 1 | 0.09 | 0.08 | 0.00 | 0.11 | 0.08 | 0.00
 | 2 | 0.02 | 0.02 | 0.00 | 0.02 | 0.01 | 0.00
 | 3 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
S05 | 0 | 0.28 | 0.25 | 0.01 | 0.28 | 0.27 | 0.01
 | 1 | 0.10 | 0.05 | 0.00 | 0.06 | 0.05 | 0.00
 | 2 | 0.00 | 0.01 | 0.00 | 0.01 | 0.00 | 0.00
 | 3 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
S06 | 0 | 0.02 | 0.02 | 0.00 | 0.03 | 0.04 | 0.00
 | 1 | 0.01 | 0.01 | 0.00 | 0.01 | 0.01 | 0.00
 | 2 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
 | 3 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
S08 | 0 | 0.06 | 0.06 | 0.00 | 0.07 | 0.09 | 0.00
 | 1 | 0.03 | 0.01 | 0.00 | 0.02 | 0.02 | 0.00
 | 2 | 0.01 | 0.00 | 0.00 | 0.01 | 0.00 | 0.00
 | 3 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
Average |  | 0.04 | 0.03 | 0.00 | 0.04 | 0.03 | 0.00
Maximal |  | 0.28 | 0.25 | 0.02 | 0.28 | 0.27 | 0.02

## Slide 12: Complexity estimates
 |  | left view |  |  | Right View |  | 
Proposed | RP | anchor P (%) | non- anchor P(%) | B slice (%) | anchor P (%) | non-anchor P(%) | B slice (%)
Average |  | 0.04 | 0.03 | 0.00 | 0.04 | 0.03 | 0.00
Maximal |  | 0.28 | 0.25 | 0.02 | 0.28 | 0.27 | 0.02
 |  | left view |  |  | Right View |  | 
Anchor | RP | anchor P (%) | non- anchor P(%) | B slice (%) | anchor P (%) | non-anchor P(%) | B slice (%)
Average |  | 27.17 | 25.30 | 8.47 | 28.09 | 24.31 | 7.97
Maximal |  | 68.77 | 74.36 | 49.99 | 67.22 | 68.00 | 49.56
 | Complexity estimate (ratio to anchor) |  | 
 | Encoder Time, % | Decoder Time, % | Rendering Time, %
S01 | 1.05 | 0.75 | N/A
S02 | 1.06 | 1.00 | N/A
S03 | 1.04 | 0.89 | N/A
S04 | 1.05 | 0.77 | N/A
S05 | 1.07 | 1.00 | N/A
S06 | 1.06 | 1.11 | N/A
S08 | 1.06 | 0.88 | N/A
Average | 1.05 | 0.91 | N/A

## Slide 13: Summary
  Harmonized IVP/VSP is proposed
    Single reference index for IVP and VSP
    Signal type of prediction to the refIDx
      Type of prediction specifies MV signaling/deriving
      Single MV is derived for motion partition (4x4...16x16)
    Gain about 0.1% on average
    Variable block size VSP (identical to MCP)
  8x8 blocks in VSP_SKIP/DIRECT
    0.04% of dBR on total MVD (gain 0.28% for GT_Fly)
    6-9% of decoding time reduction on average
    Ratio 4x4 block reduced to 4-6% on aver. (25 worse case)

## Slide 14: Thank you!