## Slide 1: 3D-CE6.h related: Differential coding method for DLT in 3D-HEVC (JCT3V-D0172)
Ming LI, Ping WU, Hongwei LI
Guoqiang SHANG, Yutang XIE

## Slide 2: Summary
As tested on HTM6.0 (CTC), DLT related syntax elements take about 66% of the coding bits of SPS.
To reduce the coding bits of DLT, differential coding is proposed to perform lossless compression on the DLT elements.
Compared with the HTM6.0 CTC anchors, using the proposed method, the coding bits for DLT are reduced by about 75% (taking an average of 32% in the SPS coding bits), while the bits for SPS are saved by 49%.
In addition, with the proposed method, the coding performance is very slightly improved by 0.02% and 0.01% on average for 1280x768 and 1920x1088 sequences, respectively, under CTC configurations. And no loss was observed in all intra results.

## Slide 3: Introduction
In HTM6.0, DLT for every view is constructed by pre-analyzing an intra period of original depth pictures associated with given layer_id. The syntax structure in HTM6.0 for DLT is given in the table below.
seq_parameter_set_rbsp( ) { | Descriptor
…… | 
if ( DepthFlag ) { | 
dlt_flag | u(1)
if (dlt_flag) { | 
num_depth_values_in_dlt | ue(v)
for ( i = 0; i < num_depth_values_in_dlt ; i++ ) { | 
dlt_depth_value[ i ] | ue(v)
} | 
} | 
} | 
…… | 
} | 

## Slide 4: Motivation
As tested on HTM6.0 (CTC), DLT related syntax elements take about 66% of the coding bits of SPS.
Sequence | View | DLT bits (D0) | SPS bits (S0) | D0/S0 (%)
Balloon | 3 | 556 | 844 | 65.88
 | 1 | 642 | 936 | 68.59
 | 5 | 618 | 914 | 67.61
Kendo | 3 | 486 | 774 | 62.79
 | 1 | 638 | 932 | 68.45
 | 5 | 650 | 946 | 68.71
Newspaper | 4 | 607 | 895 | 67.82
 | 2 | 622 | 916 | 67.90
 | 6 | 697 | 993 | 70.19
Poznan_hall2 | 6 | 421 | 711 | 59.21
 | 7 | 381 | 677 | 56.28
 | 5 | 382 | 680 | 56.18
Average |  | 558.33 | 851.50 | 65.57

## Slide 5: Proposed syntax
To reduce the coding bits for DLT, a differential coding method is proposed. The modified syntax on HTM6.0 is as below.
seq_parameter_set_rbsp( ) { | Descriptor
…… | 
if (dlt_flag) { | 
num_depth_values_in_dlt | ue(v)
dlt_depth_value[0] | ue(v)
for ( i = 0; i < num_depth_values_in_dlt ; i++ ) { | 
dlt_depth_diff_minus1_less_than_4_flag[ i ] | u(1)
if (dlt_depth_diff_minus1_less_than_4_flag[ i ]) | 
dlt_depth_diff_minus1[ i ] // shall not be negative | u(2)
else | 
dlt_depth_diff_minus1_minus4[ i ] // shall not be negative | ue(v)
} | 
…… | 
} | 

## Slide 6: Proposed semantics
num_depth_values_in_dlt specifies the number of elements in the depth lookup table for depth view components.
dlt_depth_value[ 0 ] specifies the 0-th entry in the depth lookup table for depth view components.
dlt_depth_diff_minus1_less_than_4_flag[ i ] equal to 1 specifies that the value of dlt_depth_diff_minus1[ i ] is presented. Otherwise, dlt_depth_diff_minus1_less_than_4_flag[ i ] equal to 0 specifies that the value of dlt_depth_diff_minus1_minus4[ i ] is presented.
dlt_depth_diff_minus1[ i ] specifies the i-th entry for deriving the i-th entry in depth lookup table for depth view components. The value of dlt_depth_diff_value_minus1[i] shall not be negative. The value of the i-th entry in depth lookup table is derived as dlt_depth_value[i] = dlt_depth_value[i – 1] + dlt_depth_diff_minus1[i] + 1, for i from 1 to num_depth_values_in_dlt – 1. NOTE: dlt_depth_value[0] is the smallest depth value in depth lookup table.
dlt_depth_diff_minus1_minus4[ i ] specifies the i-th entry for deriving the i-th entry in depth lookup table for depth view component. The value of dlt_depth_diff_value_minus1_minus4[ i ] shall not be negative. The value of the i-th entry in depth lookup table is derived as dlt_depth_value[ i ] = dlt_depth_value[ i – 1 ] + dlt_depth_diff_value_minus1_minus4[ i ] + 1 + 4, for i from 1 to num_depth_values_in_dlt – 1.

## Slide 7: Proposed encoding
According to the proposed syntax and semantics, DLT is encoded in the following steps:
  Step 1: Presenting the depth values into DLT array (e.g. dlt_depth_value[ ]) in ascending order.
  Step 2: Encoding the number of depth values in DLT array and the first element dlt_depth_value[0].
  Step 3: Calculating diff_minus1 = dlt_depth_value[i] – dlt_depth_value[i – 1] – 1.
  Step 4: If diff < 4 holds, encoding ‘1’ using u(1) and diff_minus1 value using u(2); otherwise, encoding ‘0’ using u(1) and (diff_minus1 – 4) value using ue(v).

## Slide 8: Experimental results
HTM6.0, CTC. Comparisons between HTM6.0 anchors and proposed on DLT and SPS coding bits. No performance loss was observed.
Sequence | View | HTM6.0 Anchor |  |  | HTM6.0 + proposed |  |  | Comparisons | 
 |  | DLT bits (D0) | SPS bits (S0) | D0/S0 (%) | DLT bits (D1) | SPS bits (S1) | D1/S1 (%) | D1/D0 (%) | S1/S0 (%)
Balloon | 3 | 556 | 844 | 65.88 | 121 | 409 | 29.58 | 21.76 | 48.46
 | 1 | 642 | 936 | 68.59 | 141 | 435 | 32.41 | 21.96 | 46.47
 | 5 | 618 | 914 | 67.61 | 141 | 437 | 32.27 | 22.82 | 47.81
Kendo | 3 | 486 | 774 | 62.79 | 109 | 397 | 27.46 | 22.43 | 51.29
 | 1 | 638 | 932 | 68.45 | 139 | 433 | 32.10 | 21.79 | 46.46
 | 5 | 650 | 946 | 68.71 | 141 | 437 | 32.27 | 21.69 | 46.19
News- paper | 4 | 607 | 895 | 67.82 | 157 | 445 | 35.28 | 25.86 | 49.72
 | 2 | 622 | 916 | 67.90 | 160 | 454 | 35.24 | 25.72 | 49.56
 | 6 | 697 | 993 | 70.19 | 175 | 471 | 37.15 | 25.11 | 47.43
Poznan _hall2 | 6 | 421 | 711 | 59.21 | 127 | 417 | 30.46 | 30.17 | 58.65
 | 7 | 381 | 677 | 56.28 | 119 | 415 | 28.67 | 31.23 | 61.30
 | 5 | 382 | 680 | 56.18 | 118 | 416 | 28.37 | 30.89 | 61.18
Average |  | 558.33 | 851.50 | 65.57 | 137.33 | 430.50 | 31.90 | 24.60 | 50.56

## Slide 9
HTM6.0, CTC. Performance comparisons between HTM6.0 anchor and proposed (3 view test case)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | -0.02% | -0.02% | 86.5% | 113.7% | 93.5%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | -0.02% | -0.02% | 113.9% | 105.3% | 101.7%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | -0.02% | -0.02% | 92.5% | 95.1% | 99.8%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.00% | 0.00% | 102.2% | 97.0% | 88.2%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | -0.03% | -0.03% | 94.3% | 106.5% | 93.3%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.00% | 0.00% | 102.0% | 98.1% | 89.7%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.00% | 0.00% | 94.0% | 97.9% | 87.4%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | -0.02% | -0.02% | 97.6% | 104.7% | 98.3%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | -0.01% | -0.01% | 98.1% | 99.9% | 89.7%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.00 | 0.00 | 97.9% | 101.9% | 93.4%

## Slide 10
HTM6.0, CTC. Performance comparisons between HTM6.0 anchor and proposed (2 view test case)
 | video 0 | video 1 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Balloons | 0.0% | 0.0% | 0.0% | -0.02% | -0.02%
Kendo | 0.0% | 0.0% | 0.0% | -0.02% | -0.02%
Newspaper_CC | 0.0% | 0.0% | 0.0% | -0.02% | -0.02%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.00% | 0.00%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | -0.02% | -0.02%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.00% | 0.00%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.00% | 0.00%
1024x768 | 0.0% | 0.0% | 0.0% | -0.02% | -0.02%
1920x1088 | 0.0% | 0.0% | 0.0% | -0.01% | -0.01%
average | 0.0% | 0.0% | 0.0% | -0.01% | -0.01%

## Slide 11
HTM6.0, All Intra. Performance comparisons between HTM6.0 anchor and proposed (3 view test case)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.00% | 0.00% | 90.5% | 95.3% | 96.7%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.00% | 0.00% | 97.7% | 116.8% | 89.3%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.00% | 0.00% | 93.5% | 103.0% | 113.2%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.00% | 0.00% | 113.4% | 100.0% | 87.0%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.00% | 0.00% | 106.3% | 104.2% | 97.4%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.00% | 0.00% | 87.6% | 97.3% | 100.0%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.00% | 0.00% | 129.0% | 105.2% | 99.9%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.00% | 0.00% | 93.9% | 105.0% | 99.7%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.00% | 0.00% | 109.1% | 101.7% | 96.1%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.00% | 0.00% | 102.6% | 103.1% | 97.7%

## Slide 12
HTM6.0, All Intra. Performance comparisons between HTM6.0 anchor and proposed (2 view test case)
 | video 0 | video 1 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Balloons | 0.0% | 0.0% | 0.0% | 0.00% | 0.00%
Kendo | 0.0% | 0.0% | 0.0% | 0.00% | 0.00%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.00% | 0.00%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.00% | 0.00%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.00% | 0.00%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.00% | 0.00%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.00% | 0.00%
1024x768 | 0.0% | 0.0% | 0.0% | 0.00% | 0.00%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.00% | 0.00%
average | 0.0% | 0.0% | 0.0% | 0.00% | 0.00%

## Slide 13: Modified WD
The proposed differential coding method on DLT is integrated into VPS extension syntax in WD.
vps_extension2( ) { | Descriptor
...... | 
dlt_flag[ layerId ] | u(1)
if( dlt_flag[ layerId ] ) { | 
num_depth_values_in_dlt[ layerId ] | ue(v)
dlt_depth_value[ layerId ][ 0 ] | ue(v)
for ( j = 0; j < num_depth_values_in_dlt[ layerId ] ; j++) { | 
dlt_depth_value[ layerId ][ j ] | ue(v)
dlt_depth_diff_minus1_less_than_4_flag[ layerId ][ j ] | u(1)
if (dlt_depth_diff_minus1_less_than_4_flag[ layerId ][ j ]) | 
dlt_depth_diff_minus1[ layerId ][ j ] // shall not be negative | u(2)
else | 
dlt_depth_diff_minus1_minus4[ layerId ][ j ] // shall not be negative | ue(v)
} | 
} | 
...... | 
} | 

## Slide 14
The semantics of the proposed syntax elements are listed below.
dlt_depth_value[ layerId ][ 0 ] specifies the 0-th entry in the depth lookup table for depth view components with layer_id equal to layerId.
dlt_depth_diff_minus1_less_than_4_flag[ layerId ][ j ] equal to 1 specifies that the value of dlt_depth_diff_minus1[ layerId ][ j ] is presented. Otherwise, dlt_depth_diff_minus1_less_than_4_flag[ layerId ][ j ] equal to 0 specifies that the value of dlt_depth_diff_minus1_minus4[ layerId ][ j ] is presented.
dlt_depth_diff_minus1[ layerId ][ j ] specifies the j-th entry for deriving the j-th entry in depth lookup table for depth view components with layer_id equal to layerId. The value of dlt_depth_diff_value_minus1[ layerId ][ j ] shall not be negative. The value of the j-th entry in depth lookup table is derived as dlt_depth_value[ layerId ][ j ] = dlt_depth_value[ layerId ][ j – 1] + dlt_depth_diff_minus1[ layerId ][ j ] + 1, for j from 1 to num_depth_values_in_dlt[ layerId ] – 1. NOTE: dlt_depth_value[layerId][0] is the smallest depth value in depth lookup table for depth view components with layer_id equal to layerId.
dlt_depth_diff_minus1_minus4[ layerId ][ j ] specifies the j-th entry for deriving the j-th entry in depth lookup table for depth view components with layer_id equal to layerId. The value of dlt_depth_diff_minus1_minus4[ layerId ][ j ] shall not be negative. The value of the j-th entry in depth lookup table is derived as dlt_depth_value[ layerId ][ j ] = dlt_depth_value[ layerId ][ j – 1 ] + dlt_depth_diff_minus1_minus4[ layerId ][ j ] + 1 + 4, for j from 1 to num_depth_values_in_dlt[ layerId ] – 1.

## Slide 15: Conclusions
A differential coding method for DLT is proposed.
Proposed method saves the DLT coding bits by an average of 75%, and SPS coding bits by 49%.
Additionally, the CTC test and all intra results show that the proposed method provides almost the same coding performance as that of HTM6.0 anchor.
Therefore, it is recommended to adopt this method into 3D-HEVC.

## Slide 17: Analyses on the worst case
The coding bits for the differential values “diff” are:
  1 <= diff <= 4, 3 bits
  diff = 5, 2 bits
  diff = 6 or 7, 4 bits
  8 <= diff <= 11, 6 bits
  12 <= diff <= 19, 8 bits
  20 <= diff <= xxx, 10 bits
  ......
Let x, y, z, u and v be the number of differential values equal to 1, 5, 6, 8 and 12, respectively. Then the max bits for coding the differential values can be expressed as:
max cost = 3x + 2y + 4z + 6u + 8v
s.t. x + 5y + 6z + 8u + 12v <= 255, and x + y + z + u + v <= 128

## Slide 18
The constrained optimization problem can be solved by scanning all the possible combinations of (x, y, z, u, v).
One case of (x, y, z, u, v) = (115, 0, 0, 4, 9) returns the maximum number of coding bits of 441.
For this case, the number of elements in DLT is 128, which consumes 15 bits by ue(v).
When the range of depth is [0, 255], the maximum number of bits for dlt_depth_value[0] is 16 by ue(v) (i.e. depth value equal to 255). For this example case, dlt_depth_value[0] shall be below 127, which costs less than 15 bits.
Moreover, one bit is for dlt_flag.
Therefore, from this analyses, the proposed method generates 441 + 15 + 16 + 1 = 473 bits for the worst case.

## Slide 19
Another case for analyzing the worst case is to remove the differential value equal to 5 and add the value equal to 20.
Let x, y, z, u and v be the number of differential values equal to 1, 6, 8, 12, and 20, respectively. Then the max bits for coding the differential values can be expressed as:
max cost = 3x + 4y + 6z + 8u + 10v
s.t. x + 6y + 8z + 12u + 20v <= 255, and x + y + z + u + v <=128
Following similar approach, one case of (x, y, z, u, v) = (115, 0, 4, 9, 0) returns the maximum number of coding bits of 441, which is the same result as the previous one.
Therefore, from this analyses, the proposed method generates 441 + 15 + 16 + 1 = 473 bits for the worst case.