## Slide 1
Page <number>
JCT3V-D0173: CE6.h related Removal of division operation for DMM and SDC
Xiaozhen Zheng
Notes: 26/7/30
<number>

## Slide 2: Summary
Page <number>
Motivation
  Remove division operations for DMM and SDC
Experimental results
  Solution1: 0.0% / -0.1% for CTC, 0.0% / 0.0% for All-intra on video / synthesized view
  Solution2: 0.0% / 0.1% for CTC, 0.0% / 0.0% for All-intra on video / synthesized view
Cross-check: JCT3V-D0204 by Qualcomm

## Slide 3: Division operation in DMM and SDC
DMM might partition a square block into two non-rectangular partitions
  Problem: The number of samples can’t be represented as 2N, which means the division for DC calculation can’t be simply achieved by the right shift operation
  The values of numerator and denominator are changed in same time that cause the size of look-up table (LUT) for the storage of division results is extremely large
Page <number>
 | Numerator (summary of samples value) | Denominator (number of samples) | LUT size
DMM | 213 | 25 | 218
SDC | 218 | 210 | 228

## Slide 4: General concept for division free
Same concept as motion vector scaling in HEVC
  Separate the calculation of denominator and numerator into two steps
tx = ( 16384 + ( Abs( td ) >> 1 ) ) / td
distScaleFactor = Clip3( −4096, 4095, ( tb * tx + 32 ) >> 6 )
  The LUT size is much smaller by using the separation calculation
Page <number>

## Slide 5: Proposed solution1
Same as the method for motion vector scaling
  Step 1: calculate the reciprocal of denominator
  iX = (0x1000 + (numNeigh >> 1)) / numNeigh (DMM)
  iX = (0x10000 + numPred>>1) / numPred (SDC)
  Step 2: Calculate DC value
  predDcVal = Clip(0, 255, ( sumNeigh x iX + 0x800 ) >> 12) (DMM)
  dcPred[p] = Clip (0, 255, (iX x sumPred + 0x8000) >> 16) (SDC)
  The LUT size is significantly reduced
    DMM: From 218 to 25
    SDC: 228 to 210
Page <number>

## Slide 6: Proposed solution2
Use the same LUT of motion vector scaling for DMM and SDC
  DMM: Same steps as motion vector scaling
    STEP1: iX = (0x4000 + (numNeigh >> 1)) / numNeigh
    STEP2: predDcVal =Clip(0, 255, ( sumNeigh x iX + 0x2000 ) >> 14)
  SDC: A pre-right shift is added to the denominator whose value is larger than 127
    STEP1: iX = (0x4000 + numPred>>1) / numPred (0<numPred<128)
    iX = (0x4000 + numPred>>4) / (numPred>>3) (numPred>=128)
    STEP2:
    dcPred[p] = Clip (0, 255, (iX x sumPred + 0x2000) >> 14) (0<numPred<128)
    dcPred[p] = Clip (0, 255, (iX x sumPred + 0x10000) >> 17) (numPred>=128)
  Motion vector scaling’s LUT can be totally used at DMM and SDC
Page <number>

## Slide 7: Experimental results
Page <number>
Solution1 (CTC)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | -0.1% | 100.0% | 103.6% | 99.8%
Kendo | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 100.0% | 108.5% | 99.7%
Newspaper_CC | 0.0% | -0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 100.1% | 106.3% | 101.2%
GT_Fly | 0.0% | 0.1% | 0.2% | 0.0% | 0.0% | -0.1% | 100.1% | 96.8% | 100.7%
Poznan_Hall2 | 0.0% | -0.4% | -0.6% | -0.2% | -0.3% | -0.2% | 99.9% | 105.6% | 104.9%
Poznan_Street | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | -0.1% | 100.0% | 98.2% | 103.1%
Undo_Dancer | 0.0% | -0.2% | -0.2% | 0.0% | 0.0% | -0.2% | 99.8% | 98.0% | 102.4%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.0% | 106.1% | 100.2%
1920x1088 | 0.0% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1% | 100.0% | 99.6% | 102.8%
average | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1% | 100.0% | 102.4% | 101.7%

## Slide 8: Experimental results (2)
Page <number>
Solution1 (AI)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.97% | 102.72% | 99.16%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.92% | 103.10% | 100.90%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.05% | 103.47% | 100.16%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | 99.54% | 99.96% | 99.38%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.37% | 102.29% | 100.72%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 99.51% | 100.37% | 98.89%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.29% | 100.63% | 98.25%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.98% | 103.10% | 100.07%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.43% | 100.81% | 99.31%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.66% | 101.79% | 99.64%

## Slide 9: Experimental results (3)
Page <number>
Solution2 (CTC)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | -0.2% | -0.1% | 0.0% | -0.1% | 100.5% | 100.3% | 101.0%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.1% | 96.8% | 99.9%
Newspaper_CC | 0.0% | -0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 100.0% | 114.4% | 100.4%
GT_Fly | 0.0% | -0.1% | -0.2% | 0.0% | -0.1% | -0.1% | 100.6% | 95.2% | 101.0%
Poznan_Hall2 | 0.0% | -0.2% | 0.1% | 0.0% | -0.1% | -0.1% | 100.5% | 101.5% | 104.4%
Poznan_Street | 0.0% | 0.0% | -0.1% | 0.0% | -0.1% | -0.1% | 100.0% | 100.3% | 101.2%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 100.1% | 97.1% | 99.4%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.2% | 103.9% | 100.4%
1920x1088 | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 100.3% | 98.5% | 101.5%
average | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 100.2% | 100.8% | 101.0%

## Slide 10: Experimental results (4)
Page <number>
Solution2 (AI)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.07% | 108.92% | 100.36%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.13% | 103.63% | 103.28%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.75% | 100.90% | 100.95%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.2% | 100.00% | 100.38% | 99.11%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.76% | 100.60% | 100.45%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 99.69% | 98.98% | 99.62%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.42% | 103.36% | 99.64%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.32% | 104.49% | 101.53%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 99.72% | 100.83% | 99.71%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.97% | 102.40% | 100.49%

## Slide 11: Conclusions
Page <number>
Two proposed solutions can replace division operation for DMM and SDC with LUT with considerable size
Both solutions don’t have impact on coding performance
Suggest adopting the proposed solutions (solution2 is preferable)

## Slide 12
Page <number>
Thank you!
www.hisilicon.com