## Slide 1
Page <number>
JCT3V-D0174: CE6.h related: Extension of reference samples sub-sampling to all block-sizes in DMM and SDC
Xiaozhen Zheng
Notes: 26/7/30
<number>

## Slide 2: Summary
Page <number>
Motivation
  Extend reference sub-sampling to all of block-sizes in DMM and SDC to further reduce computing complexity
Experimental results
  Sub-sampling for SDC: 0.0% / 0.0% for CTC, 0.0% / 0.0% for All-intra on video / synthesized view
  Sub-sampling for SDC and DMM: 0.0% / -0.1% for CTC, 0.0% / 0.0% for All-intra on video / synthesized view
Cross-check: JCT3V-D0283 by Intel

## Slide 3: Reference sub-sampling in current and proposed designs
Page <number>
Current reference sub-sampling design
  2:1 sub-sampling is used at 32x32 block in DMM, 32x32 and 64x64 blocks in SDC
Proposed reference sub-sampling design
  Apply 2:1 sub-sampling to all of block-sizes in DMM and SDC
Encoder optimization
  DC value for the original samples is calculated without sub-sampling

## Slide 4: Experimental results
Page <number>
Reference sample sub-sampling for SDC only (CTC)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 100.2% | 98.7% | 103.4%
Kendo | 0.0% | -0.1% | 0.1% | 0.0% | 0.0% | 0.1% | 100.2% | 97.2% | 102.3%
Newspaper_CC | 0.0% | -0.1% | 0.1% | 0.0% | 0.0% | -0.1% | 99.2% | 102.4% | 95.9%
GT_Fly | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 99.4% | 88.1% | 95.3%
Poznan_Hall2 | 0.0% | 0.2% | -0.2% | 0.0% | 0.0% | 0.0% | 100.2% | 98.1% | 98.2%
Poznan_Street | 0.0% | 0.3% | 0.0% | 0.0% | 0.0% | 0.0% | 100.0% | 110.3% | 107.5%
Undo_Dancer | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 99.8% | 94.5% | 95.6%
1024x768 | 0.0% | -0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 99.9% | 99.4% | 100.5%
1920x1088 | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 99.8% | 97.8% | 99.2%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.9% | 98.5% | 99.7%

## Slide 5: Experimental results (2)
Page <number>
Reference sample sub-sampling for SDC only (AI)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.7% | 100.2% | 99.3%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.8% | 100.1% | 99.3%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.4% | 97.4% | 100.2%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.2% | 98.7% | 99.0%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.9% | 102.1% | 100.5%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.9% | 103.1% | 99.3%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.6% | 104.4% | 99.7%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.0% | 99.2% | 99.6%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.9% | 102.1% | 99.6%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.9% | 100.9% | 99.6%

## Slide 6: Experimental results (3)
Page <number>
Reference sample sub-sampling for SDC and DMM (CTC)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -0.1% | 0.1% | 0.0% | 0.0% | -0.1% | 100.2% | 98.8% | 102.0%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 100.2% | 96.2% | 101.6%
Newspaper_CC | 0.0% | -0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 100.4% | 96.5% | 94.9%
GT_Fly | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | 0.1% | 99.9% | 89.8% | 97.1%
Poznan_Hall2 | 0.0% | -0.6% | 0.1% | -0.1% | -0.1% | -0.1% | 100.4% | 97.3% | 97.9%
Poznan_Street | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 100.0% | 108.3% | 111.0%
Undo_Dancer | 0.0% | -0.2% | -0.1% | 0.0% | 0.0% | -0.5% | 99.8% | 94.8% | 97.3%
1024x768 | 0.0% | -0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 100.3% | 97.2% | 99.5%
1920x1088 | 0.0% | -0.2% | 0.0% | 0.0% | 0.0% | -0.1% | 100.0% | 97.5% | 100.8%
average | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | -0.1% | 100.1% | 97.4% | 100.3%

## Slide 7: Experimental results (4)
Page <number>
Reference sample sub-sampling for SDC and DMM (AI)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.0% | 100.0% | 99.0%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.1% | 97.6% | 99.4%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 100.7% | 101.4% | 100.2%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.5% | 98.3% | 99.4%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.2% | 97.5% | 100.6%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.3% | 99.0% | 97.6%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 99.9% | 98.2% | 99.2%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.3% | 99.7% | 99.5%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.2% | 98.2% | 99.2%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.2% | 98.9% | 99.3%

## Slide 8: Experimental results (5)
Page <number>
Reference sample sub-sampling for SDC and DMM without encoder optimization (CTC)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 100.0% | 99.5% | 101.2%
Kendo | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.1% | 100.0% | 101.9% | 99.5%
Newspaper_CC | 0.0% | -0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 100.0% | 116.2% | 98.8%
GT_Fly | 0.0% | 0.2% | 0.2% | 0.0% | 0.0% | 0.0% | 100.7% | 96.2% | 101.1%
Poznan_Hall2 | 0.0% | -0.4% | -0.7% | -0.2% | -0.2% | -0.3% | 101.0% | 98.2% | 101.4%
Poznan_Street | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | 0.1% | 99.9% | 101.6% | 101.7%
Undo_Dancer | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.6% | 99.9% | 98.7% | 99.9%
1024x768 | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 100.0% | 105.9% | 99.9%
1920x1088 | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | -0.2% | 100.4% | 98.7% | 101.0%
average | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1% | 100.2% | 101.8% | 100.5%

## Slide 9: Experimental results (6)
Page <number>
Reference sample sub-sampling for SDC and DMM without encoder optimization (AI)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 100.0% | 100.1% | 96.7%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 100.0% | 99.1% | 99.2%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.2% | 102.2% | 99.7% | 101.0%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.3% | 97.1% | 99.9%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 100.3% | 99.1% | 100.2%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 100.3% | 99.2% | 97.5%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 100.0% | 98.9% | 99.1%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 100.7% | 99.6% | 99.0%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.2% | 98.6% | 99.2%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 100.4% | 99.0% | 99.1%

## Slide 10: Conclusions
Page <number>
Propose to use reference sub-sampling to all of block-sizes in DMM and SDC
The computing complexity for DMM and SDC can be further reduced
Various tests show that the proposed sub-sampling method does not have the impact on the coding performance
Suggest adopting the proposed sub-sampling method

## Slide 11
Page <number>
Thank you!
www.hisilicon.com