## Slide 1: Fast Depth Modeling Mode Selection for Depth Intra Coding
Zhouye Gu (Santa Clara University)
Jianhua Zheng (HiSilicon)
Nam Ling (Santa Clara University)
Philipp Zhang (HiSilicon)
JCT3V-D0175

## Slide 2: Introduction
Intra depth frame compression includes more intra modes to search compared with intra texture frame compression.
Additional conditions are design to skip Full-RD search of depth intra prediction mode.
implemented on HTM6.0:
23.5% encoding time saving for All Intra case without bitrate loss
2.3% encoding time saving under CTC with 0.1% bitrate gain at synthesized views
Thanks Intel for crosscheck
Thanks MERL for code crosscheck

## Slide 3: Introduction
In 3D-HEVC intra depth coding, new intra depth prediction mode (Depth Modeling Modes and Regional Boundary Chain mode) are added to the Full-RD cost calculation list after the intra prediction mode selected by fast intra mode decision
uiRdModeList[0]
uiRdModeList[1]
…
uiRdModeList[m]
uiRdModeList[m+1]
uiRdModeList[m+2]
…
uiRdModeList[m+n]
Intra prediction modes
New Intra depth prediction modes
Full RD cost Calculation

## Slide 4: Problem
However, new intra depth prediction modes are designed to preserve the edge or sharp transition of a block, while most of the blocks in depth frame are flat or smooth. Those flat or smooth block are rarely selected as the new depth intra modes.
In current design, full RD cost calculation is applied to the new depth intra modes. However, after full RD-cost calculation, only a small number of best modes are new intra depth prediction mode. (e.g. 3.4%, Kendo , QP = 25)
It is make sense to have a fast approach for the depth intra modes instead of full RD cost calculation to decide the best mode.
(a) Kendo (b) PoznanHall2
Example of Depth frames

## Slide 5: Our Proposal
Condition 1: skip full-RD cost calculation of new intra depth mode when the first mode in the full-RD calculation list is planar (uiRdModeList[0] == 0)
This is because when the first mode in the full-RD calculation list is planar, the block is very likely to be smooth and rarely select new intra depth mode as best mode.
uiRdModeList[0]
uiRdModeList[1]
…
uiRdModeList[m]
uiRdModeList[m+1]
uiRdModeList[m+2]
…
uiRdModeList[m+n]
Full RD cost Calculation
==0
Intra prediction modes
New Intra depth prediction modes

## Slide 6: Our Proposal
threshold = max((CU_depth_QP*205)>>10)-4,1) (1)
varThreshold = threshold*threshold-3*(threshold-1) (2)
Condition 2: add new intra depth mode (DMMs and Region Boundary Chain mode) to full-RD cost calculation list if the variance of block is higher than a threshold
This is because the blocks selecting new intra depth modes as best mode are usually edge blocks which have high block variance
Combining condition 1 and 2, the additional condition required to add new intra depth mode to full-RD cost calculations is:
(FullRDList[0] != planar) || (CU variance >= varThreshold) (3)

## Slide 7: Miss Selection Rate of The Proposal
 | QP = 25_34 | QP = 30_39 | QP = 35_42 | QP = 40_45
GTfly | 0.08% | 0.03% | 0.01% | 0.01%
Kendo | 0.03% | 0.02% | 0.01% | 0.00%
Newspaper | 0.18% | 0.09% | 0.03% | 0.00%
PoznanHall | 0.03% | 0.03% | 0.01% | 0.00%
Poznanstreet | 0.20% | 0.06% | 0.02% | 0.00%
Balloon | 0.05% | 0.03% | 0.01% | 0.00%
UndoDancer | 0.10% | 0.04% | 0.02% | 0.01%
Average | 0.10% | 0.04% | 0.02% | 0.00%
Miss Selection Rate: when our algorithm decides to skip new intra depth mode full-RD search for a certain block, the probability of that block choosing new intra depth mode as best prediction mode.

## Slide 8
All Intra test result
Random Access (CTC) test result

## Slide 9: Full RD Search Cycle Reduction (Reduction of Candidate Modes)
 | QP = 25_34 | QP = 30_39 | QP = 35_42 | QP = 40_45 | Sequence Average
GTfly | 30.94% | 25.28% | 27.09% | 29.43% | 28.18%
Kendo | 16.14% | 15.67% | 18.11% | 23.62% | 18.38%
Newspaper | 27.02% | 23.60% | 22.64% | 29.93% | 25.79%
PoznanHall | 27.60% | 24.21% | 28.49% | 31.50% | 27.95%
Poznanstreet | 25.99% | 27.16% | 23.45% | 26.47% | 25.76%
Balloon | 19.01% | 19.13% | 21.87% | 26.71% | 21.68%
UndoDancer | 29.46% | 28.32% | 27.42% | 28.37% | 28.39%
Average | 25.16% | 23.33% | 24.15% | 28.00 % | 25.16%
28.2% Encoding Time Saving Reported in Crosscheck Report JCT3V-D0284

## Slide 10: Summary
A fast intra prediction mode selection is designed.
23.5% encoding time saving is achieved without any coding loss for all intra case.
2.3% encoding time saving is achieved under CTC with 0.1% bitrate gain at synthesized views
Compactable with other algorithms designed to improve specific new intra depth mode performance.
Suggest to include as a software tool to speed up intra coding

## Slide 11: Thank you!