## Slide 1: 3D-HEVC: Report on Asymmetric Resolution Coding in 3D-HEVC
Shiori Sugimoto
Shinya Shimizu
Hideaki Kimata
JCT3V-D0216

## Slide 2: Motivation
System requirement
  Data volume is required to be 4x of single view video for keeping throughput of the decoder
An approach that one view in a stereoscopic pair can be coded with lower quality while the perceptual quality degradation for the stereoscopic display is not noticeable has proposed

## Slide 3: Affected tools
Texture coding tools
  Inter-view prediction
  IVRP
  VSP
  DoNBDV
  Multiview motion vector prediction
Depth coding tools
  VSO

## Slide 4: Modification : Adjustment of Inter-component correspondence
#1 : Resampling of inter-view reference picture (Inter-view prediction, IVRP)
#2 : Scaling a derived motion/disparity vector (all)

## Slide 5: Modification : VSO reference
  Reference synthesized view can be generated based on what kind of data
  If encoder has full resolution data, both of the original data and the upsampled reduced resolution data are acceptable for VSO reference

## Slide 6: Experimental condition
Input data is full resolution , downsampled before slice encoding and upsampled after slice decoding
Both resampling on the outside of coding loop are excluded in coding times
Test for two type, reduce only horizontal resolution (half), horizontal and vertical resolution (quarter)

## Slide 7: Experimental condition
  VSO reference is the synthesized view based on the original full resolution
Resampling filters
 | target | Filter
Downsampling | Input data | 12 tap sinc filter /Nearest Neighbor
 | inter-view reference picture | 12 tap sinc filter /Nearest Neighbor
Upsampling | Reconstructed picture on VSO | 6 tap lanczos filter /Nearest Neighbor
 | Output | 6 tap lanczos filter /Nearest Neighbor

## Slide 8: Experimental Results
 | video / video | video / total | synth / total | enc time | dec time
Balloons | 11.0% | 12.8% | 2.5% | 67.3% | 155.7%
Kendo | 8.2% | 9.9% | 0.8% | 65.2% | 159.0%
Newspapercc | 13.1% | 15.7% | 5.0% | 66.0% | 168.3%
GhostTownFly | 29.1% | 29.7% | 10.3% | 69.8% | 157.7%
PoznanHall2 | 23.6% | 24.1% | 7.3% | 67.1% | 163.8%
PoznanStreet | 20.5% | 21.4% | 5.8% | 67.1% | 170.4%
UndoDancer | 46.8% | 47.5% | 20.1% | 69.9% | 156.9%
1024x768 | 10.8% | 12.8% | 2.7% | 66.2% | 160.9%
1920x1088 | 30.0% | 30.7% | 10.9% | 68.5% | 162.1%
average | 21.8% | 23.0% | 7.4% | 67.5% | 161.6%
Table1. Full resolution vs 1/2 resolution in CTC of HTM6.1

## Slide 9: Experimental Results
 | video / video | video / total | synth / total | enc time | dec time
Balloons | 12.8% | 15.4% | 0.1% | 52.2% | 114.6%
Kendo | 10.0% | 12.4% | -2.6% | 50.7% | 117.2%
Newspapercc | 18.0% | 21.8% | 5.5% | 51.6% | 123.7%
GhostTownFly | 77.4% | 78.0% | 31.9% | 54.7% | 117.7%
PoznanHall2 | 22.0% | 23.2% | 2.2% | 51.7% | 120.8%
PoznanStreet | 34.1% | 35.6% | 10.1% | 52.1% | 126.4%
UndoDancer | 101.0% | 100.3% | 40.0% | 54.1% | 116.4%
1024x768 | 13.6% | 16.6% | 1.0% | 51.5% | 118.5%
1920x1088 | 58.6% | 59.3% | 21.0% | 53.1% | 120.3%
average | 39.3% | 41.0% | 12.5% | 52.4% | 119.5%
Table2. Full resolution vs 1/4 resolution in CTC of HTM6.1

## Slide 10: Experimental Results
 | video / video | video / total | synth / total | enc time | dec time
Balloons | 3.0% | 3.9% | -1.4% | 77.6% | 73.6%
Kendo | 2.3% | 3.2% | -2.9% | 77.8% | 73.7%
Newspapercc | 6.3% | 7.7% | 1.9% | 78.1% | 73.5%
GhostTownFly | 46.8% | 47.0% | 24.0% | 78.3% | 74.6%
PoznanHall2 | 0.6% | 1.3% | -3.9% | 76.9% | 73.8%
PoznanStreet | 15.7% | 16.3% | 5.9% | 77.6% | 74.1%
UndoDancer | 46.1% | 44.8% | 21.7% | 77.4% | 74.2%
1024x768 | 3.9% | 4.9% | -0.8% | 77.8% | 73.6%
1920x1088 | 27.3% | 27.3% | 11.9% | 77.6% | 74.2%
average | 17.2% | 17.7% | 6.5% | 77.7% | 73.9%
Table3. 1/2 vs 1/4 in CTC of HTM6.1

## Slide 11: Experimental Results
RD curve of synthesized view in the best case, Kendo
Chart: 
| 1822.7991999999999 | 878.77440000000013 | 480.84639999999996 | 283.27760000000001
Full resolution | 43.1115 | 40.8532 | 38.4485 | 35.9088
half resolution | 42.4111 | 40.338 | 38.0655 | 35.5918
Quarter resolution | 41.9671 | 40.008 | 37.8123 | 35.3939

## Slide 12: Experimental Results
RD curve of synthesized view in the worst case, Undo Dancer
Chart: 
| 6800.7063000000007 | 2856.5135999999998 | 1326.8560000000002 | 637.83600000000001
Full | 38.6507 | 35.8378 | 33.3219 | 31.0052
Half | 36.6232 | 34.7401 | 32.739 | 30.6654
Quarter | 35.3411 | 33.8759 | 32.2183 | 30.4026

## Slide 13: Summary
Asymmetric resolution coding in HTM can be achieved by simple modification
It provides mostly loss on coding performance compared with full resolution coding at high bit rate, but it provides gain at low bit rate in some case
It shows an increase on coding performance with resolution reduction on some sequences
Encoding time is effectively reduced
The data volume is vastly reduced to 3 unit of single view and the requirement is satisfied

## Slide 14: Conclusion
Experimental result shows a potential of asymmetric resolution coding
We need a further investigation