## Slide 1: On inter-layer reference picture output marking (JCTVC-N0056 / JCT3V-E0039)
JCT-VC 14th Meeting in Vienna, AT, 25 July - 2 Aug. 2013
Tomoyuki Yamamoto, Takeshi Tsukuba, Tomohiro Ikai
SHARP Corporation

## Slide 2: Introduction
Motivation
  Picture buffer management of inter-layer reference picture is not well defined
  Stored to temporal picture buffer only with reference picture mark
Proposed change
  Treat inter-layer reference picture similarly as other reference pictures in terms of picture buffer management
  Assign output mark to inter-layer reference picture
   The same removal process as other picture buffers can be applied

## Slide 3: DPB & RPS illustration
curr
curr
curr
Single layer
2 layers (SNR/multiview)
2 layers (spatial)
RPS
RPS
RPS
DPB
DPB
DPB
DPB

## Slide 4: Proposed text change
<JCTVC-M1008_v3>
G.8.1.2 Decoding process for inter-layer reference picture set
Output of this process is an updated list of inter-layer reference pictures RefPicSetInterLayer.
The variable currLayerId is set equal to nuh_layer_id of the current decoded picture
The list RefPicSetInterLayer is first emptied and then derived as follows.
  for( i = 0; i < NumActiveRefLayerPics; i++ ) { if( there is a picture picX in the DPB that is in the same access unit as the current picture and has nuh_layer_id equal to RefPicLayerId[ i ] ) { an interlayer reference picture rsPic is derived by invoking the subclause G.8.1.4 with picX and DirectRefLayerIdx[ currLayerId ][ RefPicLayerId[ i ] ] given as inputs RefPicSetInterLayer[ i ] = rsPic The value of PicOutputFlag for rsPic is set equal to 0 RefPicSetInterLayer[ i ] is marked as "used for long-term reference" } else RefPicSetInterLayer[ i ] = "no reference picture" }
There shall be no entry equal to "no reference picture" in RefPicSetInterLayer.
If the current picture is a RADL picture, there shall be no entry in the RefPicSetInterLayer that is a RASL picture.
NOTE – An access unit may contain both RASL and RADL pictures.
Red part is a proposed change (an additional output mark assignment).

## Slide 5: Conclusion
Proposed change
  Assign output mark to inter-layer reference picture
Benefit
  Coherent picture buffer management for every pictures in RPS
    Currently some have output mark and some does not
  The same removal process can be applied for every picture buffer
    It is useful to manage/constrain the number of picture buffers used for EL picture decoding
It is recommended to:
  Adopt proposed change to SHVC/MV-HEVC
  Continue study on inter-layer reference picture in terms of picture buffer management