## Slide 1: JCT3V-E0064: On low-delay checking process for MV-HEVC
X. Xiu, Y. Ye, Y. He, Y. He (InterDigital)
Y. Lin, X. Zheng, X. Chen, J. Zheng (HiSilicon)

## Slide 2: Summary
Low-delay checking process is used to derive collocated MV in TMVP derivation. In HTM reference software, a low-delay flag is determined at slice-level and used in the TMVP derivation
In MV-HEVC, collocated picture used in the TMVP derivation may be either a temporal reference picture or an inter-view reference picture
Propose to determine the low-delay flag additionally depending on whether collocated picture is an inter-view reference picture.
Overall BD-rate saving: 0.7% for 3-view coding, and 2.1% for dependent view coding

## Slide 3: Collocated MV derivation in MV-HEVC
colMV (i.e. collocated MV) is required for TMVP derivation
  colPU has two MVs In case the colPU is bi-predictive
  How to choose one of the two MVs as colMV
In MV-HEVC, colMV is derived depending on low-delay flag
  The low-delay flag indicates if POC of current picture is not greater than that of all reference pictures
  If low-delay flag is true, colMV is derived based on the target TMVP of current PU
  Otherwise, colMV is derived based on Collocated_picture_from_list0_flag

## Slide 4: Proposed modification on low-delay checking process
The low-delay flag is set to true, if
  POC of current picture is not greater than that of all reference pictures
  or collocated picture is an inter-view reference picture (proposed)
Figure 1. colMV derivation when inter-view reference picture is used as co-located picture.
In this case, mvCol in L0 of colPU is used to derive target TMVP(i.e. mvLX, LX=L0) of current PU

## Slide 5: Experimental results
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate |  | enc time | dec time
Balloons | 0.0% | -5.4% | -3.7% | -2.4% | -2.4% |  | 100.9% | 99.2%
Kendo | 0.0% | -3.5% | -2.4% | -1.5% | -1.5% |  | 100.5% | 102.9%
Newspaper_CC | 0.0% | -0.4% | 1.7% | 0.3% | 0.3% |  | 101.5% | 105.5%
GT_Fly | 0.0% | -0.8% | -0.3% | -0.8% | -0.8% |  | 97.0% | 110.1%
Poznan_Hall2 | 0.0% | -3.2% | 0.3% | -0.6% | -0.6% |  | 101.5% | 104.0%
Poznan_Street | 0.0% | -0.1% | 0.8% | 0.0% | 0.0% |  | 100.8% | 104.8%
Undo_Dancer | 0.0% | -1.1% | 0.1% | -0.2% | -0.2% |  | 101.3% | 103.5%
1024x768 | 0.0% | -3.1% | -1.5% | -1.2% | -1.2% |  | 101.0% | 102.5%
1920x1088 | 0.0% | -1.3% | 0.2% | -0.4% | -0.4% |  | 100.1% | 105.6%
average | 0.0% | -2.1% | -0.5% | -0.7% | -0.7% |  | 100.5% | 104.3%
Anchor: htm-dev-1.0 under MV-HEVC configuration
Average 0.7% BD-rate saving for 3-view coding
Thanks to Sharp for the cross-check report (JCT3V-E0251)

## Slide 6: Conclusion
Modification to low-delay checking process is proposed
  A slice-level change since the modification has same influence on all PUs of a slice
  Significant performance improvement for dependent view coding
Recommendation: adopt the proposed modification in MV-HEVC

## Slide 7
Thank you!

## Slide 8: Additional experimental results
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate |  | enc time | dec time
Balloons | 0.0% | -2.3% | -1.2% | -1.0% | -1.0% |  | 101.5% | 99.3%
Kendo | 0.0% | -1.1% | -0.4% | -0.4% | -0.4% |  | 100.6% | 102.5%
Newspaper_CC | 0.0% | 0.5% | 2.1% | 0.6% | 0.6% |  | 101.3% | 92.3%
GT_Fly | 0.0% | -0.2% | 0.1% | -0.6% | -0.6% |  | 97.4% | 108.8%
Poznan_Hall2 | 0.0% | -2.4% | 1.0% | -0.1% | -0.1% |  | 100.9% | 104.6%
Poznan_Street | 0.0% | 0.4% | 1.1% | 0.2% | 0.2% |  | 100.1% | 104.4%
Undo_Dancer | 0.0% | -1.0% | 0.0% | -0.2% | -0.2% |  | 101.1% | 103.7%
1024x768 | 0.0% | -0.9% | 0.2% | -0.3% | -0.3% |  | 101.1% | 98.0%
1920x1088 | 0.0% | -0.8% | 0.6% | -0.2% | -0.2% |  | 99.9% | 105.4%
average | 0.0% | -0.9% | 0.4% | -0.2% | -0.2% |  | 100.4% | 102.2%
Anchor: htm-dev-1.0 under MV-HEVC configuration
Performance of enabling inter-view reference picture as collocated picture at encoder side