## Slide 1: MV-HEVC / SHVC HLS: On use of splitting_flag with flexible coding order
JCT3V-E0104, JCTVC-N0299
Andrey Norkin, Thomas Rusert

## Slide 2: Outline
Problem statement
Possible fixes and their problems
Proposal
  Solution 1
  Solution 2
Conclusions

## Slide 3: Problem statement (1/2)
splitting_flag is used to indicate that scalabilityId is signaled in the slice header instead of the dimension_id syntax element. This gives network elements a possibility to extract scalability identifiers directly from NAL unit header
It is required that
for every i greater than 0, layer_id_in_nuh[ i ] > layer_id_in_nuh[ i – 1 ]

## Slide 4: Problem statement (2/2)
Consider 3D-HEVC common test conditions (e.g. IBP configuration). The coding order is T0, D0, T1, D1, T2, D2.

## Slide 5: Possible fixes
scalability_mask index | Scalability dimension | ScalabilityId mapping
0 | multiviewdepth | ViewId VpsDepthFlag
1 | depth multiview | VpsDepthFlag ViewId
2-15 | Reserved | 
Possible fix 1: Swap scalability_mask_index values for depth and ViewId.
Problems: Coding order such as T0 D0 D1 T1, it is still not possible. When other types of scalability are added, use of splitting_flag may again become incompatible with certain coding order of scalability dimensions.
Possible fix 2: Remove the requirement that layer_id_in_nuh[ i ] shall be greater than layer_id_in_nuh[ i – 1 ].
Problems: nuh_layer_id does not indicate the coding order any more

## Slide 6: Proposal
Use MSB in nuh_layer_id in order to force increasing values of nuh_layer_id, when the splitting_flag is used

## Slide 7: Solution 1 (syntax)
Allow MSB in nuh_layer_id being not assigned to any dimension_id when splitting_flag is equal to 1.
Allow MSB bits in nuh_layer_id take arbitrary values
vps_extension( ) { | Descriptor
… | 
splitting_flag | u(1)
for( i = 0, NumScalabilityTypes = 0; i < 16; i++ ) { | 
scalability_mask[ i ] | u(1)
NumScalabilityTypes += scalability_mask[ i ] | 
} | 
for( j = 0; j < ( NumScalabilityTypes − splitting_flag ); j++ ) | 
for( j = 0; j < NumScalabilityTypes ; j++ ) | 
dimension_id_len_minus1[ j ] | u(3)
vps_nuh_layer_id_present_flag | u(1)
} | 
…. | 

## Slide 8: Solution 1 (Semantics)

## Slide 9: Solution 1 (Semantics)

## Slide 10: SOlution 2 (syntax)
Assign the scalability_mask_index equal to 15 to reorder_id dimension
Encoders can choose to use this scalability type by indicating its use in the scalability_mask in the VPS.
vps_extension( ) { | Descriptor
… | 
splitting_flag | u(1)
for( i = 0, NumScalabilityTypes = 0; i < 16 15 + splitting_flag; i++ ) { | 
scalability_mask[ i ] | u(1)
NumScalabilityTypes += scalability_mask[ i ] | 
} | 
… | 

## Slide 11: Solution 2 (semantics)

## Slide 12: Conclusions
In HEVC scalability extensions, splitting_flag does not allow flexibly choosing the coding order between different scalability dimensions
In particular, use of splitting_flag is not compatible with the current 3D-HEVC common test conditions
Two simple solutions to fix this problem are proposed, from which the proposed solution 2 is recommended as being cleaner (specifying explicitly that MSBs in nuh_layer_id will be used for nuh_layer_id reordering).
It is proposed to adopt one of the proposed solutions 1 and 2 to the MV-HEVC, 3D-HEVC, and SHVC working drafts and the reference software