## Slide 1
VSP and Temporal Candidates in Merge
Jin Young Lee
Multimedia Platform Lab.
DMC R&D Center
Samsung Electronics

## Slide 2: Current Merge List
VSP candidate is always added in Merge list, if VSP is enabled
Merge list construction in 3D-HEVC is very similar to that in 2D-HEVC
In 2D-HEVC, temporal candidate is always added, but not guaranteed in 3D-HEVC
Temporal candidate is very useful in some sequences
- Inter-View Candidates
- Spatial Candidates
- Disparity Candidates
- VSP Candidates
Select (5) Candidates
Select (1) Candidates
Select (6) Candidates
- Temporal Candidates
Select (1) Candidates

## Slide 3: Proposed #1
VSP candidate is treated as spatial candidates
Temporal candidate is always added, but VSP candidated is not guaranteed
- Inter-View Candidates
- Spatial Candidates
- Disparity Candidates
- VSP Candidates
- Temporal Candidates
Select (5) Candidates
Select (1) Candidates
Select (6) Candidates

## Slide 4: Proposed #2
The number of spatial candidates is decreased by one
Temporal and VSP candidates is always added in Merge list
- Inter-View Candidates
- Spatial Candidates
- Disparity Candidates
- VSP Candidates
Select (4) Candidates
Select (1) Candidates
Select (6) Candidates
- Temporal Candidates
Select (1) Candidates

## Slide 5: Proposed #3
The number of total candidates is increased by one
Temporal and VSP candidates is always added in Merge list
- Inter-View Candidates
- Spatial Candidates
- Disparity Candidates
- VSP Candidates
- Temporal Candidates
Select (6) Candidates
Select (1) Candidates
Select (6) Candidates

## Slide 6: Conclusion
Proposed to guarantee temporal candidate in Merge list
Proposed #1 : VSP is treated same as inter-view, spatial, and disparity candidates
Proposed #2 : The # of inter-view, spatial, and disparity candidates is decreased by 1
Proposed #3 : The # of total candidates is increased by 1
Proposal | Video1 | Video2 | Cod. vs Video | Cod. vs Total | Syn. Vs Total
#1 | 0.1% | 0.1% | 0.0% | 0.0% | 0.0%
#2 | 0.0% | 0.0% | 0.0% | 0.0% | -0.1%
#3 | -0.1% | -0.2% | -0.1% | -0.1% | 0.0%