## Slide 1
DMM Simplification and Signalling
Jin Young Lee
Multimedia Platform Lab.
DMC R&D Center
Samsung Electronics

## Slide 2: CE5 Results
Since DMMs and chain mode have been developed with similar concept, they are significantly redundant.
DMM1 is very dominant in terms of the coding performance.
Removing the several DMMs reduces the encoding times at the same time significantly simplifies the current design and specification
Test | DMM1 | DMM2 | DMM3 | DMM4 | RBC | Comment
2-A | on | on | D0067 | on | on | 
2-B1 | D0184 | on | D0067 | on | on | 
2-B2 | D0184 | off | D0067 | on | on | 
2-C1 | on | on | off | off | on | adapted signaling
2-C2 | on | off | off | off | on | adapted signaling
2-D | on | off | off | off | off | adapted signaling
CTC | Cod. | Syn. | Enc.
2-C1 | 0.0% | 0.0% | 96%
2-C2 | 0.0% | 0.1% | 95%
2-D | 0.0% | 0.2% | 95%
AL | Cod. | Syn. | Enc.
2-C1 | 0.0% | 0.2% | 81%
2-C2 | 0.0% | 0.2% | 76%
2-D | 0.1% | 0.4% | 75%
WD
3 pages
8 pages
10 pages
Syntax
1
4
14

## Slide 3: Test2C-1
Name of depth_intra_mode | Bin String |  | 
 | ( cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_2Nx2N ) ¦ ¦ ( cLog2CbSize > 3 && cLog2CbSize < 6 ) | cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_NxN | cLog2CbSize = = 6
INTRA_DEP_SDC_PLANAR | 00 | - | 0
INTRA_DEP_NONE | 010 | 0 | 10
INTRA_DEP_SDC_DMM_WFULL | 011 | - | -
INTRA_DEP_DMM_WFULL | 100 | 10 | -
INTRA_DEP_SDC_DC | 101 | - | 11
INTRA_DEP_DMM_WPREDDIR) | 110 | - | -
INTRA_DEP_CHAIN | 111 | 11 | -

## Slide 4: Test2C-2
Name of depth_intra_mode | Bin String |  | 
 | ( cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_2Nx2N ) ¦ ¦ ( cLog2CbSize > 3 && cLog2CbSize < 6 ) | cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_NxN | cLog2CbSize = = 6
INTRA_DEP_SDC_PLANAR | 00 | - | 0
INTRA_DEP_NONE | 010 | 0 | 10
INTRA_DEP_SDC_DMM_WFULL | 011 | - | -
INTRA_DEP_DMM_WFULL | 100 | 10 | -
INTRA_DEP_SDC_DC | 101 | - | 11
INTRA_DEP_CHAIN | 110 | 11 | -

## Slide 5: Test2D
Name of depth_intra_mode | Bin String |  | 
 | ( cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_2Nx2N ) ¦ ¦ ( cLog2CbSize > 3 && cLog2CbSize < 6 ) | cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_NxN | cLog2CbSize = = 6
INTRA_DEP_SDC_PLANAR | 00 | - | 0
INTRA_DEP_NONE | 010 | 0 | 10
INTRA_DEP_SDC_DMM_WFULL | 011 | - | -
INTRA_DEP_DMM_WFULL | 100 | 10 | -
INTRA_DEP_SDC_DC | 101 | - | 11