## Slide 1: JCT3V-E0161 3D-CE2.h related: Depth to disparity vector conversion for non-horizontal camera arrangements
Yu-Lin Chang, Yi-Wen Chen, Jian-Liang Lin, Yu-Pao Tsai, Shawmin Lei
Presented by Yu-Lin Chang
JCT on 3D Video Coding Extension Development
Jul., 2013

## Slide 2: Overall Summary
In current HTM-7.0r1, only horizontal information of the camera arrangement is coded
  Only the horizontal component of a disparity vector (DV) can be converted from depth.
  The vertical component of the DV is always set equal to 0.
A depth to vertical DV conversion scheme along with high-level syntax on vertical camera parameters is proposed
  Enable the vertical component of the DV to be used under non-horizontal camera arrangements.
No coding loss observed in common test condition
Notes:     Problem and proposeVSP off, finding inter-view reference without warping

## Slide 3: Depth to Disparity Conversion in HTM
If only a linearly arranged camera setup is considered, the camera parameters include a scale factor and an offset, as shown in following equation:
dv = ( s * v + o ) >> n,
where dv is the converted DV, v is the depth sample value, s is the transmitted scale factor, o is the transmitted offset, and n is a shift parameter that depends on the required accuracy of the DV
A scale factor and offset is transmitted in the SPS/slicer header for each reference view of the current layer
The scale factor and offset is only used for horizontal component

## Slide 4: Proposed Depth to Vertical DV Conversion
Propose to use the same equation for deriving both the horizontal and the vertical components of the DV.
  dv = ( s * v + o ) >> n,
Add vertical scale factor and vertical offset to SPS/slice header for each reference view
Derive forward/backward depth to vertical disparity table for each reference view
Apply the converted vertical disparity values to the vertical component of the DV in VSP and DoNBDV

## Slide 5: Experiment Results (1/2)
Anchor: HTM-7.0r1 under CTC
Test: Proposed depth to vertical DV conversion for DoNBDV
Crosschecked by JCT3V-E0272, Thanks to MERL

## Slide 6: Experiment Results (2/2)
Anchor: HTM-7.0r1 under CTC
Test: Proposed depth to vertical DV conversion for DoNBDV and VSP
Crosschecked by JCT3V-E0272, Thanks to MERL

## Slide 7: Changes to Working Draft (1/6)
H.7.3.2.2.2 Sequence parameter set extension 2 syntax
sps_extension2( ) { | Descriptor
if( !VpsDepthFlag[ nuh_layer_id ] ) { | 
cp_precision | ue(v)
cp_in_slice_header_flag | u(1)
if( !cp_in_slice_header_flag ) { | 
for ( i = 0; i < ViewId[ nuh_layer_id ]; i++ ) { | 
cp_scale[ i ] | se(v)
cp_off[ i ] | se(v)
cp_inv_scale_plus_scale[ i ] | se(v)
cp_inv_off_plus_off[ i ] | se(v)
cp_vert_scale[ i ] | se(v)
cp_vert_off[ i ] | se(v)
cp_inv_vert_scale_plus_vert_scale[ i ] | se(v)
cp_inv_vert_off_plus_vert_off[ i ] | se(v)
} | 
} | 
} | 
} | 

## Slide 8: Changes to Working Draft (2/6)
H.7.3.5.1.1 Slice header extension syntax
slice_header_extension( ) { | Descriptor
if( cp_in_slice_header_flag ) { | 
for ( i = 0; i < ViewIdx; i++ ) { | 
cp_scale[ i ] | se(v)
cp_off[ i ] | se(v)
cp_inv_scale_plus_scale[ i ] | se(v)
cp_inv_off_plus_off[ i ] | se(v)
cp_vert_scale[ i ] | se(v)
cp_vert_off[ i ] | se(v)
cp_inv_vert_scale_plus_vert_scale[ i ] | se(v)
cp_inv_vert_off_plus_vert_off[ i ] | se(v)
} | 
} | 
} | 

## Slide 9: Changes to Working Draft (3/6)
H.7.4.5.1.1 Slice header extension semantics

## Slide 10: Changes to Working Draft (4/6)
H.8.5.4.3 Derivation process for a disparity sample array

## Slide 11: Changes to Working Draft (5/6)
H.8.5.2.2.7 View synthesis prediction process
…..

## Slide 12: Changes to Working Draft (6/6)
H.8.5.4 Derivation process for disparity vectors

## Slide 13: Conclusions
A depth to vertical DV conversion along with HLS on vertical camera parameter is proposed
The proposed scheme enables the vertical component of the DV to be used under non-horizontal camera arrangements.

## Slide 14: Thanks for your attention!
www.mediatek.com