## Slide 1: 3D-CE6.h related: Removal of post-filter for DC mode in SDC
Jian-Liang Lin, Yi-Wen Chen, Yu-Wen Huang, Shawmin Lei
JCT3V-E0165
Presented by Jian-Liang Lin
5th JCT-3V Meeting in Vienna
27th Jul – 2nd Aug. 2013

## Slide 2: Overall Summary
For the DC mode in SDC, the DC value needs to be calculated in two steps.
  It firstly calculates the mean of neighbouring samples as the initial prediction samples
  After a boundary post-filter is applied on the initial prediction samples, it has to re-calculate the mean of the prediction samples
It is proposed to remove the second step and the boundary post-filer for DC mode in SDC
The experimental results show no coding efficiency loss (0.04% coding gain) under CTC and all-Intra test conditions

## Slide 3: DC mode in SDC
The DC value needs to be calculated in two steps.
It first calculates the mean of the neighbouring samples as the initial prediction samples.
In the second step, the boundary post-filter is applied to smooth the boundary prediction samples.
After that, it needs to re-calculate the mean of the prediction samples after boundary post-filtering.
Uses it as the input of the depth lookup table to generate the index value.

## Slide 4: Proposed Simplification
The DC value only needs to be calculated in one step.
It first calculates the mean of the neighbouring samples as the prediction samples.
In the second step, the boundary post-filter is applied to smooth the boundary prediction samples
After that, it needs to re-calculate the mean of the prediction samples after boundary post-filtering.
Uses it as the input of the depth lookup table to generate the index value.

## Slide 5: Experiment Results - CTC
Anchor : HTM-7.0r1 under CTC
Tested : Proposed simplification
No coding loss (0.04% coding gain)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | -0.03% | -0.01% | -0.01% | -0.03% | 0.02% | 100.6% | 100.4% | 99.1%
Kendo | 0.00% | -0.03% | -0.08% | -0.01% | 0.03% | -0.08% | 100.3% | 100.1% | 99.8%
Newspaper_CC | 0.00% | 0.06% | -0.15% | 0.00% | 0.00% | -0.29% | 100.0% | 99.6% | 98.6%
GT_Fly | 0.00% | 0.24% | 0.03% | 0.02% | 0.02% | -0.01% | 100.8% | 100.4% | 101.5%
Poznan_Hall2 | 0.00% | 0.06% | 0.17% | 0.05% | 0.04% | 0.01% | 100.1% | 90.7% | 100.8%
Poznan_Street | 0.00% | 0.12% | 0.08% | 0.02% | 0.01% | 0.01% | 100.5% | 93.7% | 96.7%
Undo_Dancer | 0.00% | -0.19% | 0.05% | -0.02% | -0.03% | 0.07% | 100.2% | 95.5% | 102.7%
1024x768 | 0.00% | 0.00% | -0.08% | -0.01% | 0.00% | -0.12% | 100.3% | 100.1% | 99.2%
1920x1088 | 0.00% | 0.06% | 0.08% | 0.02% | 0.01% | 0.02% | 100.4% | 95.1% | 100.4%
average | 0.00% | 0.03% | 0.01% | 0.01% | 0.01% | -0.04% | 100.3% | 97.2% | 99.9%
Results are crosscheck and confirmed by Sharp (JCT3V-E0255)

## Slide 6: Experiment Results – All Intra
Anchor : HTM-7.0r1 under All Intra test conditions
Tested : Proposed simplification
No coding loss
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 100.5% | 96.9% | 98.9%
Kendo | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | -0.01% | 100.2% | 102.9% | 103.1%
Newspaper_CC | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | -0.02% | 100.6% | 97.0% | 104.0%
GT_Fly | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | -0.02% | 99.7% | 96.4% | 95.0%
Poznan_Hall2 | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | -0.02% | 100.6% | 99.6% | 98.7%
Poznan_Street | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 100.4% | 98.4% | 97.7%
Undo_Dancer | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 99.4% | 100.4% | 99.6%
1024x768 | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | -0.01% | 100.4% | 98.9% | 102.0%
1920x1088 | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | -0.01% | 100.0% | 98.7% | 97.7%
average | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | -0.01% | 100.2% | 98.8% | 99.6%

## Slide 7: Conclusions
It is proposed to remove the post-filter of DC mode in SDC.
The mean of the depth values of neighbouring samples is directly used as the final prediction samples of current depth block.
The experimental results show no coding loss in the common test conditions and all-intra test condition.
  0.04% coding gain under CTC

## Slide 8: Thanks for your attention!
www.mediatek.com