## Slide 1: JCT3V-E0168: 3D-CE4: On complexity reduction of bi-prediction for illumination compensation
Yi-Wen Chen, Tzu-Der Chuang, Jian-Liang Lin, Yu-Wen Huang, Shawmin Lei
Presented by Yi-Wen Chen
5th JCT3V Meeting in Vienna
17 Jan. – 23 Jan., 2013

## Slide 2: Overall Summary
Bi-prediction for identical motion
  HTM-7.0 changes bi-prediction to uni-prediction
  Generated bitstreams may not conform to the 3D-HEVC text when illumination compensation (IC) is enabled due to unequal clipping operations between uni-prediction and bi-prediction
In CE4 Test-2.0, we propose to align the operations between uni-prediction and bi-prediction for IC
  No change to coding performance

## Slide 3: 3D-HEVC WD of predictor calculation for IC
Unequal operations for uni- and bi- predictions
2 clipping
1 clipping
L0
L1
Bi

## Slide 4: Modified WD for IC
Unified operations for uni- and bi- predictions

## Slide 5: Simulation Results Under CTC
Anchor : HTM-7.0r1
Test : HTM-7.0r1 with the proposed modification

## Slide 6: Simulation Results Under IBP
Anchor : HTM-7.0r1
Test : HTM-7.0r1 with the proposed modification

## Slide 7: Conclusion
Current software HTM-7.0 may generate non-conforming bitstream when IC is enabled
  Resulted from identical motion checking for bi-prediction
  Unequal clipping operations between IC uni- and bi- predictions
Propose to align the clipping operations between IC uni- and bi-predictions
  0.0% BD-rate change for coded and synthesized views
  Support identical motion checking

## Slide 8: Thank you for your attention!

## Slide 9: Backup